## Slide 1: Autonomous Cyber-Physical Systems: Sensing
Spring 2018. CS 599.
Instructor: Jyo Deshmukh

## Slide 2: Overview
Sensing
  Main sensors and how they work

## Slide 3: Sensors
Transducers that convert one physical property into another
In our context, a sensor convers a physical quantity into a numeric value
Choosing sensors is a hard design problem, as sensors can have many factors that need tuning
  Accuracy: Error between true value and its measurement (noise values, rejection of external interference)
  Resolution: Minimum difference between two measurements (usually much smaller number than actual accuracy of the sensor)
  Sensitivity: Smallest change in value that can be detected

## Slide 4: Sensor selection
Factors affecting sensor selection (continued)
  Dynamic Range: Minimum and maximum values that can be accurately detected
  Time-scale/Responsiveness: How often the sensor produces output and frequency bandwidth of the measurement output over time
  Interface technology: analog, digital or serial or network streams
  Perspective: Which portion of the environment can the sensor measure (e.g. the field of vision for a camera, orientation for an ultrasonic module)

## Slide 5: Basics of IMUs
Inertial Measurement Units or IMUs are part of an Inertial Navigation System
Use accelerometers and gyroscopes to track position and orientation of an object relative to start position, orientation and velocity
Typically: 3 orthogonal rate-gyroscopes measuring angular velocities, and 3 accelerometers measuring linear accelerations (along the 3 axes)
  Stable-platform IMUs: a platform is used to mount the inertial sensors, and the platform is isolated from external rotational motion
  Strapdown IMUs: Inertial sensors mounted rigidly (more common due to smaller size)

## Slide 6: Inertial navigation algorithm (for strapdown IMUs)

## Slide 7: IMU equations
Image from [1]
Body Frame vs. Global Frame
Relation between body frame and global frame is given by a 3X3 rotation matrix , in which each column is a unit vector along one of the body axes specified in terms of the global axis
Rotation matrix is an orthogonal matrix whose determinant is 1. Rotations of about the and axes respectively achieved by following rotation matrices:

## Slide 8: IMU equations continued
Note that for a rotation matrix, . Let and be velocities in the global and body frame respectively, then:
and
We need to track through time
Let be the rotation matrix relating body frame at time to body frame at time . Then . If the rotations are small enough, can itself be written as , where is the small angle approximation of the rotation matrix

## Slide 9: IMU equations
So,
Also, = ,
where is the rotational velocity along the axis.
So actually evolves according to the linear dynamical system , and the solution for
In implementation, we can approximate the updated at each time step by a numerical integrator
Acceleration in the body frame is tracked in a similar fashion.
Once we have velocity and acceleration, we can compute position, after subtracting the acceleration due to gravity

## Slide 10: Basics of GPS
Commercial GPS systems provide (GPS) coordinates of a vehicle within 2m accuracy, this is not enough for autonomous driving
Differential GPS receivers provide decimeter level accuracy
GPS gives information about current time, latitude, longitude, and altitude
Often GPS data is used as “observations” along with an IMU-based inertial navigation system (INS) to localize the vehicle
Predict
Update
Kalman Filter/EKF

## Slide 11: Basics of LiDAR
LiDAR stands for Light detection and Ranging
Typical LiDARs e.g. Velodyne HDL-64E use multi-beam light rays
Mathematical model by “ray-casting”: rays are cast at an angle, and you get the distance from the first obstacle that reflects the light
Lidar data consists of rotational angle and distance to obstacle
This can be represented in a point cloud form by mapping each obstacle point to coordinates (with respect to the body frame)

## Slide 12: Basics of Radar
Frequency Modulated Continuous Wave Doppler radar is popular
Main idea is to compute the distance to the obstacle in a given direction by comparing transmitted and received signals
Allows estimating both distance and relative velocity
Radars may require additional signal processing to give precise answers when the environment is dusty, rainy, or foggy.
Forward-facing radars estimate relative position/velocity of lead vehicle
Surround ultrasonic sensors can help create environment models (Tesla approach)

## Slide 13: Sensor Fusion
We already learned about Kalman filter that can help do sensor fusion for localization using INS and GPU
Sensor fusion for camera and LiDAR data requires new algorithms
Centralized algorithms based on conditional random fields, Markov random fields, and decentralized algorithms based on boosting and Gaussian mixture models have been explored
Deep learning is also being explored for doing sensor fusion
Note: these approaches are exploratory, and there is no standard algorithm accepted by all

## Slide 14: Markov Random Field based sensor fusion
Random field: set of random variables described by an undirected graph, provides probabilistic framework to model image labeling problem
Markov random field: probability of each node in the graph is positive, and the conditional probability of node with respect to all nodes of the graph is equal to the conditional property of with respect to only its neighbors
In image labeling, each pixel corresponds to a random variable
Goal is to assign to each random variable a label from a finite set of labels, using Maximum a Posteriori labeling using appropriate cost functions

## Slide 15: Bibliography
O. J. Woodman, An introduction to inertial navigation - Cambridge Computer Laboratory, https://www.cl.cam.ac.uk/techreports/UCAM-CL-TR-696.pdf
Pendleton, Scott Drew, Hans Andersen, Xinxin Du, Xiaotong Shen, Malika Meghjani, You Hong Eng, Daniela Rus, and Marcelo H. Ang. "Perception, planning, control, and coordination for autonomous vehicles." Machines 5, no. 1 (2017): 6.
S. Liu, L. Li, J. Tang, S. Wu, Jean-Luc Gaudiot, Creating Autonomous Vehicle Systems, Morgan & Claypool 2018.