## Slide 1: Autonomous Cyber-Physical Systems: Stability Analysis for Nonlinear Dynamical Systems Hybrid Dynamical Systems
Fall 2025. CS 513.
Instructor: Jyo Deshmukh
Acknowledgment: Some of the material in these slides is based on the lecture slides for CIS 540: Principles of Embedded Computation taught by Rajeev Alur at the University of Pennsylvania. http://www.seas.upenn.edu/~cis540/
This lecture also uses some other sources, full bibliography is included at the end of the slides.

## Slide 2: Stability Analysis for Linear Systems
Given system where and is an matrix,
Interesting result for linear systems: System is asymptotically stable if and only if every eigenvalue of has a negative real part
Lyapunov stable if and only if every eigenvalue has non-positive real part
How to calculate eigenvalues?
  eigs(A) in Matlab
  import numpy as np
from numpy.linalg import eig
A = np.array([…])
w,v = eig(A)
Manual way: solve the characteristic equation of the matrix

## Slide 3: Stability analysis example for linear systems
Characteristic equation: i.e.
, or
i.e.,
Real part is positive represents an unstable linear system

## Slide 4: Stability analysis example for linear systems
Characteristic equation: i.e.
, or
i.e.,
Real part is negative represents a stable linear system

## Slide 5: Nonlinear Dynamical System
Simple Pendulum
  Arc length
  Linear velocity:
  Linear acceleration:
Friction

## Slide 6: Simple Pendulum Dynamics
Let , , and let , and
Rewriting previous equation:
  =
For small angles, the above equation is almost linear (replace by ), and we can use techniques for linear systems to show stability
But, for any larger angle (less than ), we know the pendulum eventually stops
How do we show pendulum system is stable?
Use my method!!
Aleksandr Lyapunov
Russian mathematician

## Slide 7: Lyapunov’s first method
Given
Step 1: find the Jacobian matrix for
Step 2: Set in to get a matrix in (say ) ( is the equilibrium point)
If linear system , is stable, original nonlinear system is stable locally at the equilibrium point. (Local = exists some neighborhood of equilibrium point)

## Slide 8: Lyapunov’s first method for pendulum
Dynamics:
  = ;
  Step 1:
  Step 2:
  Step 3:
    Eigenvalues of satisfy
    both eigenvalues have negative real parts
    Pendulum is locally stable

## Slide 9: Lyapunov’s second method
Method to prove global stability
Relies on notion of Lyapunov Functions
Intuition:
  Find Lyapunov function that could be interpreted as the energy of the system
  Stable systems eventually lose their energy and return to the quiescent state
  Prove that the energy of the system (as encoded by the Lyapunov function) decreases over time

## Slide 10: Lyapunov’s Second Method: the math
Assume w.l.o.g., that equilibrium point * is at the origin, i.e., 0
  Why is this okay?
is a Lyapunov function over the domain iff:
  : [Positivity condition]
  [Derivative negativity condition]
  if : ,
System is stable in the sense of Lyapunov if such a exists

## Slide 11: Illustration and Lie-derivative
decreases as system evolves, i.e. for every pair of points along a system trajectory,
In other words, is a decreasing function in time, or its derivative is negative semi-definite
is called Lie derivative of
By chain-rule,

## Slide 12: Lyapunov’s second method for pendulum
Choose Lyapunov function
Consider ; recall,
By observation, , except at , where it is 0
Let’s look at the Lie derivative

## Slide 13: Second method for asymptotic/exponential stability
is a Lyapunov function over the domain iff:
  : [Positivity condition]
  [Derivative negativity condition]
  if : ,
System is stable in the sense of Lyapunov if such a exists
Asymptotic stability: Change second condition to:
  [Derivative negativity condition]
Exponential stability: Change second condition to:
  or

## Slide 14: Challenges with Lyapunov’s second method
How do we find a Lyapunov function?
  Maybe use the physics of the system to understand what encodes “energy”
  For certain nonlinear systems (those with polynomial dynamics), can some algorithmic methods
  In general a hard problem
Yet, is a powerful approach to prove global stability

## Slide 15: Bounded signals
A signal is bounded if there is a constant , s.t.
Bounded signals:
  Constant signal :
  Exponential signal: , for
  Sinusoidal signals:
Not bounded:
  for any
  Exponential signal: , for
This Photo by Unknown Author is licensed under CC BY-SA

## Slide 16: BIBO stability
A system with Lipschitz-continuous dynamics is BIBO-stable if:
  For every bounded input , the output from initial state is bounded
Simple helicopter model:
  Two rotors: Main rotor gives lift, tail rotor prevents helicopter from spinning
  Torque produced by tail rotor must perfectly counterbalance friction with main rotor, or the helicopter spins
Image credit: From Lee & Seshia: Introduction to Embedded Systems - A Cyber-Physical Systems Approach, http://leeseshia.org/

## Slide 17: Helicopter Model continued
: net torque on tail of the helicopter – difference between frictional torque exerted by main rotor shaft and counteracting torque by the tail rotor
: rotational velocity of the body
Torque = Moment of inertia Rotational acceleration
What happens when is a constant input?
is not bounded helicopter model is not BIBO-stable!

## Slide 18
Hybrid Dynamical Systems

## Slide 19: Hybrid Process
Generalization of a timed process
Instead of timed transitions, we can have arbitrary evolution of state/output variables, typically specified using differential equations
?
?
off
on

## Slide 20: Bang-bang control (thermostat) hybrid automaton
?
?
off
on

## Slide 21: Executions of Thermostat
Initial state : (off, ),
If thermostat enters mode off with , then
Mode switch enabled when , and must happen before , i.e. at
In mode on, it heats the room according to:
Mode switch enabled when , and must happen before , i.e. at
?
?
off
on

## Slide 22: Behavior of thermostat
temperature
mode
time
time

## Slide 23: Hybrid Automata: State machines for hybrid processes
USC Viterbi
School of Engineering
Department of Computer Science
Mode: Vertical travel subject to gravity
Standard coordinate system
Down is negative, Up is positive
is negative because the velocity is becoming more negative (magnitude is increasing)
Sign of as the ball approaches ground is negative

## Slide 24: Hybrid Automata: State machines for hybrid processes
USC Viterbi
School of Engineering
Department of Computer Science
= 0
When does vertical travel end?
Discrete transition!
  Ball goes from vertical travel to impact and back to vertical travel
goes from downward to upward!
I.e.
restitution coefficient measures fraction of speed retained after bounce

## Slide 25: Hybrid Automata: State machines for hybrid processes
USC Viterbi
School of Engineering
Department of Computer Science
Mode: Vertical travel subject to
Vertical travel mode resumed
Initially some positive upward velocity
makes this velocity decrease
Eventually, will be zero, and then negative
But it is still the same “mode” : vertical travel subject to gravity

## Slide 26: Hybrid automaton for bouncing ball
What happens as ?
This is not a cartoon of a ball bouncing and traveling horizontally, just vs.

## Slide 27: Hybrid Process
Continuous action/transition:
Discrete mode does not change
=
satisfies the given dynamical equation for mode
At all times , the state satisfies the invariant for mode

## Slide 28: Hybrid Process
Discrete action/transition:
  Happens instantaneously
  Changes discrete mode to
  Can execute only if evaluates to true
  Changes state variable value from to
  should satisfy mode invariant of
/

## Slide 29: Executions of a hybrid process
At each cell boundary, assume that the guard is the equation of the boundary, and the reset is where
Invariant for each cell/mode is the open set enclosed by its boundaries
Suppose initial state is
(0,0)
(0,1)
(0,2)
(0,3)
(1,0)
(2,0)
(3,0)

## Slide 30: Zeno’s Paradox
Greek philosopher Zeno’s race between Achilles and a tortoise
  Tortoise has a head start over Achilles, but is much slower
  If Achilles is d meters behind at the beginning of a round
  and during the round, suppose Achilles runs d meters
  but by then, tortoise has moved a little bit further
  At the beginning of the next round, Achilles is still behind, by meters [0<<1]
By induction, if we repeat this for infinitely many rounds, Achilles will never catch up!
What is the mistake made by Zeno?
If sum of durations between successive discrete actions converges to constant, then an execution with infinitely many discrete actions describes behavior only up to time (and does not tell us the state of the system at time and beyond
Zeno assumes that if there are infinitely many points Achilles must “check off,” then it must take infinite time. But in fact, the times shrink and form a convergent series.

## Slide 31: Hybrid automaton for bouncing ball
As the ball approaches the ground, the number of discrete transitions occurring in any time interval tends to infinity: in the limit, there will be only discrete transitions and time will stop!

## Slide 32: How to deal with Zeno behavior
An infinite execution is called Zeno if infinite sum of all the durations is bounded by a constant, and non-Zeno if the sum diverges
Any state in a hybrid process is called Zeno if:
  If every execution starting in state is Zeno
  Non-Zeno if there exists some non-Zeno starting in that state
Hybrid process is non-Zeno if any state that you can reach from the initial state is non-Zeno
Thermostat: non-Zeno, Bouncing ball: Zeno
Dealing with Zeno: remove Zeno-ness through better modeling

## Slide 33: Non-Zeno hybrid process for bouncing ball
halt
bounce

## Slide 34: Reachability analysis
Suppose the grid world represents the configuration space of a robot
How do we analyze: Does the robot reach the error cell?
  Easy if we have only one initial state: just simulate!
What if the initial position of the robot is not certain (could be a set)?
What if the dynamics are not certain?
(0,0)
(0,1)
(0,2)
(0,3)
(1,0)
(2,0)
(3,0)
Initial states

## Slide 35: Time-bounded Reachability Analysis
Fundamental problem for dynamical systems
Simulation:
  Given an initial condition , compute solution such that
Time-bounded Reachability:
  Given a set of initial conditions , and a time T, compute the set such that
  A useless (but correct) answer is
  How do we find a “tight” reachable set?

## Slide 36: Computing Reachable Sets3
Main idea: compute successor states
  For a given set of states,
  For a given set ,
  For a given set , compute and
Use a recurrence relation to do fixpoint computation

## Slide 37: Fixpoint computation of reachable states
Computation:
  Initialize (initial set of states)
  Recur:
  Terminate if:
    Time-bounded: when the sum of time elapsed on all continuous transitions is
Problems:
  Termination not guaranteed for general case
  is not easy to compute in general
  Error in computing can blow-up leading to answers that are too conservative
Many Tools: SpaceEx, Flow*, C2E2, dReach, CORA (and a few others)

## Slide 38: Stability of hybrid systems
Hybrid systems can have surprising results with respect to stability
No uniform method like Lyapunov analysis for analyzing all hybrid systems
Example: Piecewise Linear (PWL) Dynamical System
  Special class of hybrid system, in which each mode has linear dynamics, guards, resets are all linear/affine
  Each mode in the PWL system can have stable dynamics (by doing eigen-value analysis), but resulting hybrid system may be unstable!

## Slide 39: Example
Dynamics in each mode are stable!

## Slide 40: Simulation results
Initial State

## Slide 41: Stability analysis for hybrid systems
Two main approaches1,2:
  Find a common Lyapunov function that works for all modes
    I.e. for each mode , dynamics are , find such that: , and
    Usually hard to find a “one-size-fits-all” Lyapunov function
  Find multiple Lyapunov functions, one for each mode
    In each mode its Lyapunov function value decreases, and at the switching instant the destination mode’s Lyapunov function value does not increase
    value decreases every time mode is entered
    Finding Lyapunov functions satisfying these conditions is again hard

## Slide 42: Design Application: Autonomous Guided Vehicle
Objective: Steer vehicle to follow a given track
Control inputs: linear vehicle speed , vehicle angular velocity , start/stop
Constraints on control inputs:
Designer choice: only if , otherwise

## Slide 43: On/Off control for Path following
Track
When , controller decides that vehicle goes straight, otherwise executes a turn command to bring error back in the interval
Turn right
Turn left
Go straight
Stationary

## Slide 44: Design Application: Robot Coordination
Autonomous mobile robots in a room, goal for each robot:
  Reach a target at a known location
  Avoid obstacles (positions not known in advance)
  Minimize distance travelled
Design Problems:
  Cameras/vision systems can provide estimates of obstacle positions
    When should a robot update its estimate of the obstacle position?
  Robots can communicate with each other
    How often and what information can they communicate?
  High-level motion planning
    What path in the speed/direction-space should the robots traverse?

## Slide 45: Path planning with obstacle avoidance
Goal
Assumptions:
  Two-dimensional world
  Robots are just points
  Each robot travels with a fixed speed
Dynamics for Robot :
  ;
Design objectives:
  Eventually reach
  Always avoid Obstacle1 and Obstacle 2
  Minimize distance travelled
Obstacle 1
Obstacle 2

## Slide 46: Divide path/motion planning into two parts
Computer vision tasks
Actual path planning task
Assume: vision algorithm identifies obstacles, and labels them with some easy-to-represent geometric shape (such as a bounding boxes)
  In this example, assume a sonar-based sensor, so we will use circles
Assuming the vision algorithm is correct, do path planning based on the estimated shapes of obstacles
Design challenge:
  obstacle shape estimate not the smallest shape containing the obstacle
  estimate varies based on distance from obstacle

## Slide 47: Estimation error
Robot maintains radii and that are estimates of obstacle sizes
Every seconds, executes following update to get estimates of shapes of each obstacle
  We don’t know , but we are guaranteed that we get a radius of an estimated shape of the obstacle that is exactly:
  is actual position of is actual (unknown) position of
Computation of is symmetric
Estimated shape
from distance
Estimated shape
from distance
Smallest shape
bounding obstacle
Estimated radius ,
where is a constant

## Slide 48: Path planning
Choose shortest path to target (to minimize time)
If estimate of obstacle 1 intersects , calculate two paths that are tangent to obstacle 1 estimate
If estimate of obstacle 2 intersects , or obstacle 1, calculate tangent paths
Plausible paths: and
Calculate shorter one as the planned path

## Slide 49: Dynamic path planning
Path planning inputs:
  Current position of robot
  Target position
  Position of obstacles and estimates
Output:
  Direction for motion assuming obstacle estimates are correct
May be useful to execute planning algorithm again as robot moves!
  Because estimates will improve closer to the obstacles
  Invoke planning algorithm every seconds

## Slide 50: Communication improves planning
Every robot has its own estimate of the obstacle
’s estimate of obstacle might be better than ’s
Strategy: every seconds, send estimates to other robot, and receive estimates
For estimate , use final estimate =
Re-run path planner

## Slide 51: Improved path planning through communication
Old path
New path available
because estimate of obstacle 1 improved after receiving estimate from

## Slide 52: Hybrid State Machine for Communicating Robot

## Slide 53: Advantage of using hybrid processes
Hybrid models combine computation, communication and control
Most real-world controllers are digital/discrete-time controllers: hybrid process/automata models describe underlying mathematical model for most CPS applications!
We can perform design-space exploration through simulations and check safety/correctness (later in the course)

## Slide 54: Bibliography
H. Lin and P. J. Antsaklis, "Stability and Stabilizability of Switched Linear Systems: A Survey of Recent Results," in IEEE Transactions on Automatic Control, vol. 54, no. 2, pp. 308-322, Feb. 2009.
Branicky, Michael S. "Multiple Lyapunov functions and other analysis tools for switched and hybrid systems." IEEE Transactions on automatic control 43.4 (1998): 475-482.
Talk by Goran Frehse, pdf of slides here: http://qmc.cs.aau.dk/slides/slides-frehse.pdf
SpaceEx: http://spaceex.imag.fr/
Flow*: https://flowstar.org/
dReach: http://dreal.github.io/dReach/
CORA: http://www.i6.in.tum.de/Main/SoftwareCORA