## Slide 1: Autonomous Cyber-Physical Systems: Communication, Coordination & Wrap-up
Fall 2020. CS 513.
Instructor: Jyo Deshmukh
USC Viterbi
School of Engineering
Department of Computer Science

## Slide 2: Multi-agent Autonomous Systems
Consensus
Coordination
Co-operation
Case studies

## Slide 3: Co-operative multi-agent systems
Each individual:
  Senses its immediate environment
  Communicates with others
  Processes gathered information
  Takes local actions in response
Swarm of birds

## Slide 4: Multi-agent robotic systems
Networks of vehicles
Drone swarms for biological applications, surveillance
Environment monitoring
Military applications
Warehouse robots
Industrial manufacturing robots

## Slide 5: Coordination tasks
Logic-based: Consensus, Synchronization, Team-Formin
Motion-based: Gather, Flock, Form a pattern
Sensor-based: Search, Estimate, Identify, Track, Map

## Slide 6: Types of multi-agent networks
set of unique identifiers
set of physical agents (states/inputs/dynamics)
Interaction graphs
From: http://coordinationbook.info/pdfs/SIAMDSminitutorial-DCRN-BulloCortesMartinez.pdf

## Slide 7: Basic Model for Consensus
Nodes:
Edges:
Neighbors of node
: value of node
: Algebraic graph/Network
  value
  topology or information flow
Olfati-Saber, Reza, and Richard M. Murray. "Consensus problems in networks of agents with switching topology and time-delays." IEEE Transactions on automatic control 49, no. 9 (2004): 1520-1533.

## Slide 8: Some neat things from algebraic graph theory
Laplacian matrix of a graph defined as:
If graph is weighted replace 1 with the weight of that edge
Multiplicity of the zero eigenvalue of the matrix is the number of components of the graph (nodes that can be reached from each other)
Speed of convergence of algorithms for flocking, rendezvous, consensus depend on the second smallest eigenvalue of the Laplacian matrix

## Slide 9: Consensus
Nodes and agree iff
Nodes of a network have reached consensus iff
Common value of all nodes is called “group decision value”
Dynamic graph : Dynamical system in which evolves according to dynamics function where

## Slide 10: -consensus problem
L be a function of
is an initial state of the system, then
-consensus problem to calculuate by applying inputs that only depend on and the neighbors of
is called a protocol with topology if the cluster satisfies the property that (i.e. if the feedback only uses a node and some subset of its neighbors)
above is called a distributed protocol: if

## Slide 11: Solving the -consensus problem
Protocol solves the -consensus problem iff there exists an asymptotically stable equilibrium of satisfiying for all
Some special cases:
  Max-consensus:
  Min-consensus:
  Average-consensus:

## Slide 12: Example of a consensus protocol
Imagine a network of agents with integrator dynamics
The protocol for fixed topology or switching topology (set of neighbors can change):
With time delay for each each

## Slide 13: Challenge problems in consensus
Different kinds of topologies
Different assumptions on structures of the graphs
Types of problems to solve (min/max/average)
How do you prove that the consensus algorithm actually converges?
  Requires ideas similar to Lyapunov functions
  Called disagreement functions that show that disagreement decreases over time
Olfati-Saber, Reza, and Richard M. Murray. "Consensus problems in networks of agents with switching topology and time-delays." IEEE Transactions on automatic control 49, no. 9 (2004): 1520-1533.

## Slide 14
Vehicle to Vehicle (V2V) and Vehicle to Everything(V2X)

## Slide 15: V2V communication
Single hop: Vehicle communicates directly with another vehicle
Multi-hop: Vehicle uses intermediate nodes for communication
Consensus around DSRC (Dedicated Short-Range Communication) using IEEE 802.11p/WAVE standards
Increasing use of 5G

## Slide 16: Taxonomy of applications for V2V/V2I
Based on taxonomy by Wilke1:
  Information services
  Safety services
  Individual motion control
  Group motion control
1. T. L. Willke, P. Tientrakool, and N. F. Maxemchuk, “A survey ofinter-vehicle communication protocols and their applications,”IEEECommun. Surveys Tuts., vol. 11, no. 2, pp. 3–20, 2nd Quart., 2009.
Material from:
Siegel, J.E., Erb, D.C. and Sarma, S.E., 2017. A survey of the connected vehicle landscape—Architectures, enabling technologies, applications, and development areas. IEEE Transactions on Intelligent Transportation Systems, 19(8), pp.2391-2406.

## Slide 17: Information services
Fault prediction and response (diagnostics, prognostics)
Data collection and generation (digital mapping, collision avoidance, path prediction, driving behavior optimization)
Data dissemination and distribution (streaming entertainment systems, music-sharing, gaming)
Efficiency improvement (improving traffic flow, reducing congestion traffic density estimation, optimal route planning)
Convenience services (Automated routing, tolling, tracking, parking vehicle locator)

## Slide 18: Safety services
Collision avoidance (visual cues like brake lights, blindspot elimination, 360o situational awareness)
Hazard reporting (enhanced perception, sense weather, disabled vehicles notifying other vehicles)
Driver monitoring (monitor impaired drivers)

## Slide 19: Individual motion control
Uses connectivity to issue warnings to vehicle operator or directly control actuators
For safety: collision avoidance
For efficiency: automated drafting
For both: assisted lane switching

## Slide 20: Group motion control
Platooning (reduces fuel consumption)
High-speed co-operative merging
Assisted obstacle avoidance
Intersection control (eliminating stop lights)

## Slide 21: V2V algorithms
Forward crash avoidance
Cooperative Adaptive Cruise Control
Cooperative Collision Avoidance
Cooperative Merging
https://www.its.dot.gov/research_archives/safety/v2v_comm_safety.htm

## Slide 22: Collision warning/avoidance
Two main problems:
  Signal detection
  Decision-making
Use own velocity, lead velocity, relative distance, acceleration, rate of change of relative distance to identify parameter values that are safe or unsafe
Lee, K. and Peng, H., 2005. Evaluation of automotive forward collision warning and collision avoidance algorithms. Vehicle system dynamics, 43(10), pp.735-751.

## Slide 23: Safe/Unsafe sets
PDFs indicate probability of hypothesis or being true

## Slide 24: Using a threshold criterion
Value of should be picked to minimize false alarms and miss rate

## Slide 25: Cooperative Adaptive Cruise Control (CACC)
Used for platoons of vehicles (e.g. trucks)
Several goals:
  Improve safety
  Improve traffic flow dynamics by damping disturbances (new cars, braking, bumps in the road)
  Increasing highway capacity by shorter following gaps
  Saving energy and pollution through aerodynamic drafting
  Improving driver comfort and convenience

## Slide 26: CACC with V2X
Many V2V variants based on where information comes from
  Immediate leader or/and follower or/and the overall Platoon Leader or/and any vehicle in range
Simplest scheme: Pairwise sharing between vehicle and immediate leader
V2I schemes: communicate with traffic management center/roadside devices either statically or dynamically
  Can help with intersections
  Can help with green-driving or eco-driving

## Slide 27: CACC uses different gap regulation strategies
Constant clearance or constant distance gap (CDG)
  Separation does not change with vehicle velocity
  Gives experience of mechanical linkage between vehicles
  Requires more formal platoon architecture and tight communication between platoon leader and followers
  Communication interruption can cause safety hazards
  Need larger gaps to ensure safety of platoon
  (Emergency brake by leader can cause domino effect)

## Slide 28: CACC uses different gap regulation strategies
Constant Time Gap
  Resembles how normal human drivers drive (except on 110 in LA )
  Distance between vehicles is proportional to their speed + a small fixed offset distance
  E.g. doubling of speed causes doubling of gap between vehicles
  Time gap criterion described in terms of time between rear bumper of leading vehicle and front bumper of trailing vehicle pass a fixed point on te roadway
  Often described as headway or time headway
  Vehicles in CTG CACC are often called a “string of vehicles” rather than platoon

## Slide 29: CACC string formation in trucks
One or more truck drivers activate CACC and set desired speed and gap
  May set preference for leader or follower when forming a new string
Local coordination: search for additional trucks or existing strings to couple with
Joining driver is displayed list of nearby trucks or strings (graphically or textually)
Once joining driver selects a platoon to couple with:
  local coordination confirms with platoon leader
  instructs leader to slow down
  instructs joining truck to speed up
  Lead driver and joining driver are shown a target speed and lane in which to travel
Once joining truck is behind the leader or string, CACC’s vehicle-following mode will engage, and lead truck’s speed will be restored and relayed

## Slide 30: CACC steady-state cruising
Steady-state cruising is what hopefully happens most of the time
Drivers still have to actively steer (unless they have lane-tracking-control) and monitor traffic
Steady-state cruising interrupted when trucks join or split strings, or when a non-platoon vehicle intervenes
Cut-ins can be handled by dynamically splitting the string and commanding a new leader and dynamically merging strings when the disturbing vehicle goes away

## Slide 31: CACC string splits and faults
CACC needs to handle trucks leaving string
Ideally, departing truck signals intent and remaining string close gaps to maintain platoon structure
In some cases may require string to be split while the truck in the middle departs
As you can see, the above protocols have NUMEROUS fault conditions, errors and abnormal operating conditions (obstacle in the road, accidents, etc.)
Safety: model each truck as an asynchronous process and reason about composition of asynchronous processes!
Specifications: Safety and String stability

## Slide 32: String stability
Suppose each vehicle looks only at vehicle in front, and for any pair of vehicles, the one with smaller index is the leader
We define two errors:
Here, is the range error, or the error from trying to maintain desired range , and is the range rate error
Assuming constant time-headway, i.e. , where is the constant time head-way for the vehicle, range error can be written as:

## Slide 33: String stability definition
For a uniform vehicle string,
A uniform vehicle string is string stable if
Assume each car’s following algorithm is represented by a linear system, then this translates to the overall system having gain less than 1
If you create a new platooning algorithm, string stability may be an important property to prove

## Slide 34: Autonomous Intersection Management
AIM protocol and its variants proposed based on V2I communication
Main idea :
  Each car equipped with a driver agent
  Each intersection equipped with an intersection manager
  Driver agents call ahead to reserve space-time in an intersection
  Intersection manager decides to grant or reject reservation requests according to an intersection control policy

## Slide 35: AIM protocol4
Approach vehicle announces arrival to manager
Vehicle indicates its size, predicted arrival time, velocity, acceleration, arrival and departure lanes
Intersection manager simulates vehicle’s path through the intersection, checking for conflicts with paths of previously processed vehicles
If there are no conflicts, issues a reservation
It is the vehicle’s responsibility to arrive at and travel through the reserved space-time block within some range of error tolerance
In case of conflict, intersection manager suggests an alternate later reservation
Car enters intersection only if reservation successful
Upon leaving intersection, car conveys successful passage to the manager

## Slide 36: Intersection control policies
Divide intersection into grid of reservation tiles

## Slide 37: Many AIM5 variants with different concerns
Decentralized (vehicles coordinating among themselves) vs. Centralized (manager)
Deliberative (planning entire trajectories) vs. reactive (planning trajectories in real-time)
Robust (Safety margins) vs. efficient (more throughput at the intersection)
Cooperative (optimizing overall traffic flow) vs. Egoistic (optimizing your own speed/time)
Homogenous (all vehicles treated the same) vs. Heterogeneous
Modeling AIM: asynchronous, timed, & hybrid process models used!

## Slide 38: Collaborative merge
Purpose: allow vehicles merging onto a freeway from a ramp to do so in safe fashion
Can be formulated as a specific case in autonomous intersection management
Specialized approaches based on highway ramp metering have existed for some time (these do not utilize V2V capability, and do not guarantee safety)

## Slide 39: Collaborative merge
Region at center of intersection called merging zone with length
Control zone of length where vehicles can communicate
Each vehicle modeled with simple second-order dynamics (position, velocity, acceleration)
Centralized solution based on layered control approaches

## Slide 40: Two-layered control approach for merging
Centralized approach (V2I only)
First layer
  Assumes each vehicle is traveling at constant speed
  Computes time for each vehicle to merge into the control zone based on this assumption
Second layer
  Determines conflicts in merging sequence
  Computes required acceleration value based on heuristic rules
Generalization with different layers of control has been proposed
Optimization: minimizing vehicle overlap (crash!) and travel time

## Slide 41: Decentralized approach
Virtual vehicle mapped onto the freeway before actual merging occurs
Allows vehicles to perform smoother and safer control actions
Uses slot-based traffic management (vehicles drive into a virtual slot)
Vehicles use V2V and V2I communication with vehicles in range
Other approaches based on MPC also exist

## Slide 42: V2I communication
Vehicle to Infrastructure communication
Applications:
  Electronic Toll Collection
  Intersection safety with Smart traffic lights
    (Cooperative Intersection Collision Avoidance System)
  Better route-planning with a traffic-congestion aware cloud system
  Computing on the cloud for complex optimization situations

## Slide 43: References
[1] Shladover, Steven E., et al. "Cooperative adaptive cruise control: Definitions and operating concepts." Transportation Research Record: Journal of the Transportation Research Board 2489 (2015): 145-152.
[2] ibid., https://escholarship.org/uc/item/7jf9n5wm
[3] Liang, Chi-Ying, and Huei Peng. "String stability analysis of adaptive cruise controlled vehicles." JSME International Journal Series C Mechanical Systems, Machine Elements and Manufacturing 43.3 (2000): 671-677.
[4] Stone, Peter, Shun Zhang, and Tsz-Chiu Au. "Autonomous intersection management for semi-autonomous vehicles." Routledge Handbook of Transportation. Routledge, 2015. 116-132.
[5] Qian, Xiangjun, et al. "Autonomous Intersection Management systems: criteria, implementation and evaluation." IET Intelligent Transport Systems 11.3 (2017): 182-189.
[6] de Campos, Gabriel Rodrigues, et al. "Traffic coordination at road intersections: Autonomous decision-making algorithms using model-based heuristics." IEEE Intelligent Transportation Systems Magazine 9.1 (2017): 8-21.
[7] Rios-Torres, Jackeline, and Andreas A. Malikopoulos. "A survey on the coordination of connected and automated vehicles at intersections and merging at highway on-ramps." IEEE Transactions on Intelligent Transportation Systems 18.5 (2017): 1066-1077.

## Slide 44: Now that you know how to design autonomous CPS
Security, Privacy are must-know!

## Slide 45: Security/Privacy for Autonomous CPS
Confidentiality: Ability to maintain secrecy from unauthorized users
  Eavesdropper should not be able to intercept and read messages sent between an Autonomous CPS agent and another agent, system or human
Integrity: Trustworthiness of received data
  If the V2X-enabled car receives a message from the cloud indicating that there is no traffic or obstacle in the next 500 meters, is the message trustworthy?
Availability: Ability of the system to be accessible
  Is it possible to make the self-driving car unresponsive by overwhelming its sensors with data?

## Slide 46: Security/Privacy for Autonomous CPS
Timeliness: Responsiveness, how recent is the data
  If an adversary keeps sending messages to the UAV, can it become unresponsive to the point that its basic control abilities are compromised?
Graceful Degradation: Can the system recover to successively reduced levels of operation in steps?
  If a sensor is compromised because of a malicious attack (e.g. an adversary flashing light into the camera, or producing fake ultrasonic pulses), can the system gracefully reach a safe state?
Privacy: Preventing unwanted transfer of information (through inference or correlation)
  Can the self-driving car leak information about the driver’s sensitive information to the infrastructure?

## Slide 47: Attacks and Attack Models
Attack model: kind of access the adversary has to the system
  Autonomous CPS applications offer a diverse set of possible attacks
Attack surface: the sum of all entry points with which the attacker can enter breach the system
  Sensors, actuators, communication present different kinds of attack vectors, rendering a large attack surface for an autonomous CPS
CPS systems are liable to:
  Cyber attacks
  Physical attacks
  Cyber-Physical attacks

## Slide 48: Taxonomy of attacks
Cyber attacks
  Network DDS
  Malware
  Exploiting software vulnerabilities: buffer overflows, code injection attacks, etc.
Physical attacks
  Sensor spoofing
  Sensor jamming
  Timing attacks
  Physical damage
CPS attacks
  Replay attacks
  State observation/inference
  Side-channel attacks
  Non-technical attacks (social engineering, phishing, etc.)

## Slide 49: Some interesting attacks from a CPS perspective
Sensor spoofing attack: Attacker provides fake sensor data
  Spoofing GPS signals
  Present a UAV/self-driving car with a doctored image that causes perception/decision layers to behave incorrectly
  Physical access to sensors permits masking or subtly changing sensor signals
Replay attack: Attacker intercepts insecure commands and replays them
  A malicious adversary could intercept messages sent in a V2X protocol, and replay the message, “safe to merge” when it is not safe to merge.

## Slide 50: Relevant attacks in CPS examples
Sensor jamming
  Signals sent using DSRC will critically influence autonomous vehicle coordination and cooperation, if these signals are jammed, autonomy will suffer
Timing attacks
  Information can be leaked by measuring the time required for a particular operation to be executed
  Many CPS applications use online optimization, path planning etc., and the time required to compute a decision may reveal secret information about internal state

## Slide 51: Relevant attacks in CPS
Side-channel attacks
  These attacks involve monitoring a physical quantity such as the power consumption, electromagnetic leaks, etc. to discover secret information about the system (e.g. can be used to guess a password based on the power profile of the CPU while it is decrypting the string).
  Timing attacks are a subclass of side-channel attacks
Information leakage/state inference
  By observing a CPS system, the attacker can create a state estimator for internal state of the system, which may be undesirable

## Slide 52: Themes in CPS security
Attack detection
Attack monitoring
Secure estimation/control
Privacy

## Slide 53: Attack detection
Attack models:
  False data/Sensor spoofing attacks
  Replay attacks
  Fault data injection attacks
Few main ideas:
  Design intrusion detection systems that detect anomalous traffic and flag alarms (for mostly cyber attacks)
  Construct appropriate observers that can detect and locate an attack
    Compute difference between estimated and measured quantities
    Using the state estimation Jacobian matrix
  Using game theoretic reasoning (attacker is player 2, system is player 1)
  In a networked setting: which sensors/nodes to choose for monitoring?

## Slide 54: Basic attack detection
Model of a CPS under attack
: state of the system
: unknown disturbance
Typical assumption: are linear functions described by matrices
is generally a multi-dimensional signal attacking any number of states of the system
Which states of the system are being attacked defines the attack signature

## Slide 55: Attack monitors2
Monitor is a deterministic algorithm that has access to continuous-time measurements and knowledge of system dynamics
Monitor raises a flag/alarm indicating presence or absence of an attack in addition to the set of sensors being attacked
An attack is detectable if the monitor raises an alarm
An attack is identifiable if the monitor is able to accurately identify which states are being attacked
An attack is undetectable if no monitor identifies an attack
Obviously, an undetectable attack is unidentifiable

## Slide 56: Undetectable & Unidentifiable attacks
Let and be two different initial states of a system.
An attack is undetectable if :
  I.e. output seen when system starts in state while under attack is the same as the output seen when the system starts in state (when not under attack)
An attack is unidentifiable if , where is an attack that uses either a lesser number of sensors or a different set of sensors than (I.e. and )
Technical conditions can be derived on detectability and identifiability of attacks for linear systems

## Slide 57: Types of monitors
Static monitors: verifies consistency of measurements without utilizing system dynamics or exploiting measurements taken at different times
Dynamic monitors: Make use of the knowledge of system dynamics
Active monitors: Injects an auxiliary input to reveal attacks
Centralized vs. distributed:
  In a networked system, a centralized attack detector can see all nodes in the system at once and use that for attack detection (not ideal because of central point of failure)

## Slide 58: Intrusion detection using statistical techniques
Assume that the observations of a process at each time follow some probability distribution (common assumption: multivariate normal distribution)
Use sample mean and sample covariance to define a statistic on new observed data
If the statistic shows large (or small values) then the observed data is anomalous and could indicate an attack
  Hotelling’s statistic = , where and are sample mean and covariance resp.

## Slide 59: Chi-squared detector
Residue of a Kalman filter: Difference between observed value and estimated value at time step
If residues of Kalman filter are i.i.d. with mean and covariance , then the detector is defined as:
Here, is the size of the window over which we are interested in detecting faults

## Slide 60: Secure control3
Given dynamical system:
And a total of sensors monitoring the system
Can we design a controller that :
    Makes the closed-loop system stable/exponentially stable?
    While facing an attack on sensors
For linear systems, , matrix

## Slide 61: Accomplishing secure control
For linear systems, you can show that the system can be secured by a controller if there exists a decoder (i.e. observer) that can reconstruct the state within some number of steps
Several technical conditions for linear systems that characterize when such observers can be constructed, how many sensors can be attacked but the system withstands the attacks, etc.
Several other bodies of work which utilize strategies such as : robust control, falling back to a sub-optimal controller, etc.

## Slide 62: Privacy in CPS
Privacy focuses on information flow properties between systems
Can my secret information flow to the adversary?
Can the adversary learn my private information through my public information?
Became a big issue for smart meter systems:
  Utility companies can infer presence or absence in the house based on the electricity consumption
  But, we want to share data with the utility company so that it can optimize some higher-level resource usage!
CPS privacy is usually a tradeoff between marginal utility gained by sharing information vs. loss of secrecy

## Slide 63: Privacy while using the cloud
Advanced encryption schemes such as partially homomorphic encryption can help share encrypted data (i.e. keeping your secrets, secret), while using a service provider like a cloud to do computationally heavy operations
Key idea: define an encryption scheme and an operation such that
Advantage: the cloud can do operations directly on the encrypted data, and send the encrypted result back. Since the ego system is the only one with the decryption key, this adds security
E.g. convex optimization on the cloud4

## Slide 64: Using logics to analyze information flow
New logics such as HyperLTL and its invariants
  LTL: property of single traces
  HyperLTL: properties of sets of traces

## Slide 65: What is a hyperproperty?
Logical formula that can be evaluated on two or more traces
(E.g. in Hyper-LTL):
Satisfying Set 1
Satisfying Set 2

## Slide 66: Examples of HyperLTL properties
Observational determinism
(For same inputs from low security users, we get same outputs to the low security users. Inputs from high-security users could be different)
Generalized noninterference
(If high inputs are the same, then if the low inputs are same, then the low outputs should be same)

## Slide 67: Applying Hyperproperties to CPS context
HyperSTL!
We can make predicates over signals leaking private information of a CPS to the external world
In contrast to HyperLTL where decisions are Boolean, in HyperSTL, we can have any functions of the internal state of the CPS application
Very new, evolving area

## Slide 68: References
T. McDermott, et al., Technical Report on Human Capital Development – Resilient Cyber Physical Systems, Available at: http://www.sercuarc.org/publications-papers/technical-report-human-capital-development-resilient-cyber-physical-systems/
Pasqualetti, F., Dörfler, F., & Bullo, F. (2013). Attack detection and identification in cyber-physical systems. IEEE Transactions on Automatic Control, 58(11), 2715-2729.
Paulo Tabuada’s talk on science of security: http://publish.illinois.edu/science-of-security-lablet/files/2015/.../SoSCPSWeek_Tabuada.pdf
Shoukry, Yasser, et al. "Privacy-aware quadratic optimization using partially homomorphic encryption." Decision and Control (CDC), 2016 IEEE 55th Conference on. IEEE, 2016.