## Slide 1: Autonomous Cyber-Physical Systems: Stability Analysis for Linear & Nonlinear Dynamical Systems
Fall 2026. CS 513.
Instructor: Jyo Deshmukh
Acknowledgment: Some of the material in these slides is based on the lecture slides for CIS 540: Principles of Embedded Computation taught by Rajeev Alur at the University of Pennsylvania. http://www.seas.upenn.edu/~cis540/
This lecture also uses some other sources, full bibliography is included at the end of the slides.

## Slide 2: Stability of Systems
Property capturing the ability of a system to return to a quiescent state after perturbation
  Stable systems recover after disturbances, unstable systems may not
  Almost always a desirable property for a system design
Fundamental problem in control: design controllers to stabilize a system
Problem: Cart-pole is inherently unstable, aim: keep it upright
Solution Strategy: Move cart in direction in the same direction as the pendulum’s falling direction
Design problem: Design a controller to stabilize the system by computing velocity and direction for cart travel

## Slide 3: Lyapunov stability
System
Equilibrium point when is zero (say
Equilibrium point is Lyapunov-stable if:
  For every ,
    There exists a , such that
      if then,
      for every we have
-ball
-ball

## Slide 4: Asymptotic + Exponential Stability
System
Equilibrium point is asymptotically-stable if:
  is Lyapunov-stable +
  There exists s.t. if , then
Equilibrium point is exponentially-stable if:
  is asymptotically stable +
  There exist s.t. if , then for all

## Slide 5: What do these definitions all mean?
Lyapunov stable: solutions starting close from equilibrium point must remain close (within forever
Asymptotically stable: solutions not only remain close, but also converge to the equilibrium
Exponentially stable: solutions not only converge to the equilibrium, but in fact converge at least as fast as a known exponential rate
  All stable linear systems are exponentially stable
  This need not be true for nonlinear systems!

## Slide 6: Analyzing stability for linear systems
Eigenvalues of a matrix :
  Value satisfying the equation . is called the eigenvector
  Equivalent to saying: values satisfying , where is the identity matrix
Interesting result for linear systems: System is asymptotically stable if and only if every eigenvalue of has a negative real part
Lyapunov stable if and only if every eigenvalue has non-positive real part
Nonlinear systems: no simple analysis technique exists
  Next time we will look at Lyapunov’s methods, which allow reasoning about stability of nonlinear systems

## Slide 7: Stability Analysis for Linear Systems
Given system where and is an matrix,
Interesting result for linear systems: System is asymptotically stable if and only if every eigenvalue of has a negative real part
Lyapunov stable if and only if every eigenvalue has non-positive real part
How to calculate eigenvalues?
  eigs(A) in Matlab
  import numpy as np
from numpy.linalg import eig
A = np.array([…])
w,v = eig(A)
Manual way: solve the characteristic equation of the matrix

## Slide 8: Stability analysis example for linear systems
Characteristic equation: i.e.
, or
i.e.,
Real part is positive represents an unstable linear system

## Slide 9: Stability analysis example for linear systems
Characteristic equation: i.e.
, or
i.e.,
Real part is negative represents a stable linear system

## Slide 10: Nonlinear Dynamical System
Simple Pendulum
  Arc length
  Linear velocity:
  Linear acceleration:
Friction

## Slide 11: Simple Pendulum Dynamics
Let , , and let , and
Rewriting previous equation:
  =
For small angles, the above equation is almost linear (replace by ), and we can use techniques for linear systems to show stability
But, for any larger angle (less than ), we know the pendulum eventually stops
How do we show pendulum system is stable?
Aleksandr Lyapunov
Russian mathematician
Use my method!!

## Slide 12: Lyapunov’s first method
Given
Step 1: find the Jacobian matrix for
Step 2: Set in to get a matrix in (say ) ( is the equilibrium point)
If linear system , is stable, original nonlinear system is stable locally at the equilibrium point. (Local = exists some neighborhood of equilibrium point)

## Slide 13: Lyapunov’s first method for pendulum
Dynamics:
  = ;
  Step 1:
  Step 2:
  Step 3:
    Eigenvalues of satisfy
    both eigenvalues have negative real parts
    Pendulum is locally stable

## Slide 14: Lyapunov’s second method
Method to prove global stability
Relies on notion of Lyapunov Functions
Intuition:
  Find Lyapunov function that could be interpreted as the energy of the system
  Stable systems eventually lose their energy and return to the quiescent state
  Prove that the energy of the system (as encoded by the Lyapunov function) decreases over time

## Slide 15: Lyapunov’s Second Method: the math
Assume w.l.o.g., that equilibrium point * is at the origin, i.e., 0
  Why is this okay?
is a Lyapunov function over the domain iff:
  : [Positivity condition]
  [Derivative negativity condition]
  if : ,
System is stable in the sense of Lyapunov if such a exists

## Slide 16: Illustration and Lie-derivative
decreases as system evolves, i.e. for every pair of points along a system trajectory,
In other words, is a decreasing function in time, or its derivative is negative semi-definite
is called Lie derivative of
By chain-rule,

## Slide 17: Lyapunov’s second method for pendulum
Choose Lyapunov function
Consider ; recall,
By observation, , except at , where it is 0
Let’s look at the Lie derivative

## Slide 18: Second method for asymptotic/exponential stability
is a Lyapunov function over the domain iff:
  : [Positivity condition]
  [Derivative negativity condition]
  if : ,
System is stable in the sense of Lyapunov if such a exists
Asymptotic stability: Change second condition to:
  [Derivative negativity condition]
Exponential stability: Change second condition to:
  or

## Slide 19: Challenges with Lyapunov’s second method
How do we find a Lyapunov function?
  Maybe use the physics of the system to understand what encodes “energy”
  For certain nonlinear systems (those with polynomial dynamics), can some algorithmic methods
  In general a hard problem
Yet, is a powerful approach to prove global stability

## Slide 20: Stability of hybrid systems
Hybrid systems can have surprising results with respect to stability
No uniform method like Lyapunov analysis for analyzing all hybrid systems
Example: Piecewise Linear (PWL) Dynamical System
  Special class of hybrid system, in which each mode has linear dynamics, guards, resets are all linear/affine
  Each mode in the PWL system can have stable dynamics (by doing eigen-value analysis), but resulting hybrid system may be unstable!

## Slide 21: Example
Dynamics in each mode are stable!

## Slide 22: Simulation results
Initial State

## Slide 23: What are the implications of this?
Most controllers/actuators operate at discrete-time intervals or are event-triggered
Could have multiple controllers/actuators that act at different time-steps
Stability becomes challenging to prove!

## Slide 24: Stability analysis for hybrid systems
Two main approaches1,2:
  Find a common Lyapunov function that works for all modes
    I.e. for each mode , dynamics are , find such that: , and
    Usually hard to find a “one-size-fits-all” Lyapunov function
  Find multiple Lyapunov functions, one for each mode
    In each mode its Lyapunov function value decreases, and at the switching instant the destination mode’s Lyapunov function value does not increase
    value decreases every time mode is entered
    Finding Lyapunov functions satisfying these conditions is again hard

## Slide 25: Bounded signals
A signal is bounded if there is a constant , s.t.
Bounded signals:
  Constant signal :
  Exponential signal: , for
  Sinusoidal signals:
Not bounded:
  for any
  Exponential signal: , for
This Photo by Unknown Author is licensed under CC BY-SA

## Slide 26: BIBO stability
A system with Lipschitz-continuous dynamics is BIBO-stable if:
  For every bounded input , the output from initial state is bounded
Simple helicopter model:
  Two rotors: Main rotor gives lift, tail rotor prevents helicopter from spinning
  Torque produced by tail rotor must perfectly counterbalance friction with main rotor, or the helicopter spins
Image credit: From Lee & Seshia: Introduction to Embedded Systems - A Cyber-Physical Systems Approach, http://leeseshia.org/

## Slide 27: Helicopter Model continued
: net torque on tail of the helicopter – difference between frictional torque exerted by main rotor shaft and counteracting torque by the tail rotor
: rotational velocity of the body
Torque = Moment of inertia Rotational acceleration
What happens when is a constant input?
is not bounded helicopter model is not BIBO-stable!