## Slide 1: Autonomous Cyber-Physical Systems: Vehicle to X Communication
Spring 2018. CS 599.
Instructor: Jyo Deshmukh

## Slide 2: Layout
Basic capabilities of V2V and V2I
Co-operative Adaptive Cruise Control
Autonomous Intersection Management
Collaborative Merging
Class Wrap-up and Big-picture story

## Slide 3: Wireless technologies and their use

## Slide 4: V2V communication
Single hop: Vehicle communicates directly with another vehicle
Multi-hop: Vehicle uses intermediate nodes for communication
V2V has been used for safety:
  Stopped vehicle or obstacle avoidance on highways
  Merging assistance from a slow incoming lane to a crowded road
  Intersection safety and collision warning systems
Consensus around DSRC (Dedicated Short-Range Communication) using IEEE 802.11p/WAVE standards
Potential applications:
  multi-vehicle sensor fusion for localization, mapping
  Platooning and energy management

## Slide 5: V2I communication
Vehicle to Infrastructure communication
Applications:
  Electronic Toll Collection
  Intersection safety with Smart traffic lights
    (Cooperative Intersection Collision Avoidance System)
  Better route-planning with a traffic-congestion aware cloud system
  Computing on the cloud for complex optimization situations

## Slide 6: Cooperative Adaptive Cruise Control (CACC)
Used for platoons of vehicles (e.g. trucks)
Several goals:
  Improve safety
  Improve traffic flow dynamics by damping disturbances (new cars, braking, bumps in the road)
  Increasing highway capacity by shorter following gaps
  Saving energy and pollution through aerodynamic drafting
  Improving driver comfort and convenience

## Slide 7: CACC with V2X
Many V2V variants based on where information comes from
  Immediate leader or/and follower or/and the overall Platoon Leader or/and any vehicle in range
Simplest scheme: Pairwise sharing between vehicle and immediate leader
V2I schemes: communicate with traffic management center/roadside devices either statically or dynamically
  Can help with intersections
  Can help with green-driving or eco-driving

## Slide 8: CACC uses different gap regulation strategies
Constant clearance or constant distance gap (CDG)
  Separation does not change with vehicle velocity
  Gives experience of mechanical linkage between vehicles
  Requires more formal platoon architecture and tight communication between platoon leader and followers
  Communication interruption can cause safety hazards
  Need larger gaps to ensure safety of platoon
  (Emergency brake by leader can cause domino effect)

## Slide 9: Constant Time Gap
Resembles how normal human drivers drive (except on 110 in LA )
Distance between vehicles is proportional to their speed + a small fixed offset distance
E.g. doubling of speed causes doubling of gap between vehicles
Time gap criterion described in terms of time between rear bumper of leading vehicle and front bumper of trailing vehicle pass a fixed point on te roadway
Often described as headway or time headway
Vehicles in CTG CACC are often called a “string of vehicles” rather than platoon

## Slide 10: Constant Safety-Factor Criterion
Motivated by guaranteeing that even most severe incidents would involve only one platoon
  With small constant-clearance-separations, severe incidents require hard braking
  Hardest braking would be by the last vehicle,
  Most dangerous condition is when lead vehicle has limited braking ability
  Sets minimum distance between platoons such that two platoons do not collide based on above factors
  Produces inter-platoon separation proportion to square of cruising speed

## Slide 11: CACC String formation in trucks
One or more truck drivers activate CACC and set desired speed and gap
  May set preference for leader or follower when forming a new string
CACC local coordination feature searches for additional trucks or existing strings to couple with
Joining driver is displayed list of nearby trucks or strings (graphically or textually)
Once joining driver selects a platoon to couple with, local coordination will confirm with platoon leader and instruct leader to slow down and joining truck to speed up
Lead driver and joining driver are shown a target speed and lane in which to travel
Once joining truck is behind the leader or string, CACC’s vehicle-following mode will engage, and lead truck’s speed will be restored and relayed

## Slide 12: CACC steady-state cruising
Steady-state cruising is what hopefully happens most of the time
Drivers still have to actively steer (unless they have lane-tracking-control) and monitor traffic
Steady-state cruising interrupted when trucks join or split strings, or when a non-platoon vehicle intervenes
Cut-ins can be handled by dynamically splitting the string and commanding a new leader and dynamically merging strings when the disturbing vehicle goes away

## Slide 13: CACC string splits and faults
CACC needs to handle trucks leaving string
Ideally, departing truck signals intent and remaining string close gaps to maintain platoon structure
In some cases may require string to be split while the truck in the middle departs
As you can see, the above protocols have NUMEROUS fault conditions, errors and abnormal operating conditions (obstacle in the road, accidents, etc.)
Safety: model each truck as an asynchronous process and reason about composition of asynchronous processes!
Specifications: Safety and String stability

## Slide 14: String stability
Suppose each vehicle looks only at vehicle in front, and for any pair of vehicles, the one with smaller index is the leader
We define two errors:
Here, is the range error, or the error from trying to maintain desired range , and is the range rate error
Assuming constant time-headway, i.e. , where is the constant time head-way for the vehicle, range error can be written as:

## Slide 15: String stability definition
For a uniform vehicle string,
A uniform vehicle string is string stable if
Assume each car’s following algorithm is represented by a linear system, then this translates to the overall system having the L-infinity gain being less than 1
If you create a new platooning algorithm, string stability may be an important property to prove

## Slide 16: Autonomous Intersection Management
AIM protocol and its variants proposed based on V2I communication
Main idea :
  Each car equipped with a driver agent
  Each intersection equipped with an intersection manager
  Driver agents call ahead to reserve space-time in an intersection
  Intersection manager decides to grant or reject reservation requests according to an intersection control policy

## Slide 17: AIM protocol4
Approach vehicle announces arrival to manager
Vehicle indicates its size, predicted arrival time, velocity, acceleration, arrival and departure lanes
Intersection manager simulates vehicle’s path through the intersection, checking for conflicts with paths of previously processed vehicles
If there are no conflicts, issues a reservation
It is the vehicle’s responsibility to arrive at and travel through the reserved space-time block within some range of error tolerance
In case of conflict, intersection manager suggests an alternate later reservation
Car enters intersection only if reservation successful
Upon leaving intersection, car conveys successful passage to the manager

## Slide 18: Intersection control policies
Divide intersection into grid of reservation tiles

## Slide 19: Many AIM5 variants with different concerns
Decentralized (vehicles coordinating among themselves) vs. Centralized (manager)
Deliberative (planning entire trajectories) vs. reactive (planning trajectories in real-time)
Robust (Safety margins) vs. efficient (more throughput at the intersection)
Cooperative (optimizing overall traffic flow) vs. Egoistic (optimizing your own speed/time)
Homogenous (all vehicles treated the same) vs. Heterogeneous
Modeling AIM: asynchronous, timed, & hybrid process models used!

## Slide 20: Collaborative merge
Purpose: allow vehicles merging onto a freeway from a ramp to do so in safe fashion
Can be formulated as a specific case in autonomous intersection management
Specialized approaches based on highway ramp metering have existed for some time (these do not utilize V2V capability, and do not guarantee safety)

## Slide 21: Collaborative merge
Region at center of intersection called merging zone with length
Control zone of length where vehicles can communicate
Each vehicle modeled with simple second-order dynamics (position, velocity, acceleration)
Centralized solution based on layered control approaches

## Slide 22: Two-layered control approach for merging
Centralized approach (V2I only)
First layer
  Assumes each vehicle is traveling at constant speed
  Computes time for each vehicle to merge into the control zone based on this assumption
Second layer
  Determines conflicts in merging sequence
  Computes required acceleration value based on heuristic rules
Generalization with different layers of control has been proposed
Optimization: minimizing vehicle overlap (crash!) and travel time

## Slide 23: Decentralized approach
Virtual vehicle mapped onto the freeway before actual merging occurs
Allows vehicles to perform smoother and safer control actions
Uses slot-based traffic management (vehicles drive into a virtual slot)
Vehicles use V2V and V2I communication with vehicles in range
Other approaches based on MPC also exist

## Slide 24: Design challenges Course Concepts
Modeling protocols, decision layer components
  Synchronous and Asynchronous processes
  Understanding system-level safety using synchronous and asynchronous composition
  Verification using Model Checking, Inductive Invariants
  Liveness properties with LTL, CTL
  Model-based and Scenario-based Testing approaches

## Slide 25: Design challenges Course Concepts
Modeling Controllers, Path planning
  Timed and Hybrid Processes, Dynamical Systems
  Markov Decision Processes & Markov Chains
  Verification using Model Checking, Inductive invariants, safety certificates (barrier certificates), Liveness checking with LTL, CTL, STL
  Testing using Falsification-based approaches
  Software synthesis using Temporal Logic-based approaches, reinforcement learning

## Slide 26: Design Challenges Course Concepts
Reasoning about environments, physical processes to be controlled
  Dynamical systems models, hybrid processes
  Signal Temporal Logic as a way to express Cyber-Physical systems specifications
  Testing and Falsification approaches
  Reasoning about safety and security
  Models for perception

## Slide 27: How does everything fit together?
You want to develop a new CPS/IoT system with autonomy
Analyze its environment: model it as a dynamical system or a stochastic system (e.g. PoMDPs)
Analyze the different components required in the software stack
  Perception vs. Decision/Planning vs. Control
Analyze what models to use for the control algorithms
  Choices are: Traditional control schemes (PID/MPC), state-machines (synchronous vs. asynchronous based on communication type), AI/planning algorithms, hybrid control algorithms, or combinations of these

## Slide 28: Safety is the key!!
Try to specify the closed-loop system as something you can simulate and see its behaviors
  Integrative modeling environment such as Simulink (plant models + software models)
  Specify requirements of how you expect the system to behave (STL, LTL, or your favorite spec. formalism)
    This step is a DO NOT MISS. It will provide documentation of your intent, and also a machine-checkable artifact
Test the system a lot, and then test some more
Apply formal reasoning wherever you can. Proofs are great if you can get them
Safety doesn’t end at modeling stage; continue reasoning about safety after deployment (through monitoring etc.)

## Slide 29: It’s been a fun class
Basics of Control
  PID, MPC, Nonlinear control, Observer design (Kalman filter)
Basics of Perception
  Vision-based systems, CNNs
Basics of Planning
  Path planning, Reinforcement learning
Basics of Security and Communicating Autonomous CPS
Models of computation
  Asynchronous, Synchronous, Timed, Hybrid Processes, Dynamical Systems, Probabilistic Models, Simulink
MODELING
AUTONOMY
Basics of Safety-Aware Mindset
Specification Languages (LTL, CTL, STL)
Falsification and Testing
Safety Invariants + Proofs
Reachability, Model Checking
SAFETY
Safe Autonomous CPS

## Slide 30: References
[1] Shladover, Steven E., et al. "Cooperative adaptive cruise control: Definitions and operating concepts." Transportation Research Record: Journal of the Transportation Research Board 2489 (2015): 145-152.
[2] ibid., https://escholarship.org/uc/item/7jf9n5wm
[3] Liang, Chi-Ying, and Huei Peng. "String stability analysis of adaptive cruise controlled vehicles." JSME International Journal Series C Mechanical Systems, Machine Elements and Manufacturing 43.3 (2000): 671-677.
[4] Stone, Peter, Shun Zhang, and Tsz-Chiu Au. "Autonomous intersection management for semi-autonomous vehicles." Routledge Handbook of Transportation. Routledge, 2015. 116-132.
[5] Qian, Xiangjun, et al. "Autonomous Intersection Management systems: criteria, implementation and evaluation." IET Intelligent Transport Systems 11.3 (2017): 182-189.
[6] de Campos, Gabriel Rodrigues, et al. "Traffic coordination at road intersections: Autonomous decision-making algorithms using model-based heuristics." IEEE Intelligent Transportation Systems Magazine 9.1 (2017): 8-21.
[7] Rios-Torres, Jackeline, and Andreas A. Malikopoulos. "A survey on the coordination of connected and automated vehicles at intersections and merging at highway on-ramps." IEEE Transactions on Intelligent Transportation Systems 18.5 (2017): 1066-1077.

## Slide 31: Platooning and Adaptive Cruise Control
Conventional ACC algorithm: constant gap control
Simplest model for following ego car:
  where, is the acceleration of the ego car, picked by a controller
One simple way to do this:
  where, are gains of a P and D component of a PD controller and is a feedforward gain

## Slide 32: Using communication
Another way of formulating ACC :
is a constant time gap (between 1 and 2 seconds)
: Controller gain
: spacing error including time headway control