## Slide 1: Autonomous Cyber-Physical Systems: Timed & Hybrid Dynamical Systems
Fall 2026. CSCI 513.
Instructor: Jyo Deshmukh
Acknowledgment: Some of the material in these slides is based on the lecture slides for CIS 540: Principles of Embedded Computation taught by Rajeev Alur at the University of Pennsylvania. http://www.seas.upenn.edu/~cis540/

## Slide 2: Models of Computation
[1] Nicolescu, Gabriela; Mosterman, Pieter J., eds. (2010). Model-Based Design for Embedded Systems. Computational Analysis, Synthesis, and Design of Dynamic Systems. 1. Boca Raton: CRC Press.
Synchronous Process Models
Asynchronous Process Models
Continuous-time models/Dynamical system models
  Like Synchronous, but time evolves continuously
Timed & Hybrid Dynamical Models

## Slide 3: Timed ESMs
Like asynchronous ESMs, have input, output channels, state variables
Special type of state variable called “clock”
Clock variables evolve continuously in time
ESM can “stay” in a mode with clock increasing monotonically from the start value
off
dim
bright
(press==1)?
c:=0
(press==1)?
clock c:=0
(press==1)? (c1)
(press==1)? (c1)

## Slide 4: Transitions of a timed ESM
Mode switch: discrete action
  machine moves from one mode to another
  guard on the transition must be true for mode switch to occur
  update specified by the transition will update/reset clock variables
off
dim
bright
(press==1)?
c:=0
(press==1)?
clock c:=0
(press==1)? (c1)
(press==1)? (c1)
(off,0.5)
(dim,0)
(press==1)?

## Slide 5: Transitions of a timed ESM
In a mode: Timed action
When machine stays in any given mode for time each clock variable increases by and all other state variables remain unchanged
Captures timing constraints
  Resetting c to 0 from offdim and guard c1 from dimoff specifies that these mode switches are 1 second apart
off
dim
bright
(press==1)?
c:=0
(press==1)?
clock c:=0
(press==1)? (c1)
(press==1)? (c1)

## Slide 6: Timed Processes: explicit clock variables
Clock variables
  Like other state variables, can be used in guards
  Can be reset to 0 during mode switches
  When the machine is in a given mode for duration the clock variable increases by
off
dim
bright
(press==1)?
c:=0
(press==1)?
clock c:=0
(press==1)? (c1)
(press==1)? (c1)

## Slide 7: Timed Process Execution
off
dim
bright
(press==1)?
c:=0
(press==1)?
clock c:=0
(press==1)? (c1)
(press==1)? (c1)
(off,0)
(off,0.5)
(dim,0)
(press==1)?
(dim,0.8)
(press==1)?
(bright,0.8)
Machine execution is through alternating timed transitions and mode switches

## Slide 8: Timed Process Execution
off
dim
bright
(press==1)?
c:=0
(press==1)?
clock c:=0
(press==1)? (c1)
(press==1)? (c1)
(off,0)
(off,0.5)
(dim,0)
(press==1)?
(dim,3.8)
Machine execution is through alternating timed transitions and mode switches
(press==1)?
(off,3.8)

## Slide 9: Timed Buffer
Input channel in of type bool
Output channel out of type bool
State variable x of type bool+. The value indicates empty
If x is , then read new value into x, and set clock to 0
If clock value is seconds, output value of x, and set x to
bool
out
bool in
x:= , clock c:=0
Tin (x==) & in?
x:=in; c:=0;
Tout (c2)
{ out := x;
x := }
Tinfull in?

## Slide 10: Timed State Machine representation
Mode captures whether x==
Clock variable tracks the time that elapsed since x received a value
Guard ensures that at least 2 seconds pass before the value of x is output
Guard does not force transitions
  can keep increasing while process remains in mode full
How do we make sure that process does not remain in full mode for at most 3 seconds?
empty
full
c out:=x, x≔
in? x:=in, c:=0
c:=0
in?

## Slide 11: Clock invariants
Attempt 1: we could make the guard
Attempt 1 fails because:
  You could keep getting new input (self-loop executes) till
Larger problem: Guards are non-forcing: nothing requires the guard to be executed
We can fix this by introducing clock invariants
Clock invariant of any mode: symbolic expression that must evaluate to true at all times, and if not, the process must exit that mode
empty
full
c out:=x, x≔
in? x:=in, c:=0
c:=0
in?

## Slide 12: Clock invariants
Add clock invariant:
(mode==full) (c 3)
Forces process to leave mode full if c becomes greater than 3
Staying in mode full when c would violate the clock invariant
Useful construct to limit how long a process stays in a certain mode
empty
full
c
c out:=x, x≔
in? x:=in, c:=0
c:=0
in?

## Slide 13: Why model using invariants and guards?
Each mode is a guard-enabled task; if guard is true, task is executed
  Going from one mode to another is a task switch
Checking if process leaves mode and goes to depends on if incoming guard of is true
Staying in does not/should not depend on the guard of
So, we use invariants:
  a condition always checked in a given mode

## Slide 14: Example with two clocks
Model with one input channel and two output channels: out1 and out2
Clock c tracks time elapsed since occurrence of the input task execution
Clock d tracks time elapsed since occurrence of output task for out1
Behavior of process: If input event occurs at some time t, then process issues output # on out1 some time t’ [t,t+1] and then issues output * on out2 at time t’’ [t’+1, t+2]
wait1
c1
idle
Wait2
c2
clock c,d:=0
in? c:=0
out1!#;d:=0
d
out2!*

## Slide 15: Formal recap of a timed process
Timed process consists of:
  An asynchronous process, where some of the state variables are of type clock (ranging over non-negative reals)
  A clock invariant I which is a Boolean expression over the state variables
Inputs, Outputs, States, Initial states, Actions: Internal, Input and Output: same as for asynchronous processes
Timed Action: Given a state q and time , action q q’ specifies a transition of duration if:
  q’ represents a state where the non-clock variables have the same value as in q, i.e. q’(x) = q(x)
  q’ represents a state where the clock variables in q are incremented by , i.e. q’(c) = q(c) + and
  For all times t [q(c), q(c)+], the clock invariant I is satisfied
  If clock invariant is convex, enough to check clock invariant at q(c) and q(c)+

## Slide 16: Composing Timed Processes
empty
full
c1
c1B1 out1:=x1, x1≔
in? x1:=in, c1:=0
c1:=0
empty
full
c2
c2B2 out2:=x2, x2≔
in? x2:=in, c2:=0
c2:=0
Each process stays in mode full for
Need to construct a new process with 4 new modes
Each new mode is a pair consisting of modes from process 1 and 2
Mode switches in the new machine correspond to mode switches in the old machine
Interesting timing behavior can arise!

## Slide 17: Composing Timed Processes
empty
full
c1 A1
c1B1 out1:=x1
in? x1:=in, c1:=0
c1:=0
empty
full
c2 A2
c2B2 out2:=x2
in? x2:=in, c2:=0
c2:=0
in?
in?
empty,
empty
full, empty
c1A1
empty, full
c2A2
full,full
c1A1
c2A2
c1B1 out1:=x1
c1B1 out1:=x1
in?
in?
c2B2 out2:=x2
c2B2 out2:=x2
in? x1:=in, c1:=0,
x2:=in, c2:=0
in? x1:=in, c1:=0

## Slide 18: Semi-synchrony
If B1 A1 B2 :
(full,full) (full,empty) can never be enabled!
Why?
reaches and the process gets kicked out of state (full,full)
But cannot be greater than so, guard from (full,full) to (full,empty) is not enabled!
empty,
empty
full, empty
c1A1
empty, full
c2A2
full,full
c1A1
c2A2
c1B1 out1:=x1
c1B1 out1:=x1
in?
in?
c2B2 out2:=x2
c2B2 out2:=x2
in? x1:=in, c1:=0,
x2:=in, c2:=0
in? x1:=in, c1:=0

## Slide 19: Semi-synchrony
If B1 A1 B2 :
  (full,full) (full,empty) cannot happen
If B1 A1 B2 :
  (full, full) (empty,full) will happen eventually
out1 guaranteed to happen before out2
Implicit coordination based on delays
  Both process clocks increase in tandem
  Global clock-based synchronization
empty,
empty
full, empty
c1A1
empty, full
c2A2
full,full
c1A1
c2A2
c1B1 out1:=x1
c1B1 out1:=x1
in?
in?
c2B2 out2:=x2
c2B2 out2:=x2
in? x1:=in, c1:=0,
x2:=in, c2:=0
in? x1:=in, c1:=0

## Slide 20: Pacemaker Modeling as a Timed Process
Most material that follows is from this paper:
Z. Jiang, M. Pajic, S. Moarref, R. Alur, R. Mangharam, Modeling and Verification of a Dual Chamber Implantable Pacemaker, In Proceedings of Tools and Algorithms for the Construction and Analysis of Systems (TACAS), 2012.
Alur’s textbook has detailed descriptions of some other pacemaker components

## Slide 21: How does a healthy heart work?
SA node (controlled by nervous system) periodically generates an electric pulse
This pulse causes both atria to contract pushing blood into the ventricles
Conduction is delayed at the AV node allowing ventricles to fill
Finally the His-Purkinje system spreads electric activation through ventricles causing them both to contract, pumping blood out of the heart
Electrical Conduction System of the Heart

## Slide 22: What do pacemakers do?
Aging and/or diseases cause conduction properties of heart tissue to change leading to changes in heart rhythm
Tachycardia: faster than desirable heart rate impairing hemo-dynamics (blood flow dynamics)
Bradycardia: slower heart rate leading to insufficient blood supply
Pacemakers can be used to treat bradycardia by providing pulses when heart rate is low

## Slide 23: Implantable Pacemaker modeling

## Slide 24: How dual-chamber pacemakers work
Two fixed leads on wall of right atrium and ventricle respectively
Activation of local tissue sensed by the leads (giving rise to events Atrial Sense (AS) and Ventricular Sense (VS))
Atrial Pacing (AP) or Ventricular Pacing (VP) are delivered if no sensed events occur within deadlines
Heart
Pacemaker
AS
VS
AP
VP

## Slide 25: The LRI mode of operation explained
ASed
LRI
c K
VP? c:=0
VS? c:=0
AS?
VS? c:=0
VP? c:=0
c K AP!; c:=0
K= 850ms
LRI = lower rate interval
LRI component keeps heart rate above minimum level
One of the pacemaker modes of operation that models the basic timing cycle
Measures the longest interval between ventricular events
Clock reset when VS or VP received
No AS received LRI outputs AP after K time units

## Slide 26
Finite State Automata: A 3-slide introduction

## Slide 27: Finite state automata
Famous equivalence between finite state automata and regular expressions
a-z
a-z,0-9
[a-z][a-z 0-9 ]
a-z
a-z
0-9
[a-z][0-9]*[a-z]
State
Accepting
state
*
0-9

## Slide 28: How does a finite state automaton work?
Starts at the initial state
In , if it receives a letter in a-z, goes to
  else, it goes to
In , if it receives a number in 0-9, it stays in
else, it goes to (as it received a-z)
In , no matter what it gets, it stays in
is an accepting state where computation halts
Any string that takes the machine from to is accepted by the machine
a-z
a-z
0-9
*
0-9

## Slide 29: Language of a finite state automaton
What strings are accepted by ?
  ab, zy, s2r, q123s, u3123123v, etc.
What strings are not accepted by ?
  2b, 334a, etc.
The set of all strings accepted by is called its language
The language of a finite state automaton consists of strings, each of which can be arbitrarily long, but finite
a-z
a-z
0-9
*
0-9

## Slide 30: Timed Automata
Useful tool to do timing analysis and explore properties of timed processes
State-space of timed automata is infinite (clocks can become arbitrarily large!)
But some questions about timed automata behavior can still be answered exactly
  Does the automaton accept any string? (also known as emptiness problem)
  Reachability of a particular configuration
We will revisit this later in the course

## Slide 31: Timing Analysis
x>=3  y:=0
A
x<=5
(y >= 6)?
(x = 7)?
x,y:=0
(y >= 2)?
B
x<=7
C
x8
y 5
(x <= 4)?
D
E
F
Which of D, E, F can be reached?
Needs careful propagation of reachable combinations of x and y
x , y when we reach B
x y when we reach C
x , y when you exit C
OR x y and machine stops

## Slide 32: How is such analysis done?
The key challenge is that if the automata has loops, then how do we know that our procedure for propagation of symbolic clock constraints will terminate?
The key insight by first papers on timed automata was that there is only a finite number of regions in the clock-space that can be visited
This gives a “pumping lemma” style argument*
Allows abstracting a finite timed automaton to an automaton where modes/states represent the regions
This was expensive, and improved by using zone-based constructions
  (zones are a uniform representation of constraints that arise during analysis)

## Slide 33
Hybrid Dynamical Systems

## Slide 34: Hybrid Process
Generalization of a timed process
Instead of timed transitions, we can have arbitrary evolution of state/output variables, typically specified using differential equations
?
?
off
on

## Slide 35: Bang-bang control (thermostat) hybrid automaton
?
?
off
on

## Slide 36: Executions of Thermostat
Initial state : (off, ),
If thermostat enters mode off with , then
Mode switch enabled when , and must happen before , i.e. at
In mode on, it heats the room according to:
Mode switch enabled when , and must happen before , i.e. at
?
?
off
on

## Slide 37: Behavior of thermostat
temperature
mode
time
time

## Slide 38: Hybrid Automata: State machines for hybrid processes
USC Viterbi
School of Engineering
Department of Computer Science
Mode: Vertical travel subject to gravity
Standard coordinate system
Down is negative, Up is positive
is negative because the velocity is becoming more negative (magnitude is increasing)
Sign of as the ball approaches ground is negative

## Slide 39: Hybrid Automata: State machines for hybrid processes
USC Viterbi
School of Engineering
Department of Computer Science
= 0
When does vertical travel end?
Discrete transition!
  Ball goes from vertical travel to impact and back to vertical travel
goes from downward to upward!
I.e.
restitution coefficient measures fraction of speed retained after bounce

## Slide 40: Hybrid Automata: State machines for hybrid processes
USC Viterbi
School of Engineering
Department of Computer Science
Mode: Vertical travel subject to
Vertical travel mode resumed
Initially some positive upward velocity
makes this velocity decrease
Eventually, will be zero, and then negative
But it is still the same “mode” : vertical travel subject to gravity

## Slide 41: Hybrid automaton for bouncing ball
What happens as ?
This is not a cartoon of a ball bouncing and traveling horizontally, just vs.

## Slide 42: Hybrid Process
Continuous action/transition:
Discrete mode does not change
=
satisfies the given dynamical equation for mode
At all times , the state satisfies the invariant for mode

## Slide 43: Hybrid Process
Discrete action/transition:
  Happens instantaneously
  Changes discrete mode to
  Can execute only if evaluates to true
  Changes state variable value from to
  should satisfy mode invariant of
/

## Slide 44: Executions of a hybrid process
At each cell boundary, assume that the guard is the equation of the boundary, and the reset is where
Invariant for each cell/mode is the open set enclosed by its boundaries
Suppose initial state is
(0,0)
(0,1)
(0,2)
(0,3)
(1,0)
(2,0)
(3,0)

## Slide 45: Zeno’s Paradox
Greek philosopher Zeno’s race between Achilles and a tortoise
  Tortoise has a head start over Achilles, but is much slower
  If Achilles is d meters behind at the beginning of a round
  and during the round, suppose Achilles runs d meters
  but by then, tortoise has moved a little bit further
  At the beginning of the next round, Achilles is still behind, by meters [0<<1]
By induction, if we repeat this for infinitely many rounds, Achilles will never catch up!
What is the mistake made by Zeno?
If sum of durations between successive discrete actions converges to constant, then an execution with infinitely many discrete actions describes behavior only up to time (and does not tell us the state of the system at time and beyond
Zeno assumes that if there are infinitely many points Achilles must “check off,” then it must take infinite time. But in fact, the times shrink and form a convergent series.

## Slide 46: Hybrid automaton for bouncing ball
As the ball approaches the ground, the number of discrete transitions occurring in any time interval tends to infinity: in the limit, there will be only discrete transitions and time will stop!

## Slide 47: How to deal with Zeno behavior
An infinite execution is called Zeno if infinite sum of all the durations is bounded by a constant, and non-Zeno if the sum diverges
Any state in a hybrid process is called Zeno if:
  If every execution starting in state is Zeno
  Non-Zeno if there exists some non-Zeno starting in that state
Hybrid process is non-Zeno if any state that you can reach from the initial state is non-Zeno
Thermostat: non-Zeno, Bouncing ball: Zeno
Dealing with Zeno: remove Zeno-ness through better modeling

## Slide 48: Non-Zeno hybrid process for bouncing ball
halt
bounce

## Slide 49: Reachability analysis
Suppose the grid world represents the configuration space of a robot
How do we analyze: Does the robot reach the error cell?
  Easy if we have only one initial state: just simulate!
What if the initial position of the robot is not certain (could be a set)?
What if the dynamics are not certain?
(0,0)
(0,1)
(0,2)
(0,3)
(1,0)
(2,0)
(3,0)
Initial states

## Slide 50: Time-bounded Reachability Analysis
Fundamental problem for dynamical systems
Simulation:
  Given an initial condition , compute solution such that
Time-bounded Reachability:
  Given a set of initial conditions , and a time T, compute the set such that
  A useless (but correct) answer is
  How do we find a “tight” reachable set?

## Slide 51: Computing Reachable Sets3
Main idea: compute successor states
  For a given set of states,
  For a given set ,
  For a given set , compute and
Use a recurrence relation to do fixpoint computation

## Slide 52: Fixpoint computation of reachable states
Computation:
  Initialize (initial set of states)
  Recur:
  Terminate if:
    Time-bounded: when the sum of time elapsed on all continuous transitions is
Problems:
  Termination not guaranteed for general case
  is not easy to compute in general
  Error in computing can blow-up leading to answers that are too conservative
Many Tools: SpaceEx, Flow*, C2E2, dReach, CORA (and a few others)

## Slide 53: Stability of hybrid systems
Hybrid systems can have surprising results with respect to stability
No uniform method like Lyapunov analysis for analyzing all hybrid systems
Example: Piecewise Linear (PWL) Dynamical System
  Special class of hybrid system, in which each mode has linear dynamics, guards, resets are all linear/affine
  Each mode in the PWL system can have stable dynamics (by doing eigen-value analysis), but resulting hybrid system may be unstable!

## Slide 54: Example
Dynamics in each mode are stable!

## Slide 55: Simulation results
Initial State

## Slide 56: Stability analysis for hybrid systems
Two main approaches1,2:
  Find a common Lyapunov function that works for all modes
    I.e. for each mode , dynamics are , find such that: , and
    Usually hard to find a “one-size-fits-all” Lyapunov function
  Find multiple Lyapunov functions, one for each mode
    In each mode its Lyapunov function value decreases, and at the switching instant the destination mode’s Lyapunov function value does not increase
    value decreases every time mode is entered
    Finding Lyapunov functions satisfying these conditions is again hard

## Slide 57: Design Application: Autonomous Guided Vehicle
Objective: Steer vehicle to follow a given track
Control inputs: linear vehicle speed , vehicle angular velocity , start/stop
Constraints on control inputs:
Designer choice: only if , otherwise

## Slide 58: On/Off control for Path following
Track
When , controller decides that vehicle goes straight, otherwise executes a turn command to bring error back in the interval
Turn right
Turn left
Go straight
Stationary

## Slide 59: Design Application: Robot Coordination
Autonomous mobile robots in a room, goal for each robot:
  Reach a target at a known location
  Avoid obstacles (positions not known in advance)
  Minimize distance travelled
Design Problems:
  Cameras/vision systems can provide estimates of obstacle positions
    When should a robot update its estimate of the obstacle position?
  Robots can communicate with each other
    How often and what information can they communicate?
  High-level motion planning
    What path in the speed/direction-space should the robots traverse?

## Slide 60: Path planning with obstacle avoidance
Goal
Assumptions:
  Two-dimensional world
  Robots are just points
  Each robot travels with a fixed speed
Dynamics for Robot :
  ;
Design objectives:
  Eventually reach
  Always avoid Obstacle1 and Obstacle 2
  Minimize distance travelled
Obstacle 1
Obstacle 2

## Slide 61: Divide path/motion planning into two parts
Computer vision tasks
Actual path planning task
Assume: vision algorithm identifies obstacles, and labels them with some easy-to-represent geometric shape (such as a bounding boxes)
  In this example, assume a sonar-based sensor, so we will use circles
Assuming the vision algorithm is correct, do path planning based on the estimated shapes of obstacles
Design challenge:
  obstacle shape estimate not the smallest shape containing the obstacle
  estimate varies based on distance from obstacle

## Slide 62: Estimation error
Robot maintains radii and that are estimates of obstacle sizes
Every seconds, executes following update to get estimates of shapes of each obstacle
  We don’t know , but we are guaranteed that we get a radius of an estimated shape of the obstacle that is exactly:
  is actual position of is actual (unknown) position of
Computation of is symmetric
Estimated shape
from distance
Estimated shape
from distance
Smallest shape
bounding obstacle
Estimated radius ,
where is a constant

## Slide 63: Path planning
Choose shortest path to target (to minimize time)
If estimate of obstacle 1 intersects , calculate two paths that are tangent to obstacle 1 estimate
If estimate of obstacle 2 intersects , or obstacle 1, calculate tangent paths
Plausible paths: and
Calculate shorter one as the planned path

## Slide 64: Dynamic path planning
Path planning inputs:
  Current position of robot
  Target position
  Position of obstacles and estimates
Output:
  Direction for motion assuming obstacle estimates are correct
May be useful to execute planning algorithm again as robot moves!
  Because estimates will improve closer to the obstacles
  Invoke planning algorithm every seconds

## Slide 65: Communication improves planning
Every robot has its own estimate of the obstacle
’s estimate of obstacle might be better than ’s
Strategy: every seconds, send estimates to other robot, and receive estimates
For estimate , use final estimate =
Re-run path planner

## Slide 66: Improved path planning through communication
Old path
New path available
because estimate of obstacle 1 improved after receiving estimate from

## Slide 67: Hybrid State Machine for Communicating Robot

## Slide 68: Advantage of using hybrid processes
Hybrid models combine computation, communication and control
Most real-world controllers are digital/discrete-time controllers: hybrid process/automata models describe underlying mathematical model for most CPS applications!
We can perform design-space exploration through simulations and check safety/correctness (later in the course)

## Slide 69: Bibliography
H. Lin and P. J. Antsaklis, "Stability and Stabilizability of Switched Linear Systems: A Survey of Recent Results," in IEEE Transactions on Automatic Control, vol. 54, no. 2, pp. 308-322, Feb. 2009.
Branicky, Michael S. "Multiple Lyapunov functions and other analysis tools for switched and hybrid systems." IEEE Transactions on automatic control 43.4 (1998): 475-482.
Talk by Goran Frehse, pdf of slides here: http://qmc.cs.aau.dk/slides/slides-frehse.pdf
SpaceEx: http://spaceex.imag.fr/
Flow*: https://flowstar.org/
dReach: http://dreal.github.io/dReach/
CORA: http://www.i6.in.tum.de/Main/SoftwareCORA