## Slide 1: Autonomous Cyber-Physical Systems: Basics of Control
Fall 2021. CS 513.
Instructor: Jyo Deshmukh

## Slide 2: Layout
Introduction to basics of linear control (without any Laplace transforms)
Introduction to nonlinear control and rule-based control
Introduction to observer design

## Slide 3: What is control theory?
Engineering techniques and theory or control of dynamical systems
Objective:
  Regulate system so that it behaves in desired fashion
  Ensure timely action to changes in system behavior
  Make sure control action does not cause system to … lose control

## Slide 4: Model-based Design
Mathematical and visual method commonly used for design controllers
Development is manifested in four steps:
  Create a dynamical system model of the plant
  Design/synthesize a controller (model)
  Simulate/test the closed-loop system for different environment (exogenous) inputs
  Generate code from the controller model and deploy the controller

## Slide 5: “Plant”
Terminology inherited from the (chemical) process industry
Can represent any physical component to be controlled, e.g. electrical, electronic, mechanical, etc.
Convenient to model such systems as ordinary differential equations (ODEs)
  State variables of ODEs represent physical quantities, e.g. pressure, temperature, Velocity, acceleration, current, voltage, etc.

## Slide 6: Open-loop vs. Closed-loop control
Open-loop or feed-forward control
  Control action does not depend on plant
  Common in many applications!
Pros:
  Cheaper, few sensors required, logic pretty straightforward
Cons:
  Quality of control poor without human intervention
  Not adaptive!
Plant
Controller

## Slide 7: Closed-loop or Feedback Control
Controller adjusts controllable inputs in response to observed outputs
  Can respond better to variations in disturbances
  Performance depends on how well outputs can be sensed, and how quickly controller can track changes in output
Many different flavors of feedback control
Plant
Controller

## Slide 8: Feedback Control
General mathematical model for feedback control
ODE representing time evolution of plant dynamics
Equation mapping plant states to observed plant
outputs
: Inputs from the Environment
Plant state variable
: Control Inputs to the Plant
: Observations of the plant
(Stateless) Feedback Control

## Slide 9: Linear Control
Linear systems are easier to analyze, understand, theorize

## Slide 10: Linear Control
Linear systems are easier to analyze, understand, theorize
Above equations reduce to:
Consider some constant input , which can be assumed w.l.o.g. to be zero, then
D: Often assumed to be zero
For simplicity, let (identity matrix),
i.e., the state is fully observable

## Slide 11: Simple Linear Feedback Control: Reference Tracking
Controller
Plant
Common objective: make plant state track the reference signal
For convenience, let (identity) and (zero matrix), i.e. full state is observable through sensors, and input has no immediate effect on output
For simplicity, assume we are tracking the zero signal, i.e.

## Slide 12: Simple Linear Feedback Control: Reference Tracking
Controller
Plant
Closed-loop dynamics:
Pick such that closed-loop system has desirable behavior
To make closed-loop system stable, pick such that eigenvalues of have negative real-parts
Controller designed this way also called pole placement controller
For simplicity, assume we are tracking the zero signal, i.e.

## Slide 13: Designing a pole placement controller
Note unstable plant!
Let . Then,
satisfy equation = 0
  Suppose we want eigenvalues at then equation would be:
  Comparing two equations, , and
  This gives . Thus controller with stabilizes the plant!
Controller
Plant

## Slide 14: Linear Quadratic Regulator
Pole placement involves heuristics (we arbitrarily decided where to put the eigenvalues)
Principled approach is to put the poles such that the closed-loop system optimizes the cost function:
is called state cost, is called control cost
Given a feedback law: , can be found precisely
In Matlab, there is a simple one-line function lqr to do this!

## Slide 15: Linear Control System Basics
Linear control system has the following form:
:describes state evolution
: describes how states are observed, may be often
Important ideas: Controllability and Observability
: State [Internal to the process being controlled]
: Control Input [actuator command]
: Output [what sensor reads]

## Slide 16: Controllability
Can we always choose eigenvalues to find a stabilizing controller? NO!
For what if is unstable, and is ?
  No controller can ever stabilize the system
How do we determine for a given , whether there is a controller?
Controllability:
  Can we find the condition on the system design that ensures that we can always move the system to whichever state/output we want?
  Important question that affects which actuators we pick for the system

## Slide 17: Checking Controllability
Find controllability matrix
[ is the state-dimension]
System is controllable if has full row rank. (i.e. rows are linearly independent)
Example:

## Slide 18: Checking Controllability
rank(R) = 3 (i.e. full rank)
So system is controllable: uses 2 actuators ()!

## Slide 19: Checking Controllability
rank(R) = 3 (i.e. full rank)
So system is controllable: but uses only 1 actuator ()!
Tip: Given matrices use Matlab command to find controllability Gramian.
Tip: Use to find rank of

## Slide 20: Observability
Very rarely are all system states visible to the external world
  E.g. model may have internal physical states such as temperature, pressure, object velocity: that may not be measurable by an external observer
  Only things made available by a sensor are visible to the real world
Observability:
  Can we reconstruct an arbitrary internal state of the system if we have only the system outputs available?
  Important question that affects which sensors we pick for the system

## Slide 21: Checking Observability
Find observability matrix
[ is the state-dimension]
System is observable if has full row rank. (i.e. rows are linearly independent)
Example:

## Slide 22: Checking Observability
Matrix is full rank
Pair is observable
Assuming sensors measure independently, we need three sensors
Assuming we have sensors to measure , another to measure , the system uses two sensors

## Slide 23: Checking Observability
What if we used only one sensor that measures sum of all states?
I.e.
Observability matrix is not full rank! Cannot reconstruct some state using only one sensor!
Tip: use matlab command to find

## Slide 24: How do we reconstruct internal state?
For linear systems (with no noise), this is done with the use of state estimators or observers
For linear systems with noisy measurements and possible “process noise” in the system itself we use Kalman filter: introduced later in the course
The most popular control method in the world started without any concerns of controllability, observability etc.
Purpose: Tracking a given reference signal

## Slide 25: Reference Tracking
“Follow a line” or “Get system to the reference value”
Plant
Controller
+
-
Error:

## Slide 26: Simplest controller: On/Off
Plant
+
-
Error:
Too much energy wasted jostling the system to and fro

## Slide 27: P controller (with control input saturation)
Plant
+
-
Error:

## Slide 28: Ignoring saturation: P-only controller
Proportional term :
  Make feedback correction proportional to error
If is small, error can be large! [undercompensation]
If is large: system may oscillate (i.e. unstable) or not converge fast enough [overcompensation]
Control error
  We can never have (either requires to be or )
  Known as the DC error or steady state error
: reference input where the steady state error is zero

## Slide 29: PI controller
Idea: Adjust to automatically become
Remember that
becomes zero only when
Drawback: For small integral gains, the response can be very slow

## Slide 30: PID-controller
Compute error signal
Idea: Speed up PI-controller by looking ahead or predicting the future

## Slide 31: PID controller
P part acts on the current error
I part acts on the past error
D part acts on the future or predicted error

## Slide 32: PID controllers
Architecture:
Controller
Plant

## Slide 33: Measuring control performance
Typical to excite closed-loop system with a “step input”
  I.e. sudden change in reference set-point
“Step” input of (say) 2.5 at time 0
Step Response in blue
  Peak/Overshoot (corr. undershoot)
  Settling Time/Settling Region
  Rise Time
  Peak Time
  Steady State Error
Image © from Mathworks

## Slide 34: PID controller in practice
Many heuristics to tune PID controllers, i.e., find values of
Several recipes to tune, usually rely on designer expertise
E.g. Ziegler-Nichols method: increase till system starts oscillating with period (say till ), then set
Matlab/Simulink has PID controller blocks + PID auto-tuning capabilities
Work well with linear systems or for small perturbations,
For non-linear systems use “gain-scheduling”
  (i.e. using different gains in different operating regimes)

## Slide 35: PID characteristics
Effect on Response by increasing | Rise Time | Overshoot | Settling Time | Steady State Error
 | Decreases | Increases | Small Change | Decreases
 | Decreases | Increases | Increases | Decreases
 | Small Change | Decreases | Decreases | No change
Effect on Response by increasing | Rise Time | Overshoot | Settling Time | Steady State Error
 | Decreases | Increases | Small Change | Decreases
 | Decreases | Increases | Increases | Decreases
 | Small Change | Decreases | Decreases | No change

## Slide 36
Nonlinear Control

## Slide 37: Feedback Linearization
Main idea: Try to choose control such the nonlinear system becomes linear
Equations of motion for inverted pendulum:
Control Input: Torque
Rewriting, with :

## Slide 38: Feedback linearization continued
To make our life easier, let , and let , then we get:
Let’s define a new control input such that, )
Voila!
This is a linear system, with which we can stabilize by finding such that has eigenvalues with negative real parts.

## Slide 39: Input Transformation
This operation is called input transformation, which leads to exact cancellation of a nonlinearity, giving rise to a linear equation
Also known as exact feedback linearization or dynamic inversion
Note that this is NOT the same as computing the Jacobian of the nonlinear system and trying to stabilize the resulting linear system at the origin (this would make the system stable only locally)
We are using feedback to linearize the system
Unfortunately, we cannot always do this

## Slide 40: State Transformation
Consider system:
How do we cancel out?
We can first change variables by a nonlinear transformation:
Now, , and

## Slide 41: State transformation continued
Equations rewritten:
Now we can pick
Rewriting in terms of ’s:
This gives us a linear system, which we can again stabilize using linear system methods

## Slide 42: Form of the controller: two “loops”
Plant
Linearization Loop
Feedback Loop
State Transformation
Input
Transformation
Pole
Placement
Controller

## Slide 43: More feedback linearization
What if we only some states are observable? Requires another form of feedback linearization called input to output linearization
If we use previous substitutions, then
  ( is not linear!)
But, we can use . Now,
  (but, oops, is now unobservable)

## Slide 44: Input-to-output linearization
Differentiate output till input appears in the RHS of output expression
Relative degree: number of times above step needs to be done
  Example:
  Differentiate both sides w.r.t. :
  Relative degree =2
Use nonlinear cancellation to make linear in new variable
Relative degree , means states are not observable
Zero dynamics: dynamics of unobservable states
  If zero dynamics is unstable, that’s bad news, can’t use feedback linearization
All the math will require a lecture by itself, so we will skip the details

## Slide 45: Model Predictive Control
Main idea: Use a dynamical model of the plant (inside the controller) to predict the plant’s future evolution, and optimize the control signal over possible futures
Plant
Model-based Optimizer
Sensor readings

## Slide 46: Receding Horizon Philosophy
Create difference equation: ;
At time t, solve an optimal control problem over next N steps:
,
Only apply optimal control input value at time
At time : get new measurements, repeat optimization

## Slide 47: Receding Horizon or MPC
Image from: https://tinyurl.com/yaej43x5

## Slide 48: Rule-based or Fuzzy Control
Based on the idea of fuzzy sets (1965, inventor: Lotfi Zadeh)
Typical notion of set membership: or
Fuzzy logic: element membership in a set is a number between and
Fuzzy operations on sets:

## Slide 49: Design of a Fuzzy Controller
Fuzzy logic acknowledges and exploits tolerance for uncertainty and imprecision
Three Steps of Fuzzy Control:
  Inputs are mapped to fuzzy sets
  Fuzzy inference consists of a number of fuzzy rules
  Final output obtained through defuzzification
Map to Fuzzy Sets
Fuzzy Rules IF A AND B THEN L * *
Defuzzification

## Slide 50: Fuzzing inputs
0.1
0.8
W = [0, 0, 0.1, 0.8, 0]
Membership functions for sets
Maps input to

## Slide 51: Fuzzy inference
Fuzzy rules:
  If is or is then
  If is and is then
Capture the effect of the fuzzy membership on the output
Get fuzzy output by adding all cases or taking the maximum
Final step is to convert fuzzy output to an actual control value
Several methods, most popular: use centroid

## Slide 52
Observer design

## Slide 53: What is state estimation and why is it needed?
Plant
Given a “black box” component, we can try to use a linear or nonlinear system to model it (maybe based on physics, or data-driven)
Model may posit that the plant has internal states, but we typically have access only to the outputs of the model (whatever we can measure using a sensor)
May need internal states to implement controller: how do we estimate them?
State estimation: Problem of determining internal states of the plant

## Slide 54: Deterministic vs. Noisy case
Typically sensor measurements are noisy (manufacturing imperfections, environment uncertainty, errors introduced in signal processing, etc.)
In the absence of noise, the model is deterministic: for the same input you always get the same output
  Can use a simpler form of state estimator called an observer (e.g. a Luenberger observer)
In the presence of noise, we use a state estimator, such as a Kalman Filter
Kalman Filter is one of the most fundamental algorithm that you will see in autonomous systems, robotics, computer graphics, …

## Slide 55: Random variables and statistics refresher
For random variable , : expected value of , also known as mean
Suppose : then : variance of , is
For random variables and , : covariance of and
For random vector , is a vector
For random vectors, and , cross-covariance matrix is matrix:
: is a normally distributed variable with mean and variance

## Slide 56: Data fusion example
Using radar and a camera to estimate the distance to the lead car:
  Measurement is never free of noise
  Actual distance:
  Measurement with radar: ( is radar noise)
  With camera: ( is camera noise)
  How do you combine the two estimates?
Use a weighted average of the two estimates, prioritize more likely measurement
  , where
Observe: uncertainty reduced, and mean is closer to measurement with lower uncertainty

## Slide 57: Multi-variate sensor fusion
Instead of estimating one quantity, we want to estimate quantities, then:
Actual value is some vector
Measurement noise for sensor is , where is the mean vector, and is the covariance matrix
is the information matrix
For the two-sensor case:
  , and

## Slide 58: Motion makes things interesting
What if we have one sensor and making repeated measurements of a moving object?
Measurement differences are not all because of sensor noise, some of it is because of object motion
Kalman filter is a tool that can include a motion model (or in general a dynamical model) to account for changes in internal state of the system
Combines idea of prediction using the system dynamics with correction using weighted average (Bayesian inference)

## Slide 59: Stochastic Difference Equation Models
We assume that the plant (whose state we are trying to estimate) is a stochastic discrete dynamical process with the following dynamics:
(Process Model)
(Measurement Model)
, | State at time ,
 | Input at time
 | Random vector representing noise in the plant,
 | Random vector representing sensor noise,
 | Output at time
 | Number of states
 | Number of inputs
 | Number of outputs
 | matrix
 | matrix
 | matrix
 | Number of states
 | Number of inputs
 | Number of outputs

## Slide 60: Step I: Prediction
We assume an estimate of at time , fusing information obtained by measurements till time : this is denoted
We also assume that the error between the estimate and the actual has 0 mean, and covariance
Now, we use these values and the state dynamics to predict the value of
Because we are still using measurements only up to time , we can denote this predicted value as , and compute it as follows:

## Slide 61: Step I: Prediction continued
We also need to update the predicted covariance between the predicted value and the “actual” value of
Thus, the a priori estimated state and error covariance are:

## Slide 62: Step II: Correction
This is where we basically do data fusion between new measurement and old prediction to obtain new estimate
Note that data fusion is not straightforward like before because we don’t really observe/measure directly, but we get measurement , for an observable output!
Idea remains similar: Do a weighted average of the prediction and new information
We integrate new information by using the difference between the predicted output and the observation

## Slide 63: Step II: Correction continued
Predicted output: , and error in predicted output =
We denote this expression as the innovation
Covariance of innovation () can be shown to be
Then to do data fusion, we use a matrix known as (optimal) Kalman gain
Where, is given by
Finally, the updated error covariance estimate is given by:

## Slide 64: Correction step summary
Innovation | 
Innovation Covariance | 
Optimal Kalman Gain | 
A posteriori state estimate | 
A posteriori error covariance estimate | 
Innovation | 
Innovation Covariance | 
Optimal Kalman Gain | 
A posteriori state estimate | 
A posteriori error covariance estimate | 

## Slide 65: What are all these equations? How to make sense?
Let’s take a simple one-dimensional example, with perfect observability (i.e. ). So, at each step, is the measurement.
Then, Kalman filter prediction equations become:
  ;
Also, the correction equations become:
  Innovation: , Innovation variance =
  Optimal gain: ,
  Updated state estimate:
  I.e. updated state estimate: (Weighted average!)

## Slide 66: Extended Kalman Filter
We skipped derivations of equations of the Kalman filter, but a fundamental property assumed is that the process model and measurement model are both linear.
Under linear models and Gaussian process/measurement noise, a Kalman filter is an optimal state estimator (minimizes mean square error between estimate and actual state)
In an EKF, state transitions and observations need not be linear functions of the state, but can be any differentiable functions
I.e., the process and measurement models are as follows:

## Slide 67: EKF updates
Functions and can be used directly to compute state-prediction, and predicted measurement, but cannot be directly used to update covariances
So, we instead use the Jacobian of the dynamics at the predicted state
This linearizes the non-linear dynamics around the current estimate
Prediction updates:

## Slide 68: EKF updates continued
Correction updates
Innovation | )
Innovation Covariance | 
Near-Optimal Kalman Gain | 
A posteriori state estimate | 
A posteriori error covariance estimate | 
Innovation | 
Innovation Covariance | 
Near-Optimal Kalman Gain | 
A posteriori state estimate | 
A posteriori error covariance estimate | 

## Slide 69: EKF drawbacks
EKF is not in general an optimal estimator
If initial state estimate is wrong filter may diverge quickly : estimates will no longer agree with reality/observations
Estimated covariance matrix tends to underestimate true covariance
Yet, EKF remains widely used! GPS, most navigation systems, Openpilot (for drones), Pixhawk (mobile robots), etc.
EKF in practice requires lot of “expert tuning of parameters”
  Most parameters occur in process models, covariance matrices, gains etc.
EKF improvement: Unscented Kalman Filter

## Slide 70: End of First Part of the Course
Models of Computation
  Synchronous, Asynchronous Models
  Timed models and Dynamical System Models
  Hybrid Models
Basics of Linear and Nonlinear Control, Observer Design

## Slide 71: Bibliography
https://www.control.lth.se/fileadmin/control/Education/EngineeringProgram/FRTF05_China/L1_updated_20181105.pdf
https://www.lehigh.edu/~eus204/teaching/ME450_NSC/lectures/lecture06.pdf
https://en.wikipedia.org/wiki/Feedback_linearization
https://en.wikipedia.org/wiki/Kalman_filter