## Slide 1: Autonomous Cyber-Physical Systems: Requirements, Linear Temporal Logic
Fall 2020. CS 513.
Instructor: Jyo Deshmukh

## Slide 2: Where we are in the course
Done with Macro-Module 1!
Module 1: Models of Computation + Control
Module 2: Formal Specification, Verification, Testing

## Slide 3: Module 2 : Formal Specification, Verification, Testing
Formal Requirements/Specifications
Requirements-based Testing
Safety Verification

## Slide 4: Requirements
Requirements: describe desirable properties of system behaviors
High assurance/safety-critical, or mission-critical systems must use formal requirements
Behavioral requirements: requirement can be evaluated on individual system behaviors
Requirements met by system if all behaviors satisfy requirements
There needs to be a clear separation between requirements (what needs to be implemented) and the design (how should it be implemented)
Unfortunately, this is not often obeyed

## Slide 5: Rigor in Requirements
Informal requirements: implicit or stated in natural language
  If an obstacle is sensed by the car, it should stop if it is safe to do so
Formal requirements: explicit and mathematically precise
  If the vision system, with a probability labels an object meters from the car as a stationary obstacle, then as long as the current velocity of the car is less than , the vehicle should execute an emergency stop maneuver within ms. Here, the maximum braking deceleration that the car can produce at velocity is , and is a safe stopping distance between vehicles

## Slide 6: Granularity
Granularity of requirements
  System-level: UAV is able to maintain a given desired altitude in presence of acceptable disturbances.
  Subsystem-level: Upon receiving a ‘turn right’ command, flight control subsystem (FCS) produces the correct actuator commands that cause the UAV to turn right.
  Function-level: For the position controller module, the maximum error between the estimated position and the position setpoint is less than 5%.
  Hardware/Timing-level: The MPC algorithm for attitude control has a worst-case execution time of 4 ms.

## Slide 7: Types of Requirements
Hard Requirements: Violation leads to endangering safety-criticality or mission-criticality
  Safety Requirements: system never does something bad
  Liveness Requirements: from any point of time, system eventually does something good
Soft Requirements: Violations lead to inefficiency, but are not critical
  (Absolute) Performance Requirements: system performance is not worse than a certain level
  (Average) Performance Requirements: average system performance is at a certain level

## Slide 8: Nonfunctional/non-behavioral requirements
Security Requirements: system should protect against modifications in its behavior by an adversarial actor
  Failure to satisfy security requirements may lead to a hard requirement violation
Privacy Requirements: the data revealed by the system to the external world should not leak sensitive information
These requirements will become increasingly important for autonomous CPS, especially as IoT technologies and smart transportation initiatives are deployed!

## Slide 9: Requirement Formalisms
Languages and Logics to describe requirements in a mathematically precise fashion
Examples:
  Automata, State Machines
  Propositional Logic, Temporal Logic, Regular Expressions
  Structured language/grammar-based requirements

## Slide 10: Detour to automata and formal languages
Most programmers have used regular expressions
Formally, regular expressions specify acceptable sequences of finite length
Example:
  [a-z][a-z 0-9] : strings starting with a lowercase letter (a-z) followed by one lowercase letter or number
  [a-z][0-9]*[a-z] : strings starting with a lowercase letter, followed by finitely many numbers followed by a lowercase letter

## Slide 11: Finite state automata
Famous equivalence between finite state automata and regular expressions
a-z
a-z,0-9
[a-z][a-z 0-9 ]
a-z
a-z
0-9
[a-z][0-9]*[a-z]
State
Accepting
state
*
0-9

## Slide 12: How does a finite state automaton work?
Starts at the initial state
In , if it receives a letter in a-z, goes to
  else, it goes to
In , if it receives a number in 0-9, it stays in
else, it goes to (as it received a-z)
In , no matter what it gets, it stays in
is an accepting state where computation halts
Any string that takes the machine from to is accepted by the machine
a-z
a-z
0-9
*
0-9

## Slide 13: Language of a finite state automaton
What strings are accepted by ?
  ab, zy, s2r, q123s, u3123123v, etc.
What strings are not accepted by ?
  2b, 334a, etc.
The set of all strings accepted by is called its language
The language of a finite state automaton consists of strings, each of which can be arbitrarily long, but finite
a-z
a-z
0-9
*
0-9

## Slide 14: Propositional Logic
Simplest form of logic with a set of atomic propositions and Boolean connectives
, Connectives =
Syntax recursively gives how new formulae are constructed from smaller formulae
Syntax of Propositional Logic |  |  | 
 |  | ¦ | the true formula
 |  | ¦ | is a prop in AP
 |  | ¦ | Negation
 |  | ¦ | Conjunction
 |  | ¦ | Disjunction
 |  | ¦ | Implication
 |  | ¦ | Equivalence
Syntax of Propositional Logic |  |  | 
 |  | ¦ | the true formula
 |  | ¦ | 
 |  | ¦ | Negation
 |  | ¦ | Conjunction
 |  | ¦ | Disjunction
 |  | ¦ | Implication
 |  | ¦ | Equivalence

## Slide 15: Semantics
Semantics (i.e. meaning) of a formula can be defined recursively
Semantics of an atomic proposition defined by a valuation function
Valuation function assigns each proposition a value 1 (true) or 0 (false), always assigns the formula the value 1, and for other formulae is defined recursively
Semantics of Prop. Logic | 
 | 1
 | 1 if 0 if
 | 1 if = 1 and , 0 otherwise
Semantics of Prop. Logic | 
 | 1

## Slide 16: Examples
: There is an upright bicycle in the middle of the road
: There is car in the field of vision
: If there is an upright bicycle in the middle of the road, the bicycle has a rider
Car is in the intersection

## Slide 17: Interpreting a formula of prop. logic
. What is
= 1
. What is
= 0
Is this true? = 1? (For all valuations)?

## Slide 18: Temporal Logic
Temporal Logic (literally logic of time) allows us to specify finite and infinite sequences of states using logical formulae
An -language is a set of sequences, each of which is possibly infinite in length, temporal logics help specify many interesting classes of -languages
Temporal logic grew out of philosophy: tense logic and modal logic
Amir Pnueli in 1977 used a form of temporal logic called LTL for requirements of reactive systems: later selected for the 1996 Turing Award
LTL is now adopted by the industry (part of Property Spec. Language, which is an IEEE standard), is supported by many tools in the EDA/CAD industry

## Slide 19: Temporal Logic = Prop. Logic + Temporal Operators
Propositional Logic is interpreted over valuations to atoms
Temporal Logic is interpreted over traces/sequences/strings
Trace is an infinite sequence of valuations
0
1
2
3
4
42
Can also write as: (0,1,1), (1,1,0), (2,0,0), (3,1,1),(4,0,1),… ,(42,1,1), …

## Slide 20: Linear Temporal Logic
LTL is a logic interpreted over infinite traces
Temporal logic with a view that time evolves in a linear fashion
  Other logics where time is branching!
Assumes that a trace is a discrete-time trace, with equal time intervals
Actual interval between time-points does not matter : similar to rounds in synchronous reactive components
LTL can be used to express safety and liveness properties!

## Slide 21: LTL Syntax
LTL formulas are built from propositions and other smaller LTL formulas using:
  Boolean connectives
  Temporal Operators
Only shown and , but can define for convenience
Syntax of LTL |  |  | 
 |  | ¦ | is a prop in AP
 |  | ¦ | Negation
 |  | ¦ | Conjunction
 |  | ¦ | NeXt Step
 |  | ¦ | Some Future Step
 |  | ¦ | Globally in all steps
 |  | ¦ | In all steps Until in some step
Syntax of LTL |  |  | 
 |  | ¦ | 
 |  | ¦ | Negation
 |  | ¦ | Conjunction
 |  | ¦ | NeXt Step
 |  | ¦ | Some Future Step
 |  | ¦ | Globally in all steps
 |  | ¦ | In all steps Until in some step

## Slide 22: LTL Semantics
Semantics of LTL is defined by a valuation function that assigns to each proposition at each time-point in the trace a truth value (0 or 1)
We use the symbol (read models) to show that a trace-point satisfies a formula
: Read as trace at time satisfies formula
If we omit , then the meaning is time 0. I.e. is the same as
Semantics is defined recursively over the formula
Base case: Propositional formulas, Recursion over structure of formula

## Slide 23: Recursive semantics of LTL: I
if ,
  i.e. if is true at time
if ⊭ ,
  i.e. if is not true for the trace starting time
if and
  i.e. if and both hold starting time
if
  i.e. if holds starting at the next time point

## Slide 24: Recursive semantics of LTL: II
if such that
  i.e. is true starting now, or there is some future time-point from where is true
if :
  i.e. is true starting now, and for all future time-points , is true starting at
if s.t. and s.t. ,
  i.e. eventually holds, and for all positions till holds, holds

## Slide 25: Visualizing the temporal operators
: NeXt Step
0
1
2
3
4
42
: Some Future step
0
1
2
3
4
42
0
1
2
3
4
42

## Slide 26: Visualizing the temporal operators
: Globally holds
0
1
2
3
4
42
: holds Until holds
0
1
2
3
4
42

## Slide 27: You can nest operators!
What does mean?
  Trace satisfies (at time 0) if at time 1, holds. I.e. holds at some point strictly in the future
0
1
2
3
4
42
What does mean?
  Trace satisfies (at time 0) if at , there is always a in the future
0
1
2
14
15
65

## Slide 28: More operator fun
What does mean?
10
11
12
13
14
42
0
What does mean?
0
1
2
14
15
65
54

## Slide 29: More, more operator fun
What does the following formula mean: ?
0
1
2
3
4
5
Is this true? is the same as ?
0
1
2
3
4
42
No! Because this trace satisfies , but not

## Slide 30: Operator duality and identities

## Slide 31: Example specifications
Suppose you are designing a robot that has to do a number of missions
Kitchen
Bedroom
Living Room
Bathroom
Study
Whenever the robot visits the kitchen, it should visit the bedroom after.
Robot should never go to the bathroom
The robot should keep working until its battery becomes low
The robot should repeatedly visit the living room
Whenever the TV is on and the living room has no person in it, then within three steps, the robot should turn off the TV
TV
Passage

## Slide 32: Example specifications in LTL
Suppose you are designing a robot that has to do a number of missions
Kitchen
Bedroom
Living Room
Bathroom
Study
Whenever the robot visits the kitchen, it should visit the bedroom after.
Robot should never go to the bathroom.
The robot should keep working until its battery becomes low
TV
Passage

## Slide 33: Example specifications in LTL
Suppose you are designing a robot that has to do a number of missions
Kitchen
Bedroom
Living Room
Bathroom
Study
The robot should repeatedly visit the living room
Whenever the TV is on and the living room has no person in it, then within three steps, the robot should turn off the TV
room occupied by a person
TV
Passage