## Slide 1: Autonomous Cyber-Physical Systems: Basics of Verification
Spring 2018. CS 599.
Instructor: Jyo Deshmukh
Acknowledgment: Some of the material in these slides is based on the lecture slides for CIS 540: Principles of Embedded Computation taught by Rajeev Alur at the University of Pennsylvania. http://www.seas.upenn.edu/~cis540/

## Slide 2: Where we are in the course
Done with Module 1!
Module 1: How you can create virtual models for your autonomous CPS designs
  Models for Software: Synchronous Components, Asynchronous and Timed Processes
  Models for Physical systems and Environment: Dynamical Systems, Probabilistic Models
  CPS Models: Hybrid Processes/Systems, Closed-loop control for linear and nonlinear systems, Stability Analysis, State Estimation
Module 2: What you can do with these virtual CPS models that you now know how to construct

## Slide 3: Module 2 : Analyzing closed-loop models
Basics of Verification
Formal Requirements/Specifications
Requirements-based Testing
Some Formal Verification Techniques

## Slide 4: Requirements
Sounds like a boring topic about documentation, is anything but that!
A requirement describes a desirable property of the system behaviors.
High assurance/safety-critical, or mission-critical systems should use formal requirements.
A system design meets its requirements if all system executions satisfy all the requirements.
There should ideally be clear separation between requirements (what needs to be implemented) and the design (how should it be implemented).
Unfortunately, this simple philosophy is often not followed by designers.

## Slide 5: Rigor in Requirements
Requirements can be informal: Either implicit or stated in natural language
  If an obstacle is sensed by the car, it should stop if it is safe to do so
Formal requirements are stated explicitly in a mathematically precise fashion
  If the vision system, with a probability labels an object meters from the car as a stationary obstacle, then as long as the current velocity of the car is less than , the vehicle should execute an emergency stop maneuver within ms. Here, the maximum braking deceleration that the car can produce at velocity is , and is a safe stopping distance between vehicles.

## Slide 6: Granularity
Granularity of requirements
  System-level: UAV is able to maintain a given desired altitude in presence of acceptable disturbances.
  Subsystem-level: Upon receiving a ‘turn right’ command, flight control subsystem (FCS) produces the correct actuator commands that cause the UAV to turn right.
  Function-level: For the position controller module, the maximum error between the estimated position and the position setpoint is less than 5%.
  Hardware/Timing-level: The MPC algorithm for attitude control has a worst-case execution time of 4 ms.

## Slide 7: Types of Requirements
Hard Requirements: Violation leads to endangering safety-criticality or mission-criticality
  Safety Requirements: system never does something bad
  Liveness Requirements: from any point of time, system eventually does something good
Soft Requirements: Violations lead to inefficiency, but are not critical
  (Absolute) Performance Requirements: system performance is not worst than a certain level
  (Average) Performance Requirements: average system performance is at a certain level

## Slide 8: Other kind of requirements
Security Requirements: system should protect against modifications in its behavior by an adversarial actor
  Failure to satisfy security requirements may lead to a hard requirement violation
Privacy Requirements: the data revealed by the system to the external world should not leak sensitive information
These requirements will become increasingly important for autonomous CPS, especially as IoT technologies and smart transportation initiatives are deployed!

## Slide 9: Safety Requirements
A safety requirement states that a system always stays within the set of good states (i.e. nothing bad every happens)
Examples:
  Collision avoidance: the distance between a car and a pedestrian is always greater than a threshold
  Patient’s blood glucose never drops below 80 mg/dL
  Maximum temperature specification on the battery is not exceeded
Safety requirements can be formalized using transition systems

## Slide 10: Transition System
Transition System is a tuple
  : Set of State Variables over finite or infinite domains
  : Function mapping to initial values
  : Transition description giving code to update variables in
Semantics:
  Each combination of values assigned to state variables can be interpreted as a state. : set of all possible states (could be an infinite set)
  : Finite or infinite set of initial states which is a subset of
  : Finite or infinite set of transitions, which is a subset of
Values to input variables are chosen nondeterministically
  Why? This is an abstraction technique (i.e. making something less concrete)
  We are interested in making sure that no matter what input value, the TS has desirable behavior

## Slide 11: Transition Systems and state
All kinds of components (synchronous, asynchronous, timed, hybrid, continuous components have an underlying transition system
Caution: the word “state” can be confusing, as it is overloaded
  State is used to represent modes in an ESM
  State in the transition system underlying a component captures any given runtime configuration of the component
  If a synchronous component has finite input/output types and a finite number of “states” in its ESM, then it has a finite-state transition system
  Continuous components, Timed Processes, Hybrid Processes in general, have infinite number of states

## Slide 12: Example of a TS
: { mode, x }
Semantics:
: { mode off, x 0 }
has an infinite number of transitions
  (off, 0) (off, 0)
  (off, 0) (on, 0)
  (on, n) (on, n+1) if n < 10
  (on, n) (off, 0) otherwise
off
on
(press==0)?
(press==1)?
(press==0) & (x<10) ?
0
(press==1) or (x10) ?

## Slide 13: Example transitions for TS
(off,0)
(on,0)
(on,1)
(on,2)
(on,100)
(off,42)
off
on
(press==0)?
(press==1)?
(press==0) & (x<10) ?
0
(press==1) or (x10) ?
(on,42)

## Slide 14: TS describes all possible transitions
(off,0)
(on,0)
(on,1)
(on,2)
(on,100)
(off,42)
off
on
(press==0)?
(press==1)?
(press==0) & (x<10) ?
0
(press==1) or (x10) ?
(on,42)
Transitions indicated as dotted lines can’t really happen in the component
But, the TS will describe then, as the states of the TS are over!

## Slide 15: Reachable states of a modified switch TS
off
on
(press==0)?
(press==1)?
(press==0) & (x<2) ?
0
(press==1) or (x 2) ?
(off,0)
(on,0)
(on,1)
(on,2)
(on,100)
(off,42)
(on,42)
Reachable states and transitions

## Slide 16: Reachability
A state of a transition system is reachable if there is an execution starting in some initial state that ends in .
Algorithm to compute reachable states from a given set of initial states (just BFS):
Procedure ComputeReach(TS)
  , k:=1;
  While
  Temp :=
  ForEach
  If () Temp := Temp
  EndForEach
  Temp,
  EndWhile
  Return
  EndProcedure

## Slide 17: Desirable behaviors of a TS
Desirable behavior of a TS:
  Defined in terms of acceptable (finite or infinite) sequences of states
  If all unacceptable sequences of a TS are finite in length, then the property encoding acceptable behavior is called a safety property
Safety property can be specified by partitioning the states into a safe/unsafe set
  , ,
  Any finite sequence that ends in a state is a witness to undesirable behavior, or if all (infinite) sequences starting from an initial state never include a state from , then the TS is safe.
  In other words, to get a proof of safety, do reachability computation, and if ComputeReach(TS) = , then the TS is safe

## Slide 18: Safety invariants
An invariant is a Boolean expression over the state variables of a TS
A property is called an invariant of TS if every reachable state of TS satisfies
An invariant is a safety invariant if
Examples of invariants for modified switch:
Examples of non-invariants:
Suppose, , and
  Then, we can verify that is a safety invariant for modified switch: proof towards the end
off
on
(press==0)?
(press==1)?
(press==0) & (x<2) ?
0
(press==1) or (x 2) ?

## Slide 19: Proving that something is an invariant
Given TS and a property , prove that all reachable states of TS satisfy
Recall ComputeReach(TS), it actually gives an inductive definition of reachable states
  All states specified by are reachable using 0 transitions
  If a state is reachable using transitions, and is a transition in , then is reachable using transitions
  Reachable = Reachable using transitions for some

## Slide 20: Inductive Safety Proof
Given TS and a property , prove that all reachable states of TS satisfy
Base case: Show that all initial states satisfy
Inductive case: assume state satisfies , then show that if , then must also satisfy
off
on
(press==0)?
(press==1)?
(press==0) & (x<2) ?
0
(press==1) or (x 2) ?

## Slide 21: Inductive Invariant
A property is an inductive invariant of a transition system TS if
  Every initial state satisfies
  If any state satisfies , and , then satisfies
By definition, if is an inductive invariant, then all reachable states of TS satisfy , and hence it is also an invariant

## Slide 22: Proving inductive invariants: I
Consider transition system TS given by
  :
  : if then (else remains unchanged)
Is an inductive invariant?
Base case: is zero, so is trivially satisfied
Inductive case:
  Pick an arbitrary state (i.e. arbitrary value for state variable ), say
  Now assume satisfies , i.e.
  Consider the transition, there are two cases:
    If , then after the transition, and
    If , then , which is .
  In either case, after the update
  So is an inductive invariant, and the proof is complete

## Slide 23: Proving inductive invariants: II
Consider transition system TS given by
  : ,
  : if then (else remain unchanged)
Is an inductive invariant?
Base case: Initial state is (), so is trivially satisfied
Inductive case:
  Pick an arbitrary state (i.e. arbitrary value for state variable ), say
  Now assume satisfies , i.e.
  Consider the transition if then
    What if )? Clearly, does not satisfy !
  So is not an inductive invariant for TS, and the proof fails

## Slide 24: Proving inductive invariants: III
Consider transition system TS given by
  : ,
  : if then (else remain unchanged)
Is an inductive invariant?
Base case: Initial state is (), so is trivially satisfied
Inductive case:
  Pick an arbitrary state (i.e. arbitrary value for state variable ), say
  Now assume satisfies , i.e. and
  Consider the transition if then , else
  Now, if , because , , and thus . Thus, is satisfied
  The else case is trivially satisfied
  So in either case, holds
So, is an inductive invariant!

## Slide 25: How do we prove safety invariants?
To establish that is an invariant of TS:
Find another property such that
  (i.e. every state satisfying must satisfy )
  is an inductive invariant
    Show initial states satisfy
    Assume an arbitrary state satisfies , consider any state such that , then prove that satisfies
This is a sound and complete strategy for establishing safety invariants

## Slide 26: Soundness and Completeness
Formal system: a set of axioms, a grammar for specifying well-formed formulas, and a set of inference rules for deriving new true formulas from axioms
Sound: Starting from the axioms and using inference rules of the formal system, we cannot arrive at a formula that is equivalent in meaning to false.
Complete: Proof system is complete with respect to a property if every formula having that property can be derived using the inference rules
Proof rule for proving invariants is sound and complete:
  Sound: It is a correct proof technique
  Complete: If is an invariant, there is some stronger inductive invariant satisfying inductive conditions that we can find

## Slide 27: Safety Proof for Switch
Let’s try the inductive invariant:
off
on
(press==0)?
(press==1)?
(press==0) & (x<2) ?
0
(press==1) or (x 2) ?
Base case: trivially satisfies
Inductive hypothesis: assume that a state satisfies
Inductive step: prove that any s.t. satisfies
  Case I:
    = [trivial]
    = [satisfies second conjunct in ]
  Case II:
    if , this implies that , so satisfies
    otherwise, this again implies that satisfies
So is an inductive invariant
Further, (note that every state satisfying will satisfy )
So is an invariant of the TS!

## Slide 28: Next time
Wrap-up of verification basics
Temporal Logic