## Slide 1: Autonomous Cyber-Physical Systems: Intro to Models of Computation Synchronous & Asynchronous Process Models
Fall 2024. CSCI 513.
Instructor: Jyo Deshmukh
Acknowledgment: Some of the material in these slides is based on the lecture slides for CIS 540: Principles of Embedded Computation taught by Rajeev Alur at the University of Pennsylvania. http://www.seas.upenn.edu/~cis540/

## Slide 2: Model-based Development (MBD) or design
[1] Nicolescu, Gabriela; Mosterman, Pieter J., eds. (2010). Model-Based Design for Embedded Systems. Computational Analysis, Synthesis, and Design of Dynamic Systems. 1. Boca Raton: CRC Press.
Most popular paradigm for principled software development in CPS
We will learn various aspects of MBD through this course
MBD when used for designing embedded software1 has 4 main steps
  Model the physical components/environment (also known as a plant model)
  Analyze the plant, and synthesize/design the control-software at a high-level
  Co-Simulate the plant and control-software for testing/analysis
  Automatically generate code from the control-software model for deployment
Popular MBD frameworks such as Simulink®, LabView™, RationalRose, DyMola, TargetLink, Scade, Python etc.

## Slide 3: Models of Computation: Functional
Classical model of computation: Programs as Functions
  Start from a given input,
  Produce a certain output and then terminate
  Desired functionality can be described by a mathematical function
  Emphasis is on data computation
  Canonical model: Turing machines e.g. compute square-root, encrypt some text, etc.

## Slide 4: Models of Computation: Reactive/Interactive
Interactive Programs:
  Interact with the user in their own time, i.e., react to user’s commands, but with no real-time constraints
  Emphasis is on user-interaction; e.g., web browsers, word processors, etc.
Reactive Programs:
  Continuously interact with the environment at a rate decided by the environment
  Emphasis is on system-environment interaction; e.g., aircraft autopilot, mail-servers, etc.

## Slide 5: Models of Computation: Timing
What’s the notion of time in the model?
  Real-time or Logical time-steps of execution?
What time do different components in the model use?
  Single global clock for full synchronization?
  Different clocks in each component?
What level of granularity do we need in time?
  Discrete time-steps or Continuous dense time?

## Slide 6: Interpreting models
We know how to interpret imperative/functional programs
How do we interpret models? What are their execution semantics?

## Slide 7
Most convenient model of computation for an Autonomous CPS is a
reactive and concurrent model of computation.
An autonomous CPS can be viewed as a network of components that communicate
either synchronously or asynchronously.

## Slide 8: Models of Computation
Synchronous Model of Computation
Asynchronous Model of Computation
Timed Models
  Like Asynchronous models, but with explicit time information
  Can make use of global time for coordination
Continuous-time models/Dynamical system models
  Like Synchronous, but time evolves continuously
Hybrid Dynamical Models

## Slide 9: Models of Computation: this lecture
[1] Nicolescu, Gabriela; Mosterman, Pieter J., eds. (2010). Model-Based Design for Embedded Systems. Computational Analysis, Synthesis, and Design of Dynamic Systems. 1. Boca Raton: CRC Press.
Synchronous Model of Computation
Asynchronous Model of Computation
Timed Model
  Like Asynchronous models, but with explicit time information
  Can make use of global time for coordination
Continuous-time models/Dynamical system models
  Like Synchronous, but time evolves continuously
Hybrid Dynamical Models

## Slide 10
Synchronous Models

## Slide 11: Synchronous Models
All components execute in a sequence of rounds in lock-step
Example:
  Components in a digital hardware circuit with a central global clock
  Fixed-step Simulation Models of Discrete Components in Simulink

## Slide 12: Simple Representation of a Synchronous Component
Input Names and Types
State Variables Declaration and initialization
Output Names and Types
Component
Update action that happens in each round

## Slide 13: Simplest synchronous component: delay
(Boolean = {0, 1})
Input variable: in of type Boolean
Output variable: out of type Boolean
State variable: x of type Boolean, initialized to 0
In each round, component updates output from the state and state from input
bool in
bool out
bool x := 0
out:=x ; x:= in

## Slide 14: Execution of “Delay”
Initialize state to 0
Repeatedly execute rounds
In each round:
  Choose value for input (provided from environment, e.g., by user)
  Execute update code
bool in
bool out
bool x := 0
out:=x ; x:= in
1 / 0
1
1 / 1
1
0 / 1
0
0 / 0
0
1 / 0
1
0

## Slide 15: Synchrony hypothesis
Time needed to execute update is negligible compared to arrival times between consecutive inputs
Synchronous execution is a logical abstraction
  Execution time of update code is 0
  Production of outputs, updates to state and arrival of inputs happen instantaneously
With multiple components, assume all execute synchronously and simultaneously
Design-time burden: validate synchrony hypothesis

## Slide 16: Formalization of synchronous comp.
Synch. comp. is a tuple: , where:
Symbol | Designation | Examples
 | Set of Inputs | {
 | Set of State Variables | 
 | Set of Outputs | 
 | Set of Updates | 
Symbol | Designation | Examples
 | Set of Inputs | 
 | Set of State Variables | 
 | Set of Outputs | 
 | Set of Updates | 
Input Names and Types
State Variables Declaration and initialization
Output Names and Types
Component
Update action that happens in each round

## Slide 17: Semantics of updates & initialization
Let the set of input, output, and state values be
Semantics of the initialization function:
  At time/round 0, maps the state variables to some specified value (or values) in
Semantics of the update function (some sequence of conditionals and assignments):
  Set of transitions where each transition is of the form: , where is the old value of the state variables, is the new value of the state variables, is the value of the input in that round, and is the value of the output
  is a subset of

## Slide 18: What are the for these components?
bool in
bool out
bool x := 0
out:=x ; x:= in
bool in
int out
int y:= 0
bool z:= 0
out:=y ;
if (z==0)
y:= y + 1
else
y:= y-1
z := in
Notes: int = {int_min,..,-1,0,1,..int_max}
Q_I = {0, 1}, Q_O = {0, 1}, Q_X = {0,1}
Q_I = {0,1}, Q_X = int x {0,1}, Q_O = int

## Slide 19: Transitions for Delay
bool in
bool out
bool x := 0
out:=x ; x:= in

## Slide 20: Composition of Synchronous Components
bool in1
bool out1
bool x1 := 0
out1:=x1 ; x1:= in1
bool in2
bool out2
bool x2 := 1
out2:=x2 ; x2:= in2
Delay sequentially composed with Delay

## Slide 21: Composition of Synchronous Components
bool in1
bool out1
bool x1 := 1
out1:=x1 ; x1:= in1
bool in2
bool out2
bool x2 := 0
out2:=x2 ; x2:= in2
1 / 1
1
0 / 1
0
0 / 0
0
1 / 0
1
1 / 1
1
1
1 / 0
1
1 / 1
1
0 / 1
0
0 / 0
0
1 / 0
1
0
Delay 1
Delay 2
Observe:
in2 is the same as out1 in every round
Ignoring first 2 rounds, outputs of d2 are the inputs to d1 delayed by 2 rounds

## Slide 22: What does this model achieve?
bool in
int out
int y:= 0
out:=y ;
if (in==0)
y:= y + 1
else
y:= y-1
int c
bool warn := 0
bool warn
10101010
11111111
10001111
001100
if (c 2)
if (warn == 1)
error := 1;
else
warn := 1;
end
end
bool error
bool error := 0

## Slide 23: What does this model achieve?
bool in
int out
int y:= 0
out:=y ;
if (in==0)
y:= y + 1
else
y:= y-1
int c
bool warn := 0
if (c 2)
if (warn == 1)
error := 1;
else
warn := 1;
end
end
bool warn
If number of ‘0’ inputs seen by the first component exceeds the number of ‘1’ inputs it has seen by 2, at any point in its execution, then the ‘warn’ light becomes high
If this happens again, the ‘error’ light becomes high
bool error
bool error := 0

## Slide 24: Determinism
A synchronous component is deterministic if:
  It has a single initial state
  Updates ensure that for every state and input , there is a unique state and output such that is a transition
Determinism means for same input sequence you get same state/output sequence every single time
Note:
  Nondeterminism is useful for modeling uncertainty/unknown
  It is not the same as probabilistic/random choice!

## Slide 25: Extended State Machines
Commonly used to describe behavior of synchronous models
Does this ESM remind you of something?
0
1
(in==0)?
0
(in==1)?
0
(in==1)?
1
(in==0)?
1

## Slide 26: Anatomy of an ESM
Commonly used to describe behavior of MBD models
From state
Guard Condition?
Assignment
To state
Initial state

## Slide 27: Component Switch: What does this do?
bool press
bool out
int x := 0
bool q := 0
switch (q)
case 0: if (press==1) q:= 1
case 1: if (press==0) & (x < 10)
q:=1; x:= x+1
elseif (press==1) or ( x >= 10)
q:=0; x:= 0; out:= 1
end
end

## Slide 28: ESM corresponding to Switch SRC
Off
(q==0)
on
(q==1)
(press==0)?
(press==1)?
(press==0) & (x<10) ?
0
(press==1) | (x10) ?
; out:=1
q = 0 : off
= 1 : on

## Slide 29: ESM notation
Implicit mode : discrete state variable over some finite enumeration. Here: {1, 0}
Transitions correspond to mode-switch
Each mode-switch has guard/update. Example:
  Guard: (press==0) & (x<10) and
  Update: x:= x+1
off
on
(press==0)?
(press==1)?
(press==0) & (x<10) ?
0
(press==1) | (x10) ?
; out := 1

## Slide 30: ESM execution
Start in mode off; initial state = (off,0)
Sample executions:
off
on
(press==0)?
(press==1)?
(press==0) & (x<10) ?
0
(press==1) or (x10) ?

## Slide 31: ESM transitions could be nondeterministic!
off
on
(press==0)?
(press==1)?
(press==0) & (x10) ?
0
(press==1) or (x10) ?

## Slide 32: Finite-state Components
bool in
bool out
bool x := 0
out:=x ; x:= in
bool in
int out
int y:= 0
bool z:= 0
out:=y ;
if (z==0)
y:= y + 1
else
y:= y-1
z := in
Component is finite state if all variables are over finite types
FS
Not FS!

## Slide 33: Cruise Controller Example
CruiseController
event second
event cruise
event inc
event dec
Clock
Sensor
event rotate
Display
nat speed
event(nat) cruiseSpeed
ThrottleController
event(real) F
Driver Inputs

## Slide 34: Sensors
Rotation Sensor: Wheel speed sensor or vehicle speed sensor
Type of a tachometer
Counts number of rotations per second and as the wheel radius is known, can compute the linear speed of the car
(From Porter and Chester Institute slides on Google Image Search)

## Slide 35: Actuator
ThrottleController is an actuator that gets a force/torque required to adjust the throttle plate which leads to tracking the desired speed
CruiseController
event second
event cruise
event inc
event dec
Clock
Sensor
event rotate
Display
nat speed
event(nat) cruiseSpeed
ThrottleController
event(real) F

## Slide 36: Decomposing CruiseController further

## Slide 37: MeasureSpeed Component
event rotate
nat speed
nat count := 0, s:=0
if rotate?
count:=count + 1;
if second?
s:= round( K* count);
count:=0;
speed:=s
MeasureSpeed SRC
event second

## Slide 38: Synchronous components: summary
Synchronous dataflow languages used to model synchronous components
  Scade-suite from Esterel Technologies: used in many avionics' applications
Benefit: system design is simpler
Challenge: How do we ensure synchronous execution when components may execute on different hardware?

## Slide 39
Asynchronous Components

## Slide 40: Asynchrony
Synchrony: All components execute in a sequence of rounds in lock-step
Asynchrony: No lock-step computation!
Natural model for networked, distributed communicating components executing independently and at possibly different speeds
As there is no central, global clock, explicit coordination is required between components
Examples:
  Processes in distributed computation, multiple threads in any modern OS
  Interrupt-driven processing

## Slide 41: Asynchronous Component Example
bool in
bool out
x:=
Tin x := in
= bool
Tout
x { out := x;
x := }
Tasks: Tin,Tout
Guarded Update

## Slide 42: Asynchronous Reactive Component
Input channel in of type bool
Output channel out of type bool
State variable x of type bool+. The value indicates empty or null.
x initialized to
Input task Tin reads input value into x
Output task Tout produces output if x is not empty
bool
out
bool in
x:=
Tin x := in
Tout
x { out := x;
x := }

## Slide 43: Asynchronous Reactive Component Execution
Execution Model: In each step only one task is executed
Task can be executed only if it is enabled (i.e. if its guard condition is true)
If multiple guard conditions are true, one task is nondeterministically executed
Sample execution:
bool in
x:=
Tin x := in
Tout
x { out := x;
x := }
bool
out
Buffer

## Slide 44: Example: Asynchrony + Nondeterminism
ARC may have no inputs or outputs, just internal tasks
  Update may have no guards
In each step, execute Tx or Ty
Sample execution:
Interleaved model of concurrency
int x:= 0, y≔ 0
Tx x := x+1
Ty y:= y+1
(0,0)
(1,0)
(0,1)
(2,0)
(1,1)
(0,2)
(1,2)

## Slide 45: Asynchronous Process/Reactive Component
Set of input channels: I
  ESM representation: in?v, where v is the value to be received
Set of output channels: O
  ESM representation: out!v, where v is the value to be written
Set of state variables X
Initialization Init which maps state variables to initial values
bool in
x:=
Tin x := in
Tout
x { out := x;
x := }
bool
out

## Slide 46: Updates are different from Synchronous Comps.
Input Task defines updates of the form: G x:= E(X,in)
Guard condition G: some expression over only state variables X; input task can be executed only if G is true
For each in in I, we associate a read-set (X {in}): variables that can appear in expression E for input task associated with in (rationale: can read value on in only if that task is enabled)
Any state variable can appear in the LHS of the assignment
Defines a set of input actions of the form: q q’
  where q is value of state variables before update, and q satisfies G
  value of state variables after update is q’ = E(Xq, inv)

## Slide 47: Updates are different
Output Task: defines updates of the form: G out := E(X)
Guard condition G: some expression over only variables in X; output task can be executed only if G is true
For each out in O, we associate a write-set {out}: variables that appear on LHS of the assignment
Any expression containing only state variables can appear in E
Defines an output action of the form qq’
  where q is value of state variables before update, and q satisfies G
  value of state variables after update is q’
  value v is output on channel out

## Slide 48: Updates are different
Internal Task: defines updates of the form: G x := E(X)
Guard condition G: some expression over only variables in X; internal task can be executed only if G is true
Any expression containing only state variables can appear in E, only state variables appear on LHS
Defines an internal action of the form qq’
  where q is value of state variables before update, and q satisfies G
  value of state variables after update is q’
  No input is read or output is produced!

## Slide 49: Asynchronous Merge: Sequence of Actions
bool in1
queue(bool) x1 , x2
Tin1 Full(x1) Enqueue(x1,in1)
bool in2
Tin2 Full(x2) Enqueue(x2,in2)
Tout1 Empty(x1) out := Dequeue(x1)
bool out
Tout2 Empty(x2) out := Dequeue(x2)
(
(<1>,)
(<1>,<0>)
(<1>,<0,1>)
(<1>,<1>)
in1?1
in2?0
in2?1
out!0
out!1
Tin1
Tin2
Tin2
Tout2
Tout2
Asynchronous Processes can also be represented with extended state machines

## Slide 50: Composing Asynchronous Processes
Parallel composition: Inputs, Outputs, States and Initialization similar to the synchronous case
Input consumption needs to be synchronized with output production for the ‘temp’ variable
bool in
x1 :=
Tin1 x1 := in
Tout1
x1 { temp := x1;
x := }
Buffer
x2:=
Tin2 x2 := temp
Tout2
x2 { out := x2;
x2 := }
Buffer
bool out
bool temp

## Slide 51: Composed DoubleBuffer
Defining P1 || P2
In each step only 1 task executes
If y is an output channel of P1 and input channel of P2:
A1: output task for P1 with code: G1 U1
A2: input task for P2 with code: G2 U2
Composition has output task for y with code: G1 G2 U1;U2
bool in
x1 :=
Tin1 x1 := in
Tout1
x1 { temp := x1;
x := }
Buffer
x2:=
Tin2 x2 := temp
Tout2
x2 { out := x2;
x2 := }
Buffer
bool out
bool in
x1 := , x2 :=
Tin1 x1 := in
Tout2 x2 { out:=x2; x2 ≔}
Double
Buffer
bool out
Tout1in2 x1 { local bool temp;
temp:=x1; x1 ≔;x2:=temp}

## Slide 52: Blocking vs. Non-blocking Synchronization
int x := 0
Ttmpe (x is even)
x:= tmp
P2
int y := 0
Tout tmp := y;
y:= y+1
P1
int tmp
Task Tout of P1 can produce a value on the output only if P2 has an input task that is enabled to consume the value with some input task
In this example, once x becomes odd, P2 cannot consume (no enabled input task) and it blocks communication
Process is non-blocking on channel in if at least one guarded update corresponding to input task for in is enabled
Process is non-blocking if for every input channel, the disjunction of all guards corresponding to input tasks for that channel is valid or the Boolean formula 1 (true).
How do you make P2 non-blocking?
Ttmpo (x is odd)
x:=tmp

## Slide 53: Deadlocks
Common error in asynchronous designs
Caused by each process waiting for another process to execute a task, but no task is enabled
P1
bool y1 := 0, z1 := 0
T11: (y1==0)y1:= 1;
T12: (y1==1) z1 := r2
T13: (z1==1) r1 := 1
r1
r2
(
(0,0)
(1,),
(0,0)
(1,0),
(1,0)
T11
T21
bool y2 := 0, z2 := 0
T21: (y2==0)y2:= 1;
T22: (y2==1) z2 := r1
T23: (z2==1) r2 := 1
P2

## Slide 54: Wrapping it all up
Synchronous components/processes:
  Good abstraction if you have a common shared clock at which each component in your software executes
Asynchronous components/processes
  Good abstraction if you have interrupts, user-driven actions
Next time:
  Continuous-time models