## Slide 1: Will future cars have formally verified powertrain control software?
Jyotirmoy V. Deshmukh
(with Jim Kapinski, Xiaoqing Jin, Isaac Ito & Ken Butts)

## Slide 2: What is a Powertrain?
© http://www.greencarcongress.com/2014/11/20141118-mirai.html
© Google Image search
© Motor Trend. Tundra powertrain
Main components in delivering power
Automotive context: engine and transmission
This talk: engine, fuel cell stack, engine + electric motor, etc.

## Slide 3: What is Powertrain Control Software
Real-time Control Algorithms
  Examples: Air/Fuel Ratio Control, Idle Speed Control, Exhaust-gas recirculation, boost control, Electronic throttle control, battery management systems, etc.
On-board Diagnostic Algorithms
  Fuel and air metering, emissions controls, misfire indication, telematics, fleet tracking, etc.

## Slide 4: What do we mean by formally verified?
?
Safety
Low exhaust gas emissions
Good Fuel Efficiency
Drivability
Comfort
© Google Image search
© Google Image search

## Slide 5: Overview
Automotive industry
  Trends in Powertrain Control
Model-based Development: Verification & Validation
Promising Techniques
  Some success stories
Challenge Problems

## Slide 6: Automotive Sector
?
 Automotive Industry Trends  MBD Verification  Techniques  Challenges

## Slide 7: Exciting things on the horizon, but safety first!
© http://www.toyota-global.com
 Automotive Industry Trends  MBD Verification  Techniques  Challenges

## Slide 8: Exciting things on the horizon
Smart Mobility: Last mile transit
Intelligent Transportation Systems
  V2V and V2X communication
Alternate fuels and power sources
IHS automotive forecasts revenue from services:
  $500B vehicle maintenance
  $5B service subscriptions
  $50B ads in cars!
http://toyota-global.com
http://www.forbes.com/sites/joannmuller/2013/06/26/connected-cars-10-tough-problems-automakers-must-solve/
 Automotive Industry Trends  MBD Verification  Techniques  Challenges

## Slide 9: Lots of opportunities for CPS majors
Distributed systems: V2V, V2X protocols, Connected cars, Coordination
Big Data/Machine Learning: Learning driver preferences, traffic patterns, automobile health & maintenance, energy usage
Online optimization
Privacy/Security
Programming Languages, architectures and models for the Internet of Things
 Automotive Industry Trends  MBD Verification  Techniques  Challenges

## Slide 10: Who’s driving the innovations?
Govt. Environmental Agencies
Energy Economics
Tech Companies & Social Media
Consumer
 Automotive Industry Trends  MBD Verification  Techniques  Challenges

## Slide 11: Are IC Engine cars a solved problem?
US Energy Information Administration Report: Motor gasoline remains dominant fuel through 20401
EPA estimates 4% of 2014 MY cars meet 2025 CO2 targets2
Off these, most are HVs, EVs, PHVs
HVs, EVs, PHVs are generally more expensive!
[1] www.eia.gov/forecasts/AEO/
[2] http://www.epa.gov/oms/fetrends.htm
“Since the MY 2025 standards are over a decade away, there’s considerable time for continued improvements in gasoline vehicle technology.” – EPA report, 2014.
 Automotive Industry Trends  MBD Verification  Techniques  Challenges
NO!

## Slide 12
Macroscopic Background
GDP per capita
(PPP)
Population
(in millions)
Global: 7,000+
Car ownership
(per 1000 people)
China
India
US
Japan
Number of cars
(in millions)
Global: 1,016
1,347
(#1)
1,210
(#2)
314
(#3)
127
(#10)
239
(#1)
75
(#3)
78
(#2)
58
17
590
8,387
3,663
48,328
34,748
JAMA 2010
Year 2011, 2012
20
(#13)
IMF, 2011 Int$
760
Population, Economy & Car Ownership
 Automotive Industry Trends  MBD Verification  Techniques  Challenges
Emerging countries have a large potential to grow in car ownership
Populations in emerging countries may not be able to afford HVs, PHVs, EVs, smarter cars

## Slide 13: Up and coming PT technologies
Timeline | Strategies
2015 | Boosting and Downsizing: Turbocharging, Supercharging, Stop & Start technology, Low speed Torque enhancements
2025 | High efficiency combustion: Lean Stratified Spark Ignition, Low temperature combustion, Combined turbo/super charging
2050 | Plug-in/Hybrid, Fuel cell electric will dominate, Advanced thermodynamic cycles will be investigated
Mark Kuhn, “Automotive Powertrain Technologies through 2016 and 2025,” University of Michigan Transportation and Research Institute Conference, 2012
 Automotive Industry Trends  MBD Verification  Techniques  Challenges

## Slide 14: As we increase features …
70 to 100 ECUs in modern luxury cars, close to 100M LOC
Engine control: 1.7M LOC
  F-22 raptor: 1.7M, Boeing 787: 6.5M
Frost & Sullivan: 200M to 300M LOC
Electronics & Software: 35-40% of luxury car cost
Charette, R., “This Car Runs on Code”, IEEE spectrum, http://spectrum.ieee.org/transportation/systems/this-car-runs-on-code
1977: first GM car with embedded software
1981: GM: 50K LOC for entire US fleet
 Automotive Industry Trends  MBD Verification  Challenges

## Slide 15: Where does increasing software complexity come from?
 Automotive Industry Trends  MBD Verification  Techniques  Challenges
[1] http://www.epa.gov/oms/fetrends.htm
Many new and current powertrain technologies growing in market share1!

## Slide 16: Automotive platforms: coming to a car near you!
Examples
  VW: Modular transverse matrix (MQB)
  Toyota: TNGA Modular platform
  Renault-Nissan: Common Module Family
Purpose: share design, engineering (including software) and production efforts
Need components to understand common interfaces
The future: Lego-like Cars?
 Automotive Industry Trends  MBD Verification  Techniques  Challenges

## Slide 17
MBD Verification and Validation
 Automotive Industry Trends  MBD Verification  Techniques  Challenges

## Slide 18: MBD process
Controller Specification Model
Auto-Code Generation
Integrated
code
Prototype
Design
Prototype modeling and
implementation
System
evaluation
Requirement
New design
Legacy Code
Lots and lots of testing, now by driving!
Lots and lots of testing
Requirements and Design co-developed
Feasibility study / requirement analysis
Dev.
target
Verify this!
X-In-the-Loop-Simulators
Model-based testing
 Automotive Industry Trends  MBD Verification  Techniques  Challenges

## Slide 19: Example: Cold Start Control of Gas Engine
Example Target: Reduce Hydro-Carbon emissions during startup by 5%
Idea: Activate catalyst converter as fast as possible
Control Design: Use throttle, fuel injection and spark timing to reach target
Controller
Water temp.
Crank Angle
AFR sensor
Sensor inputs
Throttle
Angle
Fuel
Injection
Spark Timing
HC
Catalyst
Modification
Throttle
Fuel inj.
Spark
Standard spec
Throttle
Fuel inj.
Spark
Coding
Implement
Evaluate!
Experimental engine system
Next iteration
Related components
Standardize, if successful
 Automotive Industry Trends  MBD Verification  Techniques  Challenges

## Slide 20: Model-based Development
Plant Model
  Model behavior of physical components
  Data-driven or physics-based (first principles)
  E.g. mean-value engine model, turbocharger model, electronic throttle, etc.
  Tools: SimScape, MapleSIM, AMESim, DyMola, Modelica-based tools
Plant Modeling challenges
  Tradeoff between complexity and fidelity
  Need to validate models against data
  No standard architecture, very domain-specific
 Automotive Industry Trends  MBD Verification  Techniques  Challenges

## Slide 21: Model-based Development
Controller Model
  Block-diagram-based models
  Executable representation
  Hierarchical, Real-time software specifications
  Automatic Code Generation
  Tools: Simulink, NI LabView, Scilab/SciCos, Ptolemy
Challenges
  Granularity?
    Scheduler + entire ECU, Application-level, Feature-level?
  How close to hardware?
    Interrupts, Shared Memory?
 Automotive Industry Trends  MBD Verification  Techniques  Challenges

## Slide 22: MBD V&V
10s
1m
1hr
1s
Tested
time horizon
System
Domain
Feature
Module
Software scale
SiL
MiL
Hardware scale
ECU
Vehicle
Program
Hardware Unit
Unit test
HiL
Test cell
Vehicle
Hybrid Systems Research applicable & Our Focus
 Automotive Industry Trends  MBD Verification  Techniques  Challenges

## Slide 23: V&V in the industry: both tools and practice
Mostly focused on “verifying” the controller
  By that, I mean “verifying” the generated C code
  By that, I mean testing the generated C code
Code coverage metrics, test-case generation
Some formal methods being marketed by tool vendors
  Static analysis: Dead code detection, Divide by zero
  Property Proving
But, what about the closed-loop system?
What about 20+ years of HSCC, ACC, CDC, CAV, EMSOFT,… papers?
 Automotive Industry Trends  MBD Verification  Techniques  Challenges

## Slide 24: Past experience in Toyota: I
System
Domain
(Engine)
Feature
Module
Lessons Learned:
Requirements keep evolving
More time spent validating functional interference with legacy software than validating the function itself
Reachability analysis of hybrid systems
Modeling language
(SysML, VDM, …)
 Automotive Industry Trends  MBD Verification  Techniques  Challenges

## Slide 25: Past Experience in Toyota: II
System
Engine
Feature
Module
Lessons Learned:
Deriving module-level requirements is time-consuming
Things are not usually wrong at the module-level
No engine stall!
?
Less physical meaning
 Automotive Industry Trends  MBD Verification  Techniques  Challenges

## Slide 26: Small concrete problem1: A/F control to reduce emissions
Catalytic converters reduce HC, CO2, and NOx emissions
Conversion efficiency optimal at stoichiometric value
 Automotive Industry Trends  MBD Verification  Techniques  Challenges
[1] X. Jin. J. Kapinski. J. Deshmukh, K. Ueda, K. Butts, Powertrain Control Verification Benchmark, HSCC 2014

## Slide 27: Gasoline Engine
Intake manifold
Exhaust manifold
Measured Air Flow
Measured A/F
Fuel injectors
AIR
 Automotive Industry Trends  MBD Verification  Techniques  Challenges

## Slide 28: Dynamical phenomena
Fuel puddling or Port wetting
Fuel commanded
Fuel puddle
“wets” the wall
Exhaust entry
O2 sensor measures
A/F ratio
Transport Delay
Actual fuel aspirated into combustion chamber
Exhaust Gas Variable Transport Delay
 Automotive Industry Trends  MBD Verification  Techniques  Challenges

## Slide 29: The plant model
Delay Differential Equation
 Automotive Industry Trends  MBD Verification  Techniques  Challenges

## Slide 30: Controller Hybrid Automaton
startup
sensor failure
normal
power
No Feedback Control
Only feedforward estimator
Feedback Control
+ Feedforward estimator
Startup Time
 Automotive Industry Trends  MBD Verification  Techniques  Challenges

## Slide 31: Challenge: Verify these Temporal Logic Requirements
Normalized A/F Ratio
Normal Mode Requirements | 
 | A/F ratio always within 5% after initial startup time
 | After every rising or falling edge of pulse input, signal settles within seconds, and remains settled till the next edge
 | RMS error is less than 0.05
 | Maximum overshoot is 0.05
Normal Mode Requirements | 
 | A/F ratio always within 5% after initial startup time
 | RMS error is less than 0.05
 | Maximum overshoot is 0.05
Existing formal verification techniques struggle
Some early results with C2E21
 Automotive Industry Trends  MBD Verification  Techniques  Challenges
[1] C. Fan, PS. Duggirala, S. Mitra, M. Viswanathan, Progress on Powertrain Verification Challenge with C2E2, ARCH 2015, Best Talk Award

## Slide 32: A really real example
Diesel Air Path model + Model Predictive Controller
Developed by Toyota MBD + University of Michigan
Strongly nonlinear 8th order model
Gain scheduled controller with
  Actuator inversion
  Selective constraint enforcement
 Automotive Industry Trends  MBD Verification  Techniques  Challenges

## Slide 33: MBD: Opportunities & Challenges
Engine Hardware/Control Software Co-design
  Can we design control software for potential variations in engine hardware components?
Virtual Calibration
  Is plant model accurate enough?
Early bug-detection
  Is plant model rich enough to find bugs in closed-loop system?
Machine-checkable Requirements
  Who will write them?
 Automotive Industry Trends  MBD Verification  Techniques  Challenges

## Slide 34
Scaling and Industrializing MBD V&V:
A case for simulation-guided formal analysis
 Automotive Industry Trends  MBD Verification  Techniques  Challenges

## Slide 35: Spectrum of Analysis Techniques
Can apply to real designs? (scalability)
How formal/exhaustive?
Linear Analysis (symbolic)
Test Vector Generation for Model Coverage
Simulation
Linear Analysis (numerical)
Concolic
Testing
Theorem
Proving
(Bounded) Model Checking
Stability
Proofs
Reachability
Analysis
The One Tool to Rule Them All
Unexplored Frontier
Program Analysis
Formal Verification
Software Testing
Control Theory Techniques
 Automotive Industry Trends  MBD Verification  Techniques  Challenges

## Slide 36: Why simulations?
Help design validation
Provide visual feedback
Can use existing design artifacts
Can uncover bugs
Simulations are cheap and usually fast
Do not require knowledge of:
  Temporal Logic, SAT modulo theories, Bounded Model Checking, Undecidability, Hybrid Automata, ….
Test-suites can be shared and built up across models
 Automotive Industry Trends  MBD Verification  Techniques  Challenges
Control Designers already use them a lot
What we learned: If you want engineers to pay attention, speak to them in a language they understand!

## Slide 37: Simulation-guided Analysis: not a new idea
Concolic Testing
  [K. Sen, G. Agha. CUTE and jCUTE: Concolic unit testing and explicit path model-checking tools, CAV 2006]
  [A. Kanade, R. Alur, F. Ivančić, S. Ramesh, S. Sankaranarayanan, K.C. Shashidhar, Generating and analyzing symbolic traces of Simulink/Stateflow models, CAV 2009]
Proofs from tests
  [A. Gupta, R. Majumdar, and A. Rybalchenko. From tests to proofs. STTT 2013]
SciDuction
  [S. A. Seshia, Sciduction: Combining induction, deduction, and structure for verification and synthesis, DAC 2012]
….
 Automotive Industry Trends  MBD Verification  Techniques  Challenges

## Slide 38: A Few Promising Techniques
Requirement Falsification
Mining Requirements
Simulation-guided Dynamical Analysis
Simulation-guided Reachability Analysis
Conformance Testing
Monitoring
 Automotive Industry Trends  MBD Verification  Techniques  Challenges

## Slide 39: Requirement Falsification
Given model ; property
Find input and initial conditions s.t.
does not satisfy
Not verification, but systematic bug-finding
No guarantees of completeness (except asymptotic/ probabilistic)
 Automotive Industry Trends  MBD Verification  Techniques  Challenges

## Slide 40: Some key enablers
Robust satisfaction1,2 of by simulation trace
Function mapping and to
Positive number = satisfies
Negative number = does not satisfy
Moving towards zero = moving towards violation
 Automotive Industry Trends  MBD Verification  Techniques  Challenges
[1] G. Fainekos, and G. J. Pappas. Robustness of temporal logic specifications for continuous-time signals. Theoretical Computer Science 2009.
[2] A. Donzé, and O. Maler. Robust satisfaction of temporal logic over real-valued signals. FORMATS 2010

## Slide 41: Falsification by optimization
Optimizer:
Minimize robust satisfaction value
\

\
 Automotive Industry Trends  MBD Verification  Techniques  Challenges
Black-box Global optimizers
Powerful heuristics to get close to global optimum

## Slide 42: Requirement Falsification
S-TaLiRo [Fainekos, Sankaranarayanan, et al., TACAS ’11, HSCC ’10, ACC ‘12]
Metric Temporal Logic based requirements
Supports several stochastic optimizers
Breach [Donzé, CAV ‘10, NSV ‘13]
Signal Temporal Logic based requirements
Supports Nelder-Mead
Can exploit sensitivity info
RRT-REX [Dreossi, Donzé, Dang + Toyota MBD, NFM ‘15]
RRT-based optimal search
Blends maximizing coverage and minimizing robust satisfaction value
All three tools can work with real Toyota models
Are able to find rare bugs
Our Vice President and President (for TTC) have seen demos of S-TaLiRo!
 Automotive Industry Trends  MBD Verification  Techniques  Challenges

## Slide 43: Requirements in an Industrial Setting
Formal methods/verification engineers love them
Control designers write them in Word documents
  (in Japanese and/or German)
Control designers (and occasionally temporal logic pundits) have a hard time writing them
Continue to evolve, are outputs of the design process rather than inputs to the design process
 Automotive Industry Trends  MBD Verification  Techniques  Challenges

## Slide 44: Mining Requirements
How do control designers check correctness?
What do you do when your chief engineer leaves?
Formal techniques need machine-checkable requirements
Key Idea: Identify Temporal Logic Patterns from Simulation Data!
Req: Settle in the red-band
 Automotive Industry Trends  MBD Verification  Techniques  Challenges

## Slide 45: Mining Temporal Logic
Given: Model
Designer intent translated to parameterized templates
Learn parameter values from simulation traces
Falsifier to invalidate learnt requirement
Use counterexamples to refine
Given: Data
Supervised Learning: labeled data
Unsupervised learning: unlabeled data
Detect anomalies
 Automotive Industry Trends  MBD Verification  Techniques  Challenges
  Yang, Hoxha, Fainekos, ICTSS 2012
  Jin, Donzé, Deshmukh, Seshia, HSCC 2013
  Kong, Jones, Ayala, Gol, Belta, HSCC 2014
  Jones, Kong, Belta, CDC 2014

## Slide 46: Simulation-guided Dynamical Analysis
Infer from simulation data1,2,3,4
  Lyapunov functions
  Contraction Metrics
Learn barrier certificates to prove system safety
Estimate region of attraction
Prove using nonlinear solvers such as dReal5
[1] U. Topcu, P. Seiler, A. Packard, Local stability analysis using simulations and sum-of-squares programming, Automatica, 2008
[2] J. Kapinski, J. Deshmukh, Discovering Forward Invariant Sets for Nonlinear Dynamical Systems , AMMCS 2013
[3] J. Kapinski, J. Deshmukh, S. Sankaranarayanan, N. Aréchiga, Simulation-guided Lyapunov Analysis for Hybrid Dynamical Systems, HSCC 2014
[4] A. Balkan, J. Deshmukh, J. Kapinski, P. Tabuada, Simulation-guided Contraction Analysis ICC 2015
[5] S.Gao, S. Kong, E. Clarke, dReal: An SMT Solver for Nonlinear Theories of the Reals, CADE 2013
 Automotive Industry Trends  MBD Verification  Techniques  Challenges

## Slide 47: Dynamical Analysis in practice
Can find barrier certificates using only simulations!
  < 24 mins to compute barrier
  dReal proved correctness of barrier in < 20 mins
 Automotive Industry Trends  MBD Verification  Techniques  Challenges

## Slide 48: Simulation-guided Reachability
Unsafe
Initial
Simulation Trace up to time T
Reach-Tube up to time T
Cover infinite set of initial states by regions centered at finite number of initial states
Get reach-tubes by bloating each simulation trace appropriately
Check if any reach-tube intersects the unsafe set
Refine if necessary
 Automotive Industry Trends  MBD Verification  Techniques  Challenges

## Slide 49: How to bloat?
Approximate bisimulation
  [G. Zheng and A. Girard, Bounded and unbounded safety verification using bisimulation metrics, HSCC 2009]
  [F. Lerda, J.Kapinski, E. Clarke, B.Krogh, Verification of Supervisory Control Software Using State Proximity and Merging, HSCC 2008]
Sensitivity analysis
  [A. Donzé, O. Maler, Systematic Simulation using Sensitivity Analysis, HSCC 2007]
C2E2: global and local discrepancy functions
  [P. S. Duggirala, S. Mitra, M. Vishwanathan, Verification of annotated models from executions, EMSOFT 2013]
  [C. Fan, S. Mitra, Bounded Verification with On-the-Fly Discrepancy Computation, Tech Report 2015]
 Automotive Industry Trends  MBD Verification  Techniques  Challenges
A/F
time

## Slide 50: Conformance Testing
Is behavior of models and “similar”?
Multiple Distance metrics in theory
  Skorokhod metric
  Kossentini-Caspi metric
    [C. Kossentini, P. Caspi, Approximation ,Sampling and Voting in Hybrid Computing Systems]
  Metric by R. Goebel, R. Sanfelice and A. Teel
    [R. Goebel, R. Sanfelice and A. Teel , Hybrid Dynamical Systems, Princeton University Press]
  -closeness metric
    [H. Abbas, H. Mittleman, G. Fainekos, Formal property verification in a conformance testing framework, MEMOCODE 2014]
  -approximate bisimulation relations
    [A. Girard, G. Pappas, Approximation metrics for discrete and continuous systems, IEEE Trans. On Automatic Control, 2007]
 Automotive Industry Trends  MBD Verification  Techniques  Challenges

## Slide 51: Key enablers
Efficient algorithms to compute distance metrics
  H. Abbas, Mittlemann, Fainekos, Formal Property Verification in a Conformance Testing Framework, MEMOCODE 2014
  R. Majumdar, V. Prabhu, Computing the Skorokhod Distance between Polygonal Traces, HSCC 2015 – Talk tomorrow!
Simulation & optimization-guided conformance testing
Model 1
Model 2
Distance Estimator
Cost Function
Output Traces
Pick new input
Optimizer-guided input
Optimizer
 Automotive Industry Trends  MBD Verification  Techniques  Challenges

## Slide 52: Monitoring Temporal Logic Requirements
Large corpus of work for LTL, MTL (for Boolean monitoring)
  [M. Leucker, C. Schallhart, A brief account of runtime verification, Journal of Logic and Algebraic Programming, 2007]
Boolean monitoring
  Good to detect when things have gone wrong
  Ideally, we want to know before they go wrong
Quantitative Online monitoring: more directional
  [A. Dokhanchi, B. Hoxha, G. Fainekos, On-line monitoring for temporal logic robustness, RV 2014]
  [J. Deshmukh, A. Donzé, S. Ghosh, X. Jin, G. Juniwal, S. A. Seshia, Robust online monitoring for Signal Temporal Logic, DAC WiP 2015]
Code generation: efficient memory foot-print
Possible application: on-board diagnostics?
 Automotive Industry Trends  MBD Verification  Techniques  Challenges

## Slide 53
Here are some grand challenges….
 Automotive Industry Trends  MBD Verification  Techniques  Challenges

## Slide 54: Grand Challenge I: Requirement Engineering
Key challenge for Toyota, Bosch, and others
  [H. Roehm, R. Gmehlich, T. Heinz, J. Oehlerking and M. Woehrle: Industrial Examples of Formal Specifications for Test Case Generation, ARCH 2015]
 Automotive Industry Trends  MBD Verification  Techniques  Challenges

## Slide 55: Grand Challenge I: Requirement Engineering
 Automotive Industry Trends  MBD Verification  Techniques  Challenges
Key challenge for Toyota, Bosch, and others
  How do you present requirements to control designers?
  How do they convey their intention without using formalisms?
  Is Temporal Logic the right requirement language?

## Slide 56: Grand Challenge II: Good enough plant model
MBD needs good plant models
  Models can be created to explain a bug, but can they be used to find a bug?
Can there be a plant model that is a true over-approximation of the real plant?
  Just parameters are not enough
  Entire subsystems describing physical phenomena could be missing
Stochastic models relevant, but not widespread
 Automotive Industry Trends  MBD Verification  Techniques  Challenges

## Slide 57: Grand Challenge III: Compositional Reasoning
Assume-guarantee reasoning
  [Frehse PhD thesis 2005, Rajhans HSCC 2013]
Component-based
  [S. Tripakis and others, UC Berkeley and Aalto Univ.]
Differential Dynamic Logic
  [A. Platzer’s group at CMU]
Stability, Barrier certificates
  [U. Topcu, A. Packard, R. Murray, CDC 2009; C. Sloth, G. Pappas, R. Wisniewski, HSCC 2012]
Trajectory Splicing
  [A. Zutshi, S. Sankaranarayanan, J. Deshmukh, J. Kapinski, CDC 2013, EMSOFT 2014]
 Automotive Industry Trends  MBD Verification  Techniques  Challenges

## Slide 58: Grand Challenge IV: Reachability
Will SpaceEx, Flow*, CORA, C2E2, dReach and others digest industrial-scale models?
  Delay-differential equations?
  Look-up Tables?
  Differential Algebraic Equations?
  Controllers that are essentially C code?
Engineers will continue to use only Simulink models
  Burden of translation is on the HSCC community tool-makers
False positives are a way to rapidly lose engineer interest
 Automotive Industry Trends  MBD Verification  Techniques  Challenges

## Slide 59: Grand Challenge V: Impending invasion of concurrency
Huge push for multi-core and many-core ECUs
Immediate Challenges: Real-time +
  Partitioning/Parallelizing
  Load balancing
  Memory mapping,
  Cross-core reads, overhead?
  Legacy software?
Philosophical challenges
  Concurrency is a known hard problem
  Programming Languages
  Domain-specific Determinism: semantic equivalence vs. predictable run-time
  Control designers rarely know about memory models, parallelization, etc.
 Automotive Industry Trends  MBD Verification  Techniques  Challenges

## Slide 60: A big question: how to leverage for MBD?
Computation power
Cheaper data analysis
Data
Storage
Cyber physical systems theory
?
Plant modeling
& simulator
 Automotive Industry Trends  MBD Verification  Techniques  Challenges

## Slide 61
To conclude …
 Automotive Industry Trends  MBD Verification  Techniques  Challenges

## Slide 62: Conclusions
Will future powertrains be formally verified?
Depends
The glass half full
Hybrid systems community will produce some amazing tools and techniques to handle industrial-size models
The researchers and the practitioners will be able to communicate using a shared language
 Automotive Industry Trends  MBD Verification  Techniques  Challenges

## Slide 63: Conclusions
 Automotive Industry Trends  MBD Verification  Techniques  Challenges
Will future powertrains be formally verified?
Depends
The glass half empty
Growth of powertrain complexity will continue to outpace verification research

## Slide 64: Conclusions
 Automotive Industry Trends  MBD Verification  Techniques  Challenges
Will future powertrains be formally verified?
My view
Brilliance of the HSCC (and the larger CPS) community keeps producing high quality research solutions
Emphasis on tools that work on examples (on many more than our own cherry-picked ones) is critical
Help engineers improve productivity
There won’t be a dearth of problems

## Slide 65: A note of thanks
The hybrid systems community continues to respond to industrial problems and challenges
  This helps us in our jobs!
  Thank you all.
Thanks to our colleagues from Bosch for detailed discussions
Thank you, Sriram and Antoine, for this opportunity
Thank you to the audience for your attention

## Slide 66: Questions? Comments?
http://www.toyota-global.com/innovation/intelligent_transport_systems/mobility/images/its_mobility_02_large.jpg

## Slide 67: Acknowledgments
This presentation is a composite of several previous presentations from fellow team members from Toyota, and I wish to acknowledge them for making their slides and presentations available to me:
  Ken Butts
  Tomoyuki Kaga
  Tomoya Yamaguchi
  Shunsuke Kobuna
  Jim Kapinski
  Xiaoqing Jin
  Hisahiro “Isaac” Ito