## Slide 1: Autonomous Cyber-Physical Systems: Planning and Decision-Making
Fall 2020. CS 513.
Instructor: Jyo Deshmukh

## Slide 2: Decision-making hierarchy
Route Planning
Behavioral Planning
Lane following
Lane changing
Adaptive cruising
Intersection negotiation
Collision avoidance
Trajectory planning/Motion planning
Low-level Feedback control
Road topology, network
Perception layer outputs
Estimated pose and free space
Vehicle state estimates
User-specified
destination
Sequence of way-points
Motion specification
Reference path
Steering and throttle commands

## Slide 3: Route planning
Represent road network/topology as a directed graph
  Nodes represent way-points
  Edges represent a cost of traveling between nodes
Cost can represent time, distance, fuel economy, a weighted combination of some of these, etc.
Simplest solutions based on Dijkstra’s shortest-path or A* search algorithms
  In practice, these do not scale well
  Lots of different algorithms proposed in the literature5

## Slide 4: Dijkstra’s Shortest path algorithm
ShortestPath (Graph G(V, E), src)
  ; ;
A
C
D
E
F
B
3
2
6
6
5
5
1
5
 | A |  | B |  | C |  | D |  | E |  | F |  | Q
1 |  |  |  |  |  |  |  |  |  |  |  |  | 
2 |  |  |  |  | 3 | A | 6 | A | 6 | A |  |  | 
3 |  |  |  |  | 3 | A | 6 | A | 5 | C | 8 | C | 
4 |  |  | 10 | E | 3 | A | 6 | A | 5 | C | 8 | C | 
5 |  |  | 10 | E | 3 | A | 6 | A | 5 | C | 8 | C | 
6 |  |  | 9 | F | 3 | A | 6 | A | 5 | C | 8 | C | 
7 |  |  | 9 | F | 3 | A | 6 | A | 5 | C | 8 | C | 
 | A |  | B |  | C |  | D |  | E |  | F |  | Q
1 |  |  |  |  |  |  |  |  |  |  |  |  | 
2 |  |  |  |  | 3 | A | 6 | A | 6 | A |  |  | 
3 |  |  |  |  | 3 | A | 6 | A | 5 | C | 8 | C | 
4 |  |  | 10 | E | 3 | A | 6 | A | 5 | C | 8 | C | 
5 |  |  | 10 | E | 3 | A | 6 | A | 5 | C | 8 | C | 
6 |  |  | 9 | F | 3 | A | 6 | A | 5 | C | 8 | C | 
7 |  |  | 9 | F | 3 | A | 6 | A | 5 | C | 8 | C | 

## Slide 5: Dijkstra’s shortest path algorithm
Computes for each node, the shortest path from the source to that node
Classic example of a dynamic programming algorithm
Original algorithm runs in
Optimization using Fibonnaci Heaps allows complexity
Does not work for graphs with cycles or negative weights!
  Bellman-Ford algorithm for graphs with negative weights and cycles (but no negative cycles)
  Floyd-Warshall for finding shortest paths between all pairs of nodes

## Slide 6: Behavior planning for autonomous driving
Also known as maneuver planning
Plans high-level driving actions, driving maneuvers
Behavior planner considers static and dynamic obstacles and traffic rules
  Cruise control, Adaptive Cruise Control : road speed, following lead
  Lane switching, merging
  Decelerating to stop, Remaining stopped
Input: HD road map, road network, localization information (where am I?), perception of environment around the vehicle
Output: driving maneuver and constraints for local planner : typically a sequence of discrete actions

## Slide 7: Behavior planning
Some elements of behavior planning:
  Trajectory prediction of moving objects in the environment
  Finite state machine based planning

## Slide 8: Trajectory prediction
Cars, cyclists: a number of models available
  Physics-based models
  Maneuver-based models
  Interaction-aware models
Human motion prediction: much harder, lots of ongoing research

## Slide 9: Physics-based trajectory prediction
Evolution models: dynamic or kinematic
  Dynamic models:
    Use Lagrangian mechanics models (sum of all forces on the vehicle should be zero)
    Usually simplified to be fast enough for trajectory prediction (e.g. 2-wheeled bicycle model)
  Kinematic models:
    Ignore many forces, focus on velocity, direction of vehicle etc.
    E.g. constant velocity, constant acceleration, constant turn rate and velocity, constant turn rate and acceleration models

## Slide 10: Trajectory prediction
Use kinematic or dynamic model and “evolve” it in time:
  usually not reliable because it assumes perfect knowledge of current state
Simulate based on evolution model but add Gaussian noise
Explicitly model uncertainty parameters and do Monte Carlo simulation
(1)
(2)
(3)
Pictures from: https://robomechjournal.springeropen.com/articles/10.1186/s40648-014-0001-z

## Slide 11: Maneuver-based motion models
Represent vehicles as independent maneuvering entities
Two ideas: use prototype trajectories or try to predict driver intention
Prototype trajectories: partition road network into regions, and group trajectories into clusters corresponding to a motion pattern (turn right/go straight etc.); match partial trajectory to cluster
How to match trajectories? Distance metrics: Hausdorff, Longest Common Subsequence (LCS), Quaternion-based LCS, etc.
Use Gaussian Process Regression to represent motion patterns
Maneuver intention estimation and execution: use context and heuristics to determine what maneuvers will be performed (using machine learning techniques)
  Estimation: Neural Nets (Perceptrons), Logistic Regression, Relevance vector machines, HMMs
  Execution: Gaussian Processes, RRTs, stochastic reachability sets
Pictures from: https://robomechjournal.springeropen.com/articles/10.1186/s40648-014-0001-z

## Slide 12: Interaction-aware models
Represent cars as maneuvering entities that interact with each other
Based on Dynamic Bayesian Networks: generalization of HMMs and Kalman Filters
  Value of a variable calculated from internal regressors and immediate prior values
Picture from wikipedia
Pictures from: https://robomechjournal.springeropen.com/articles/10.1186/s40648-014-0001-z

## Slide 13: Collision prediction
Deterministic: Check if ego trajectory will intersect with predicted trajectory (discretize at each time step, or compute analytically)
Probabilistic: Explicitly model uncertainty
Risk indicators for collision
  Time to collision (TTC): time remaining before collision may occur
    used to decide when to apply brakes, to identify which is the least dangerous maneuver
  Time to react: Time available for driver to act before collision is inevitable
    Used to identify latest time at which braking/acceleration/steering etc. can help avoid collision

## Slide 14: Trajectory prediction for pedestrians
Physics-based : Dynamical models of pedestrians
  Single dynamic model or multiple dynamical models
Pattern-based: Learn motion patterns from data
  Sequential methods: Learn conditional models and recursively apply learned transition functions for inference
  Non-sequential methods: Model distribution over full trajectories
Planning-based methods (based on estimating pedestrian’s long-term goals)
Pattern-based methods using recurrent neural networks such as LSTMs are increasingly popular today

## Slide 15: FSM-based planning
Each state in the FSM is a maneuver or “mode”
Decelerate
Track Speed
Distance to stop sign
threshold?
Distance to stop sign
threshold?

## Slide 16: Planning using finite state machines
Model driving contexts and behaviors as finite sets, and use finite state machines to represent possible transitions between contexts
Planning then becomes a problem of choosing appropriate transitions that ensure a desired behavior
Can view this is a 2-player game between the car’s controller (player 1) and the environment (player 2)
Game-theoretic approaches for FSMs can identify winning strategies for the controller

## Slide 17: Behavioral planning under uncertainty
FSM-based view may not adequately address uncertainty
Uncertainty exists in the intention of traffic participants
Intention prediction of cars, bicycles, pedestrians
  Techniques based on Gaussian mixture models
  Switching linear dynamical and stochastic systems
  Gaussian Process Regression
A big new push is probabilistic planning formalisms using Markov Decision Processes such as Partially Observable Markov Decision Processes
We will learn about MDPs/PoMDPs either later today or in the RL lecture

## Slide 18: Motion planning
Behavior plan decides a high-level set of maneuvers (e.g. cruise-in-lane, turn right, turn left, etc.)
This plan needs to be translated into a reference path or a reference trajectory to be followed by the vehicle.
Motion planning computes a feasible reference plan that respects feasibility (according to vehicle dynamics), obstacle avoidance, while optimizing certain costs (e.g. maximizing comfort, minimizing battery usage, etc.)
Popular approaches
  Variational methods from nonlinear optimal control
  Graph-search approaches using discretization of the state-space
  Incremental tree-based methods

## Slide 19: Path planning vs. Trajectory planning
Path planning:
  Simply provides a parametric function
    is the configuration space or state-space of the vehicle
    gives the initial configuration, and gives the final configuration, and for all intermediate , gives the intermediate configurations
  May not include a velocity profile or those for other states, but delegates this to lower-level control
Trajectory planning: Is aware of vehicle dynamics and can account for dynamic obstacles

## Slide 20: Trajectory planning
Defines a parametric function , where
  is the planning horizon, and is the set of configurations
  precisely describes how the vehicle’s behavior evolves in configuration space at each time
Trajectory planning is a more nuanced version of path planning

## Slide 21: Trajectory planning setup
: set of all continuous functions from to
Let , then:
  (where is a set of initial configurations/states)
  (where is a set of goal states)
Set of all allowed states at time denoted as
encodes holonomic constraints
  A constraint is holonomic if you can express it as , where the ’s are coordinates, i.e. constraint depends only on spatial configuration
  Holonomic constraints can encode path constraints, and dynamic and static obstacles

## Slide 22: Trajectory planning setup continued
is a differential constraint specifying constraints on smoothness of the path, velocity, acceleration, jerk constraints etc.
is a cost functional mapping any trajectory to some cost in
Optimal trajectory can be stated as follows:

## Slide 23: Trajectory planning setup continued
Trajectory planning in dynamic environments and static path planning are both PSPACE-hard problems
  At least as complex as checking SAT of a quantified Boolean formula (QBF)
  Example QBF formula:

## Slide 24: Variational methods
Rely on results from nonlinear continuous optimization
We transform the trajectory optimization to the following standard form:
Standard trick to go from constrained to unconstrained optimization is to introduce penalty functions
  Penalty method:
  Barrier function method:
  ()

## Slide 25: Variational methods
Common to use logarithmic barrier functions with Newton-like iterative methods
One problem: Trajectory space is infinite-dimensional. Solution:
  Direct methods:
    Restrict to finite-dimensional subspace, , where are some basis functions (e.g. piecewise linear interpolation uses PWL basis functions)
    Requires numerical integration approximations for the trajectory combined with optimizers like conjugate gradient descent
  Indirect methods: use Pontryagin’s minimum principle that gives optimality conditions for trajectory optimization problem
    Requires solving boundary-value problems of ODEs, that can be approximated numerically

## Slide 26: Graph-search-methods
Variational methods may get stuck in local optima, graph-search methods try to do global search
Configuration space is represented as a graph , where is a set of selected discrete configurations, and is a set of edges, where each edge is labeled by the path segment that the edge represents.
  If , then and
Feasible path can be found by concatenating feasible edges
Does require discretization of the configuration/state space!
  Hand-crafted lane graphs2
  Geometric representations
  Sampling-based discretization

## Slide 27: Some geometric representations3
Voronoi diagrams
Occupancy Grid Map
Cost Map
State Lattice
Driving Corridors
Several nice results or path planning using geometric representations, but usually computationally expensive!

## Slide 28: Sampling-based methods
Typical constraints (differential, holonomic) are usually very difficult to obtain at real-time through sensors
Sampling-based methods explore reachability of free configuration space by trying to apply controls (steering) and checking for collisions
Main purpose of these methods is to construct a roadmap, and use it for planning
Steering functions:
  Random : returns a path obtained by applying a random steering command
  Heuristic: tries to guide vehicle from point to point
  Exact: computes exact path that takes vehicle from to
  Optimal: Returns an optimal exact path

## Slide 29: Probabilistic Roadmap (PRM) Construction
for
  for
    if
    endif
  end
End
return
Sample:
Return points on a grid
Random samples
Interesting:
-nearest neighbors using appropriate distance function
Points within a ball of radius around
Trajectory plan: Use Dijkstra’s shortest-path algorithm on the resulting roadmap

## Slide 30: Heuristic search A*
Once we have a roadmap, how do we find the best path in the roadmap?
Dijkstra’s shortest path algorithm: uses best first search to build a tree representing shortest paths from a given source to all other vertices in the graph
We typically need a path to only a single vertex (in the goal set), in this case a heuristic can be used to guide the search process
Most prominent heuristic search algorithm is A*
Shown to be optimally efficient if heuristic function is admissible (never overestimates the cost)

## Slide 31: How A* works
Constructs tree of paths from initial node, expanding paths one step at a time, till one of the path reaches the goal
In each iteration, A* determines which partial path to expand based on an estimate of the cost
It selects the path that minimizes , where, .
= cost of path from start node to ,
= estimate of the cheapest cost to go from to the goal
: heuristic function
is admissible, if it never over-estimates actual cost to get to the goal
Dijkstra’s shortest path: special case of A*, where

## Slide 32: A* implementation
A* (Graph G(V, E), )
  /* newly discovered nodes, not yet explored */
  /* already evaluated nodes */
  /* best predecessor node so far */
  /* cost of reaching from */
    /* estimate of reaching from via */
  ;
  ;
  /* if you are here, it means is either a new open node or has we just found a lower cost path to */

## Slide 33: Weighted A*
Admissibility criterion forces A* to inspect all equally promising paths to find the optimal
Approximate shortest paths can be found by relaxing the admissibility criterion (i.e. the function)
  This guarantees that the path found is no worse than times the optimal path
Weighted A* variants involve defining a heuristic that is a function of . E.g. static weighted A* uses

## Slide 34: Many variants of A*
Real-time re-planning: D*, Focused D*, D* Lite: recompute shortest path anytime the underlying graph changes, making use of results from previous search
Anytime search algorithms: Quickly find a (possibly sub-optimal) path first, and continue to improve the solution if there is more computational time
  Anytime A*: weighted heuristic that continues searching using cost of previously identified path as upper bound and admissible heuristic as lower bound
  Other variants such as Anytime Repairing A*, Anytime Dynamic A* etc.

## Slide 35: Rapidly Exploring Random Trees (RRTs)
RRT one of a family of algorithms based on incremental sampling, i.e. when you do not want to a priori build the entire roadmap
Also known as single-query PRMs
Very fast algorithm, allows on-the-fly construction of paths
// is a tree
for
// Find point in that is closest to
// Find control that gets you closest to from
end
Plan = Path from to s.t.

## Slide 36: RRT in action
Target
Sample goal
Select closest neighbor
Find collision-free control
Obstacle
Target
Obstacle
Target
Obstacle

## Slide 37: Problems with RRT
Suppose you are given a function that assigns costs to paths
RRT solution is usually far from optimal
Karaman & Frazzoli (2010) showed that probability of RRT converging to an optimal solution is 0
First alternative: RRG (Rapidly exploring Random Graph)
  Connects new sample to all vertices within some distance to it
  Can create graphs with cycles
  Improves optimality: probability of RRG converging to an optimal solution is 1

## Slide 38: Many variants of PRMs and RRTs
Many variants: RRT* (rewires the tree as better paths are found), PRM*, etc.
Some of them add optimality criteria such as costs on edges
Algorithms differ in the underlying structure maintained: PRM (forest), RRT (tree), RRG (graphs with possible cycles), RRT* (acyclic graphs) etc.
There are two key considerations:
  Probabilistic completeness: given infinite time, will the procedure identify a path to the goal set
  Asymptotic optimality: does the optimal path found by the algorithm converge to the actual optimum in the limit

## Slide 39: Combining RRTs with STL
Define path planning objectives in STL
Define robustness of STL on partial trajectories
Use RRT to explore the search space
When selecting nearest neighbors of the goal point, select ones with high robustness
Allows path-planning with STL objectives!
Combining RRTs with LTL objectives has been extensively studied in the literature

## Slide 40: Markov Decision Process
Markov chain with a controller!
Represented as a tuple , where:
  as before (can add to the definition if needed)
  is a finite set of actions
  is the transition probability function such that for all states and ,
  is a reward function. defines the immediate reward received for transitioning from state to state
  is a discount factor representing diminishing rewards with time

## Slide 41: Autonomous Robot controlling its actions
Assume fixed target location
Reward for transitions going to target cell = 1, otherwise 0
Just part of the robot MDP showing two different actions, each action leading to next states with some probability
Which action to choose from each cell?
How do we find an optimal policy (that maximizes rewards)?
up
0.9
0.1
dn
0.9
0.1

## Slide 42: Markov Decision Process
MDP can be described as a tuple , where:
  finite set of states
  : finite set of actions
  is the transition probability function such that for all states and ,
  is a reward function. (Sometimes a reward function is written with actions as well, i.e. . We will use only state-reward functions to make it easy.)
  is a discount factor representing diminishing rewards with time

## Slide 43: MDP run
Start in some initial state and choose action
  Results in some state drawn according to
    Pick a new action
      Results in some state drawn according to
        ...
Total payoff for this run:

## Slide 44: MDP as two-player game
System starts in some initial state and player 1 (controller) chooses action
  Results in player 2 (environment) picking state according to
    Player 1 picks a new action
      Player 2 picks state drawn according to
        ...
Total payoff for this run:

## Slide 45: Policies and Value Functions
Policy is any function mapping states to actions
  This is deterministic view of policies, later we will look at stochastic policies
Policy is basically the “implementation” of our controller. It tells the controller what action to take in each state.
If we are executing policy , then in state , we take action
Value of a state under policy (denoted ) is the expected payoff starting in and following thereafter
I.e.

## Slide 46: Bellman Equation
Bellman showed that :
  computing optimal reward/cost over several steps of
  a dynamic discrete decision problem (i.e. computing the best decision in each discrete step)
  can be stated in a recursive step-by-step form
  by writing the relationship between the value functions in two successive iterations.
This relationship is called Bellman equation

## Slide 47: Value function satisfies Bellman equations
I.e. expected sum of rewards starting from has two terms:
  Immediate reward
  Expected sum of future discounted rewards
Note that above is the same as:
For a finite-state MDP, we can write one such equation for each , which gives us linear equations in variables (the unknown for each . This can be solved efficiently (Gaussian elimination).

## Slide 48: Optimal value function
We now know how to compute the value for a given policy
Computing best/optimal policy:
There is a Bellman equation for optimal value function:
And optimal policy is the that make above equation hold, i.e.

## Slide 49: Planning in MDPs
How do we compute the optimal policy?
Two algorithms:
  Value iteration
  Policy iteration
Value iteration: Repeatedly update estimated value function using Bellman equation
Policy iteration: Use value function of a given policy to improve the policy

## Slide 50: Value iteration
: Value of state at the beginning of the iteration
Initialize ,
While {
}
Can be shown that after finite number of iterations converges to

## Slide 51: Policy iteration
Let be the policy at the beginning of the iteration
Initialize randomly
While () {
/* i.e. compute */
}
Can be shown that this algorithm also converges to the optimal policy
Can use the LP formulation to solve this, or an iterative algorithm

## Slide 52: Using state-action pairs for rewards
When using rewards for action-values , indicates the reward obtained by taking action in state and following the policy thereafter
Optimal-action-value policy denoted by
Note that previous formulas change a bit, as the reward depends on which action is taken (and is thus is subject to transition probability)

## Slide 53: Challenges
Value iteration and Policy iteration are both standard, and no agreement on which is better
In practice, value iteration is preferred over policy iteration as the latter requires solving linear equations, which scales ~cubically with the size of the state space
Real-world applications face challenges:
  Curse of modeling: Where does the (probabilistic) environment model come from?
  Curse of dimensionality: Even if you have a model, computing and storing expectations over large state-spaces is impractical

## Slide 54: Approximate model (Indirect method)
Use data to estimate model
  Run many simulations
  Estimate
Perform optimal policy search over the approximate model
Model converges asymptotically if all state-action pairs are visited infinitely often

## Slide 55: Q-learning: (Model-free method)
Called a model-free method, because it does not assume knowledge of a model of the environment
Learning agent tries to learn optimal policy from its history of interactions with the environment
Agent interaction described in tuples called “experience”
Recall that function for each state and action returns the expected reward of that action (and all subsequent actions) at that state
Q-learning uses a technique called “temporal differences” to estimate optimal value in each state
Agent maintains a table of values for each state and action

## Slide 56: Q-learning
Whenever the agent is in state and takes action , we have new data about the reward that we get, we use this to update our estimate of the value at that state
Agent updates its estimate of using following equation:
Learning rate controls how aggressively you update the old value.
  means that you update value very slowly
  means that you simple replace the old value with the new value
is the estimate of the optimal future value
Note that in learning, when we update the value of a state , we have some knowledge of what happens when we take action in state .

## Slide 57: Q-learning
Q-learning learns an optimal policy no matter which policy you are following – hence it’s called an off-policy method
One issue in Q-learning (and more broadly in RL): How should an agent decide which actions to choose to explore?
  Is it better to explore more actions, or exploit an action for which we got a good reward (i.e. pursue the chosen path deeper)?
  This is called the exploitation-exploration tradeoff, a parameter to choose for many RL algorithms
One way to do this is using the Boltzmann distribution:
The parameter (called temperature) controls probability of picking non-optimal actions. If is large, all actions are chosen uniformly (explore), if is small, then the best actions are chosen.

## Slide 58: Some more challenges for RL in autonomous CPS
Uncertainty!
In all previous algorithms, we assume that all states are fully visible and precisely estimable
In CPS examples, there is uncertainty in states (sensor/actuation noise, state may not be observable but only estimated, etc.)
The approach is to model the underlying system as a Partially-Observable Markov Decision Process (POMDP) -- pronounced POM-DPs

## Slide 59: POMDPs
6-tuple :
  : set of states
  : set of actions
  : set of observations
  : transition function
    gives the probability of state transitioning to under action
  observation function
    gives the probability of observing if action is taken in state
  reward function
    gives a reward for taking action in state

## Slide 60: RL for POMDPs
Control theory concerns with planning problems for discrete or continuous POMDPs
Strong assumptions required to get theoretical results of optimality
  Underlying state-transitions correspond to a linear dynamical system with Gaussian probability distribution
  Reward function is a negative quadratic loss
Solving generic discrete POMDP is intractable, finding tractable special cases is a hot topic

## Slide 61: RL for POMDPs
Policies in POMDPs are mappings from belief states to actions
Instead of tracking arbitrarily long observation histories, we track belief states
A belief state is a distribution over states; in belief state , probability is assigned to being in
Computing belief states:
  Start in some initial belief state prior to any observations
  Compute new belief state based on current belief state , action , and observation :

## Slide 62: RL for POMDPS
Kalman filter: exact update of belief state for linear dynamical systems
Particle filter: approximate update for general systems

## Slide 63: Algorithms for planning in POMDPs
Tons of literature, starting in 1960s
Point-based value iteration:
  Select a small set of reachable belief points
  Perform Bellman updates at those points, keeping value and gradient
Online search for POMDP solutions
  Build AND/OR tree of the reachable belief states from current belief
  Approaches like branch-and-bound, heuristic search, Monte Carlo Tree search

## Slide 64: Bibliography
Pendleton, Scott Drew, Hans Andersen, Xinxin Du, Xiaotong Shen, Malika Meghjani, You Hong Eng, Daniela Rus, and Marcelo H. Ang. "Perception, planning, control, and coordination for autonomous vehicles." Machines 5, no. 1 (2017): 6.
Paden, Brian, et al. "A survey of motion planning and control techniques for self-driving urban vehicles." IEEE Transactions on Intelligent Vehicles 1.1 (2016): 33-55. https://arxiv.org/pdf/1604.07446.pdf
Katrakazas, C., Quddus, M., Chen, W. H., & Deka, L. (2015). Real-time motion planning methods for autonomous on-road driving: State-of-the-art and future research directions. Transportation Research Part C: Emerging Technologies, 60, 416-442.
https://en.wikipedia.org/wiki/A*_search_algorithm
Bast, D. Delling, A. Goldberg, M. Müller-Hannemann, T. Pajor, P. Sanders, D. Wagner, and R. F. Werneck, “Route planning in transportation networks”, https://arxiv.org/pdf/1504.05140.pdf
https://www.annualreviews.org/doi/pdf/10.1146/annurev-control-060117-105157
https://journals.sagepub.com/doi/pdf/10.1177/0278364920917446?casa_token=rawjqqG8ZdQAAAAA:xPgWGamXwyciEb8pAqHcaHYXF96Mz7cmu4TKtvk7jMxz8X63ndFuxm5X7osUQRaibeC2aN_g2WCw1Q