## Slide 1: Autonomous Cyber-Physical Systems: Basics of Verification
Fall 2020. CS 513.
Instructor: Jyo Deshmukh

## Slide 2: Safety Requirements/Specifications
A safety requirement states that a system always stays within the set of good states (i.e. nothing bad every happens)
Examples:
  Collision avoidance: the distance between a car and a pedestrian is always greater than a threshold
  Patient’s blood glucose never drops below 80 mg/dL
  Maximum temperature specification on the battery is not exceeded
Safety requirements can be formalized using transition systems

## Slide 3: Transition System
Transition System is a tuple
  : Set of State Variables over finite or infinite domains
  : Function mapping to initial values
  : Transition description giving code to update variables in
off
on
(press==0)?
(press==1)?
(press==0) & (x<10) ?
0
(press==1) or (x10) ?

## Slide 4: Transition System
Semantics:
  Each combination of values assigned to state variables can be interpreted as a state. : set of all possible states (could be an infinite set)
  : Finite or infinite set of initial states which is a subset of
  : Finite or infinite set of transitions, which is a subset of
Values to input variables are chosen nondeterministically
  Why? This is an abstraction technique (i.e. making something less concrete)
  We are interested in making sure that no matter what input value, the TS has desirable behavior

## Slide 5: Example of a TS
: { mode, x }
Semantics:
: { mode off, x 0 }
has an infinite number of transitions
  (off, 0) (off, 0)
  (off, 0) (on, 0)
  (on, n) (on, n+1) if n < 10
  (on, n) (off, 0) otherwise
off
on
(press==0)?
(press==1)?
(press==0) & (x<10) ?
0
(press==1) or (x10) ?

## Slide 6: Transition Systems and state
All kinds of components (synchronous, asynchronous, timed, hybrid, continuous components have an underlying transition system
State in the transition system underlying a component captures any given runtime configuration of the component
Continuous components, Timed Processes, Hybrid Processes in general, have infinite number of states

## Slide 7: Example transitions for TS
(off,0)
(on,0)
(on,1)
(on,2)
(on,100)
(off,42)
off
on
(press==0)?
(press==1)?
(press==0) & (x<10) ?
0
(press==1) or (x10) ?
(on,42)

## Slide 8: TS describes all possible transitions
(off,0)
(on,0)
(on,1)
(on,2)
(on,100)
(off,42)
off
on
(press==0)?
(press==1)?
(press==0) & (x<10) ?
0
(press==1) or (x10) ?
(on,42)
Transitions indicated as dotted lines can’t really happen in the component
But, the TS will describe then, as the states of the TS are over!

## Slide 9: Reachable states of a modified switch TS
off
on
(press==0)?
(press==1)?
(press==0) & (x<2) ?
0
(press==1) or (x 2) ?
(off,0)
(on,0)
(on,1)
(on,2)
(on,100)
(off,42)
(on,42)
Reachable states and transitions

## Slide 10: Desirable behaviors of a TS
Desirable behavior of a TS:
  Defined in terms of acceptable (finite or infinite) sequences of states
  If all unacceptable sequences of a TS are finite in length, then the property encoding acceptable behavior is called a safety property
Safety property can be specified by partitioning the states into a safe/unsafe set
  , ,
  Any finite sequence that ends in a state is a witness to undesirable behavior, or if all (infinite) sequences starting from an initial state never include a state from , then the TS is safe.

## Slide 11: Safety invariants
An invariant is a Boolean expression over the state variables of a TS
A property is called an invariant of TS if every reachable state of TS satisfies
An invariant is a safety invariant if
Examples of invariants for modified switch:
  [note: is an int]
off
on
(press==0)?
(press==1)?
(press==0) & (x<2) ?
0
(press==1) or (x 2) ?

## Slide 12: Safety invariants
Examples of non-invariants:
Suppose, , and
  Then, we can verify that is a safety invariant for modified switch: proof towards the end
off
on
(press==0)?
(press==1)?
(press==0) & (x<2) ?
0
(press==1) or (x 2) ?

## Slide 13: Inductive Safety Proof
Given TS and a property , prove that all reachable states of TS satisfy
Base case: Show that all initial states satisfy
Inductive case: assume state satisfies , then show that if , then must also satisfy
off
on
(press==0)?
(press==1)?
(press==0) & (x<2) ?
0
(press==1) or (x 2) ?

## Slide 14: Inductive Invariant
A property is an inductive invariant of a transition system TS if
  Every initial state satisfies
  If any state satisfies , and , then satisfies
By definition, if is an inductive invariant, then all reachable states of TS satisfy , and hence it is also an invariant

## Slide 15: Proving inductive invariants: I
Consider transition system TS given by
  :
  : if then (else remains unchanged)
Is an inductive invariant?
Base case: is zero, so is trivially satisfied

## Slide 16: Proving inductive invariants: I
Inductive case:
  Pick an arbitrary state (i.e. arbitrary value for state variable ), say
  Now assume satisfies , i.e.
  Consider the transition, there are two cases: (Note: is an integer)
    If , then after the transition, and
    If , then (because guard is not true), which is .
  In either case, after the update
  So is an inductive invariant, and the proof is complete
  :
  : if then

## Slide 17: Proving inductive invariants: II
Consider transition system TS given by
  : ,
  : if then (else remain unchanged)
Is an inductive invariant?
Base case: Initial state is (), so is trivially satisfied

## Slide 18: Proving inductive invariants: II
Inductive case:
Pick an arbitrary state (i.e. arbitrary value for state variable ), say
Now assume satisfies , i.e.
Consider the transition if then
What if )? Clearly, does not satisfy !
So is not an inductive invariant for TS, and the proof fails

## Slide 19: Proving inductive invariants: III
Consider transition system TS given by
  : ,
  : if then (else remain unchanged)
Is an inductive invariant?
Base case: Initial state is (), so is trivially satisfied

## Slide 20: Proving inductive invariants: III
Inductive case:
Pick an arbitrary state (i.e. arbitrary value for state variable ), say
Now assume satisfies , i.e. and
Consider the transition
  If then , else
  Now, if , and thus . Thus, is satisfied
  Else case is trivially satisfied because do not change value
In both cases, holds, so, is an inductive invariant!

## Slide 21: How do we prove safety invariants?
To establish that is an invariant of TS:
Find another property such that
  (i.e. every state satisfying must satisfy )
  is an inductive invariant
    Show initial states satisfy
    For arbitrary , and any s.t. , show
This is a sound and complete strategy for establishing safety invariants

## Slide 22: Soundness and Completeness
Formal system: a set of axioms, a grammar for specifying well-formed formulas, and a set of inference rules for deriving new true formulas from axioms
Sound: Starting from the axioms and using inference rules of the formal system, we cannot arrive at a formula that is equivalent to false.
Complete: Proof system is complete with respect to a property if every formula having that property can be derived using the inference rules
Proof rule for proving invariants is sound and complete:
  Sound: It is a correct proof technique
  Complete: If is an invariant, there is some stronger inductive invariant satisfying inductive conditions that we can find

## Slide 23: Safety Proof for Switch
Let’s try the inductive invariant:
off
on
(press==0)?
(press==1)?
(press==0) & (x<2) ?
0
(press==1) or (x 2) ?
Base case: trivially satisfies
Inductive hypothesis: assume that a state satisfies
Inductive step: prove that any s.t. satisfies
  Case I:
    = [trivial]
    = [satisfies second conjunct in ]
  Case II:
    if , this implies that , so satisfies
    otherwise, this again implies that satisfies
So is an inductive invariant
Further, (note that every state satisfying will satisfy )
So is an invariant of the TS!

## Slide 24
Automatic Verification

## Slide 25: Model checking & Automatic Verification
Coming up with invariants and proofs requires considerable human ingenuity!
Initial techniques for formal verification i.e. rigorously establishing program correctness were all largely manual
Model checking (invented around 1981-82) was the first approach at trying to automate the process of proving program correctness
Model checking inventors,
ACM 2007 Turing Award winners
(L to R)
E. Allen Emerson
Ed Clarke
Josef Sifakis

## Slide 26: What is model checking?
Checking if all behaviors of the system model are contained within the behaviors specified by a property specification
E.g. specifications:
  When adaptive cruise control is engaged, the speed of the car is between 20 and 60mph
  Always, if the drone detects an obstacle along its current flight path, it makes a call to the re-planning module within 1 second
  No two robots can be within 2 meters of each other
First algorithm for model checking used “Kripke Structures” as models (a kind of labeled transition system), and CTL for specifications

## Slide 27: CTL model checking
Atomic proposition : Label each state that satisfies
: Label a state if any successor satisfies
: Label a state if all of its successors satisfy
: Label all states satisfying as
Until there is no change:
Add states with label if it has a successor labeled

## Slide 32
No more states with at least one successor green!
Check the states you have: if it contains the initial state, then the model satisfies

## Slide 33: CTL model checking
: Label all states satisfying as
Until there is no change:
Add states with label if all its successors are labeled
: Label all states satisfying as
Until there is no change:
Remove label from a state if it does not have any successor labeled

## Slide 35
Cannot remove any more states as all remaining states have at least one green successor!
Check the states you are left with: if it contains the initial state, then the model satisfies

## Slide 36
: What if bottom state was not green?

## Slide 37: : What if bottom state was not green?
Cannot remove any more states as all remaining states have at least one green successor!
Check the states you are left with: if it contains the initial state, then the model satisfies

## Slide 38: Greatest and least fixpoints
similar to
: similar to and (with the caveat that needs to be satisfied on every state that has a successor to a state marked
Fixpoint = point at which there is no change, i.e.
Consider the operation of adding/removing states as the function
  Fixpoint = Point at which you can no longer add/remove states
Least fixpoint = When adding states, smallest set you can get?
  You can always add all the states: not very useful
Greatest fixpoint = When removing states, largest set you can get?
  You can always remove all the states: not very useful

## Slide 39: CTL model checking in a nutshell
Fixpoint computation based algorithm
Many improvements to CTL model checking over the years (with the help of symbolic algorithms to accelerate fixpoint computation, represent sets of states, etc.)
Bounded model checking:
  Don’t check the entire state space using a “backward reachability” algorithm, but instead go forward in time from the initial state
  Use of SAT solvers to check feasibility of paths to failure states
Many good model checkers: NuSMV, CBMC, etc.

## Slide 40: Reachability
A state of a transition system is reachable if there is an execution starting in some initial state that ends in .
Algorithm to compute reachable states from a given set of initial states (just BFS):
Procedure ComputeReach(TS)
  , k:=1;
  While
  Temp :=
  ForEach
  If () Temp := Temp
  EndForEach
  Temp,
  EndWhile
  Return
  EndProcedure
  To get a proof of safety, do reachability computation, and if ComputeReach(TS) = , then the TS is safe
  Bounded model checking is like doing reachability analysis (but with temporal logic properties)

## Slide 41: Proving that something is an invariant
Given TS and a property , prove that all reachable states of TS satisfy
Recall ComputeReach(TS), it actually gives an inductive definition of reachable states
  All states specified by are reachable using 0 transitions
  If a state is reachable using transitions, and is a transition in , then is reachable using transitions
  Reachable = Reachable using transitions for some

## Slide 42
LTL model checking

## Slide 43: LTL Monitors
A safety monitor classifies system behaviors into good and bad
Safety verification can be done using inductive invariants or analyzing reachable state space of the system
  A bug is an execution that drives the monitor into an error state
Can we use a monitor to classify infinite behaviors into good or bad?
Yes, using theoretical model of Büchi automata proposed by J. Richard Büchi in 1960

## Slide 44: Büchi automaton: Example 1
Extension of finite state automata to accept infinite strings
0
1
States :
Input variable with domain :
Final state:
Transitions: (as shown)
Given trace (infinite sequence of symbols from , is accepted by , if there exists a path from the initial state where appears infinitely often
1
0

## Slide 45: Büchi automaton Example 2
: , : :
Transitions: (as shown)
Note that this is a nondeterministic Büchi automaton
accepts if there exists a path along which a state in appears infinitely often
  Fun fact: there is no deterministic Büchi automaton that accepts this language

## Slide 46: Büchi automaton Example 3
What is the language of ?
  LTL formula:
  I.e. always when , in some future step,
  In other words, must be followed by
|
1 &
: , : :
Transitions: (as shown)

## Slide 47: Büchi automaton and LTL
Language of an automaton: set of all strings accepted by the automaton
0
1
What is the language of ?
LTL formula
1
0

## Slide 48: Büchi automaton Example 2
: , : :
Transitions: (as shown)
What is the language of ?
LTL formula

## Slide 49: Büchi automaton Example 3
What is the language of ?
LTL formula:
I.e. always when , in some future step,
In other words, must be followed by
|
1 &
: , : :
Transitions: (as shown)

## Slide 50: Using Büchi monitors
Theoretical result: Every LTL formula can be converted to a Büchi monitor/automaton
Size of is generally exponential in the size of ; blow-up unavoidable in general

## Slide 51: LTL Model checking
Construct composition of the original transition system and the Büchi monitor
If there are cycles in the composite process that visit the states specified by the Büchi condition then we have found a violation
Reachable cycles in process composition correspond to counterexamples!
Implemented in many verification tools (e.g. the SPIN model checker developed at NASA JPL)
Many open source tools to translate LTL properties to Büchi monitors: quite popular in the robotics domain

## Slide 52: LTL is a language for expressing system requirements
So far we have seen how we can express behaviors of individual system traces using LTL
A system starting from some initial state satisfies a LTL requirement if all system behaviors starting in satisfy the requirement
Denoted as
E.g. a system is safe w.r.t. a safety requirement if all behaviors satisfy
Does (Blinker, (x0,y0)) (x0)?
nat x := 0; bool y:= 0
A x := x + 1
B: even(x)
y: = 1-y
Blinker

## Slide 53: Processes & Fairness
nat x := 0; bool y:= 0
A x := x + 1
B: even(x)
y: = 1-y
Blinker
Liveness property: (x 10)
  Is this property guaranteed to hold?
  No, task A may be executed less than 10 times.
Liveness Property: y (eventually y is 1)
  Is this property guaranteed to hold?
  No, task B may never be selected for execution!
But, this seems like a very unrealistic or broken scheduler!
For infinite executions involving multiple tasks, it is important for the execution to be fair to each task

## Slide 54: Weak vs. Strong fairness
A fairness assumption is a property that encodes the meaning of what it means for an infinite execution to be fair with respect to a task.
Weak fairness: If a task is persistently enabled, then it is repeatedly executed.
  I.e. if after some point the task guard is always true, then the task is infinitely often executed.
Strong fairness: If a task is repeatedly enabled, then it is repeatedly executed.
  I.e. if the task guard is infinitely often true, then the task is infinitely often executed.
nat x := 0; bool y:= 0
A x := x + 1
B: even(x)
y: = 1-y
Blinker

## Slide 55: Expressing fairness assumptions in LTL: I
Fairness assumptions can be expressed in LTL!
Add a new variable taken that takes value ‘A’, ‘B’
Weak fairness: ((taken = ))
Task A: is , so this simplifies to: wf(A) (taken=A)
Task B: wf(B) (even(x)) (taken=B)
Does (wf(A) wf(B)) (x 10)?
  Yes!
Does (wf(A) wf(B)) y?
  No!
nat x ; bool y
A x := x + 1; takenA
B: even(x)
y: = 1-y; taken B
Blinker
{A,B,} taken

## Slide 56: Expressing fairness assumptions in LTL: II
Strong fairness: ((taken = ))
Task A: is , so this simplifies to: sf(A) (taken=A)
Task B: sf(B) (even(x)) (taken=B)
Does (sf(A) sf(B)) (x 0)?
  Yes!
Does (sf(A) sf(B)) y?
  Yes!
nat x ; bool y
A x := x + 1; takenA
B: even(x)
y: = 1-y; taken B
Blinker
{A,B,} taken
If a process satisfies a liveness requirement under strong fairness, it satisfies it under weak fairness: strong fairness is a stronger formula than weak fairness

## Slide 57
Formal verification for Dynamical Systems

## Slide 58: Safety verification using barrier certificates
Barrier certificate: safety invariant for a continuous dynamical system
It establishes an invisible barrier that trajectories of a system cannot cross
  (think of it as a force-field)
Reasoning very similar to that of an inductive invariant
  Establish that the initial states all lie within the barrier
  Establish that the unsafe states are all outside the barrier
  Show that the next states for all states on the barrier are inside the barrier

## Slide 59: Strict barrier certificate
Given system
Function that serves as a classifier between good and bad states
Barrier conditions:
  (The last condition models the barrier pushing the system back!)
Unsafe
Initial

## Slide 60: Example
  Initial state set:
  Unsafe set:
Barrier:
  From plot:
    for initial states, ,
    for unsafe states,
Unsafe
Initial
Barrier

## Slide 61: Example
Finally, =
  =
    =
    =
From the plot, the above function is always negative for values of where
Barrier

## Slide 62: Time-bounded Reachability
Verification basics and Hybrid Systems lecture: reachability analysis using a “fix-point based algorithm”
  uses a breadth-first approach to compute reachable states over an infinite time-horizon
Barrier certificates: also provide infinite time safety results, but require manual ingenuity in coming up with a barrier; difficult to do for hybrid/nonlinear systems
Time-bounded reachability: Starting from some initial state in a given set of initial states, does the system behavior ever reach an unsafe state within a given time bound?

## Slide 63: Problem definition
Let be the solution trajectory of a given dynamical system (could be nonlinear, hybrid, timed, …) when the system starts in initial state
Time-bounded reachability: Prove that:
Counterexample to time-bounded reachability shown below
Unsafe
?
Trajectory segment with unsafe states
Trajectory segment with safe states

## Slide 64: Solutions to time-bounded reachability
To solve time-bounded reachability exactly:
  Compute set of all states reachable from :
  Check if is empty
  Challenge: computing is very hard (even for the simplest case of general linear dynamical systems)
Instead, we focus on approximating
  Under-approximation
  Over-approximation
  Combination of both

## Slide 65: Under-approximation
When we under-approximate the set of initial states, at each time, the set of reachable states that we compute is a subset of the actual set of reachable states
Best example of under-approximation is (guaranteed) numerical simulation
  Guaranteed numerical simulation: better than numerical integration schemes as it gives bounds on error in numerical integration (e.g. VNODE)
Under-approximation is:
  Sound for bug-finding: if we find a bug, then it is really a bug
  Unsound for verification: if we do not find a bug, does not mean the system is safe

## Slide 66: Under-approximation: sound for bug-finding
The good case: under-approximation found a trace that contained unsafe states – we found a bug in the system!

## Slide 67: Under-approximation: unsound for verification
The bad case: under-approximation did not find a trace that contained unsafe states – we cannot conclude anything.

## Slide 68: Over-approximation
When we over-approximate the set of initial states, at each time, the set of reachable states that we compute is a superset of the actual set of reachable states
Most formal verification techniques are based on over-approximation
Over-approximation is:
  Unsound for bug-finding: if we find a bug, then it may not really be a bug
    Because of over-approximation error
  Sound for verification: if we do not find a bug, we have a proof that the system cannot reach an unsafe state in any time in

## Slide 69: Reachability for piecewise affine (PWA) systems
PWA systems are a simplification of hybrid automata
For a PWA system with modes:
  Each mode described by an affine invariant of the form
  In each mode the dynamics are described as: +
A lot of research over last 20 years on computing the set of reachable states for PWA systems
  Focus: reduce approximation error and increase scalability (in number of modes)
  Tools: PHAver, d/dt, CheckMate, SpaceEx

## Slide 70: Reachability for affine systems
Recall that for a linear system (for now assume no inputs):
Let , now is just some constant matrix
If is some polyhedral set, we can compute the exact set of reachable states for every state in at time , because is just a linear transform
Thus, we get
Could be acceptable for continuous systems: between discrete time steps, solution remains in the neighborhood of the aproximations (and we can over-estimate this neighborhood numerically)

## Slide 71: Problem for CPS (hybrid systems)
Controller may be event-triggered, where it detects the level of a certain physical quantity, and based on that changes mode of operation
An event firing between consecutive time steps could take the PWA system in a different mode!
We need to account for what may happen between time-steps
This is done by covering the reach-sets computed at times and by a shape that includes both
Lots of research done on which shape is the best, and different shapes have different tradeoffs
  Ellipsoids, Zonotopes, Support Functions
  SpaceEx tool uses support functions, and is pretty accurate for reasonably sized PWA systems now
Wrong!

## Slide 72: Reachability for nonlinear systems
Not all systems can be modeled as PWA!
Nonlinear systems:
  Approach I: first PWA-ize the system, then do reachability. Drawback: Error encountered during PWA-ization accumulates
  Approach 2: use more interesting models such as Taylor models (based on Taylor series representations): used in tool Flow*
  Approach 3: throw the problem at a powerful nonlinear SMT solver: used in tool dReach

## Slide 73: Combining under and over-approximations
Also known as simulation-guided reachability analysis
Main idea:
  Sample some initial states, perform simulations starting from these states
  Use “continuity”-like arguments to bloat the trajectories in a sound manner
  If bloated trajectories cover initial state space, go to step 4, if not go back to step 1
  If bloated trajectories do not intersect unsafe set, conclude system is safe. If bloated trajectories intersect unsafe set, try to refine bloated trajectories to check if there is a true counterexample

## Slide 74: Simlulation-guided reachability depiction
Unsafe
Initial
Simulation Trace up to time T
Reach-Tube up to time T

## Slide 75: Secret sauce: how to bloat
Main idea: Solutions of ODEs are “sensitive” to their initial conditions
Such sensitivity gives an estimate on how far two trajectories can go if they start apart
A key notion is a discrepancy function that bounds how far trajectories can grow
Obtaining a that shows trajectories remain bounded within some reasonable factor of the distance between their initial conditions is very useful
  We only simulate from , and we know how all neighbors of will behave!
Technique implemented in tool C2E2, DryVR

## Slide 76: Bibliography
Breach : https://link.springer.com/chapter/10.1007/978-3-642-14295-6_17
Prajna, S., & Jadbabaie, A. (2004, March). Safety verification of hybrid systems using barrier certificates. In International Workshop on Hybrid Systems: Computation and Control (pp. 477-492).
Duggirala, Parasara Sridhar, et al. "C2E2: a verification tool for stateflow models." International Conference on Tools and Algorithms for the Construction and Analysis of Systems.
Frehse, Goran, Colas Le Guernic, Alexandre Donzé, Scott Cotton, Rajarshi Ray, Olivier Lebeltel, Rodolfo Ripado, Antoine Girard, Thao Dang, and Oded Maler. "SpaceEx: Scalable verification of hybrid systems." In International Conference on Computer Aided Verification, pp. 379-395. Springer, Berlin, Heidelberg, 2011.
Chen, Xin, Erika Ábrahám, and Sriram Sankaranarayanan. "Flow*: An analyzer for non-linear hybrid systems." In International Conference on Computer Aided Verification, pp. 258-263. Springer, Berlin, Heidelberg, 2013.
Frehse, Goran. "PHAVer: Algorithmic verification of hybrid systems past HyTech." International workshop on hybrid systems: computation and control. Springer, Berlin, Heidelberg, 2005
Asarin, E., Dang, T., & Maler, O. (2002, July). The d/dt tool for verification of hybrid systems. In International Conference on Computer Aided Verification (pp. 365-370). Springer, Berlin, Heidelberg.
Fan, Chuchu, Bolun Qi, Sayan Mitra, Mahesh Viswanathan, and Parasara Sridhar Duggirala. "Automatic reachability analysis for nonlinear hybrid models with C2E2." In International Conference on Computer Aided Verification, pp. 531-538. Springer, Cham, 2016.
Donzé, Alexandre, and Oded Maler. "Systematic simulation using sensitivity analysis." In International Workshop on Hybrid Systems: Computation and Control, pp. 174-189. Springer, Berlin, Heidelberg, 2007