## Slide 1: Autonomous Cyber-Physical Systems: Signal Temporal Logic, Model-based Testing, Falsification
Fall 2021. CS 513.
Instructor: Jyo Deshmukh
USC Viterbi
School of Engineering
Department of Computer Science

## Slide 2: Typical day in a control designer’s life
Uh Oh!
time
,
time
… should be okay
,
Looks good
time
,

## Slide 3: Signal Temporal Logic (STL)
STL : logic to formalize control-theoretic properties, properties of path-planning algorithms, express timing constraints, causality relations
LTL: properties of step-wise, discrete-valued reactive systems
  Operating systems, Distributed systems, shared-memory programs, device drivers etc.
Invented by Dejan Nickovic and Oded Maler

## Slide 4: Before STL, there was MTL
MTL = Metric Temporal Logic
Extended LTL with the notion of temporal operators that range over time-intervals
Example formula:
  : At all times between time 0 and 3, the propositions and are true
MTL required separate definition of predicates. E.g. could mean “it is raining”, or it could mean “, etc.
STL introduced signal predicates as atomic formulas

## Slide 5: Expressing specifications in STL
0
100
50
1
3
Always between time 0 and 100
Eventually at some time t between time 20 and 60
From that time t, always till the end of the signal trace
0
100
1
-0.1
+0.1
60

## Slide 6: Can we express our engineer’s requirements?
Uh Oh!
time
,
time
… should be okay
,
Looks good
time
,

## Slide 7: STL is interpreted over Signals
Signal is a function from a time domain to a value domain
Time domain can be
  A discrete domain: e.g. positive integers (traces for LTL), arbitrary finite set of values,
  A dense domain: e.g. a continuous set of real-valued time-instants
Value domain can be
  A finite domain: e.g. Booleans (traces for LTL), some finite enumeration (e.g. a set of modes)
  An infinite domain: e.g. integers, reals, etc.
  A combination of any number of these

## Slide 8: More about Signals
A signal that has only one kind of value domain is called univariate (only one thing varies), and with multiple domains is called multivariate
Number of distinct components of a signal is called its dimension
Thus, signal value at any given time is a vector of values, each of which may come from a different value domain
If we designate a time domain by , and a value domain by , then signals are basically functions from to
In this lecture, we will assume that the time domain is the dense domain , and the value domain is , where is the signal dimension
Thus a signal is a function from to

## Slide 9: STL Syntax
Syntax of STL |  |  | 
 |  | ¦ | is a function over the signal ,
 |  | ¦ | Negation
 |  | ¦ | Conjunction
 |  | ¦ | At some Future step in the interval
 |  | ¦ | Globally in all times in the interval
 |  | ¦ | In all steps Until in interval
Syntax of STL |  |  | 
 |  | ¦ | 
 |  | ¦ | Negation
 |  | ¦ | Conjunction
 |  | ¦ | 
 |  | ¦ | 
 |  | ¦ | 

## Slide 10: STL semantics
Semantics of STL specified recursively over a signal at each time
For each STL formula , here’s how we define it’s semantics:
If is the signal predicate , then iff
,

## Slide 11: Recursive Boolean Semantics of STL
 | ,

## Slide 12: Recursive Boolean Semantics of STL
0.1
0.2
0.3
0.4
0.5
0.6
0.7
1
2
3
 | T | T | T | F | F | T | T | T
 | T | T | T | F | F | T | T | T
0,0
T
at time | 
at time | For all must hold
at time t | At least one must hold
T
T
T
T
T
T

## Slide 13: Example STL formulas: Overshoot
time
Overshoot:
Step:

## Slide 14: Example STL formulas: Settling Time
time
Settling Time:
Step:

## Slide 15: Robot Path Specification
Whenever the robot visits the kitchen, it should visit the bedroom within the next 15 mins.
Robot should not go to the bathroom in the first 60 mins.
: Box describing room
: Position of robot at time
Kitchen
Bedroom
Living Room
Bathroom
Study
TV
Passage
(0,5)
(15,25)

## Slide 16: Robot Path Specification
Kitchen
Bedroom
Living Room
Bathroom
Study
Passage
The robot battery should last between 4 hours and 6 hours
For the first 10 hours, the robot is never in any room for more than mins

## Slide 17: STL has quantitative semantics
Quantitative semantics defined using the notion of a Robust Satisfaction Value, or Robustness Value
Robustness is a function that maps
  a given trace ,
  a formula ,
  and a time
  to some real value
We can interpret robustness as “distance to violation” of a given formula

## Slide 18: Distance to violation/satisfaction
GOOD
GOOD
How far is
bad?
0
100
50
3
BAD
0
100
50
3
BAD
How bad is the violation?

## Slide 19: How do quantitative semantics help our engineer?
Uh Oh!
time
,
time
… should be okay
,
Looks good
time
,
= -0.2
= 0.01
= 0.2

## Slide 20: Recursive Quantitative Semantics
, | 

## Slide 21: Robustness computation example
0.1
0.2
0.3
0.4
0.5
0.6
0.7
1
2
3
 | 1 | 1 | 0.5 | -0.5 | -1 | 0.5 | 0 | 0.5
 | 1 | 1 | 0.5 | -0.5 | -1 | 0.5 | 0 | 0.5
0,0
1
1
0.5
0.5
0.5
0.5
at time | 
at time | Minimum over robustness of for
at time t | Maximum over robustness of for
0.5

## Slide 22: Test yourself
0.1
0.2
0.3
0.4
0.5
0.6
0.7
1
2
3
0,0
What about:
0.1
0.2
0.3
0.4
0.5
0.6
0.7
1
2
3
0,0
What is the robustness of this formula?

## Slide 23
Model-based Testing, Falsification

## Slide 24: Closed-loop Models
Closed-loop Models contain:
  Dynamics describing Physical Processes (Plant)
  Code describing Embedded Control, Sensing, Actuation
  Models of connection between plant and controller (hard-wired vs. wired network vs. wireless communication)
For simplicity, consider the composed plant model, controller and communication to be a model that is excited by an input signal and produces some output signal
Consider that the correctness of the model is specified by some property

## Slide 25: Verification vs. Testing
For simplicity, is a function from to ; let the set of all possible functions representing input signals be
Verification Problem:
Prove the following:
Falsification/Testing Problem:
Find a witness to the query:
These formulations are quite general, as we can include the following “model uncertainties” as input signals: Initial states, fixed parameter values, time-varying parameter values, noise, etc.

## Slide 26: Challenges with real-world systems
If plant model, software and communication is simple (e.g. linear models), then we can do formal analysis
Most real-world examples have very complex plants, controllers and communication!
Verification problem, in the most general case is undecidable
  It can be mathematically proven that there is no algorithm which will take the description of an arbitrary closed-loop model and a property, and give a yes/no answer to the verification problem.

## Slide 27: Falsification/Testing
Falsification or testing attempts to find one or more signals such that is true.
In verification, the set (the time domain) could be unbounded, in falsification or testing, the time domain is necessarily bounded, i.e. , where is some finite numeric constant
In verification the co-domain of , could be an unbounded subset of , in falsification, we typically consider some compact subset of
For the input signal component, let denote its compact co-domain
Then the input signal is a function from to where
In simple words: input signals range over bounded intervals and over a bounded time horizon

## Slide 28: Falsification re-framed
Given:
Set of all such input signals :
Input signal : function from to where
Model that maps to some signal with wlog the same domain as , and co-domain some subset of
Property that can be evaluated to true/false over given and
  (No liveness properties!)
Check:

## Slide 29: Input/Output Properties for Closed-loop Models
Properties/Specifications/Requirements are rarely monolithic formulas
Typically specified as a pair: a pre-condition on the inputs, and a post-condition on the outputs
Verification problem then stated as:
  Prove that:
Testing problem stated as:
  Find such that

## Slide 30: Input Properties/Pre-conditions
Common practice in control theory to excite closed-loop models with input signals of certain special shapes
Motivation comes from theory of linear systems, where a step-response or impulse-response are enough to characterize all behaviors of the system
Such special shapes do not provide comprehensive information for nonlinear closed-loop systems, yet, it is still common to excite these systems with a few common patterns
Frequently, input signal patterns come from engineering insights or application-specific domain expertise

## Slide 31: Common input patterns used for testing
Step
Ramp
Impulse
Pulse Train
Multiple Steps
Sinusoid

## Slide 32: Testing in practice
Each time-point in a signal is an independent dimension, i.e. the signal can change arbitrarily at each time-point in the signal
Number of independent domains is infinite (e.g. consider a signal defined over rational time-points)
Typical testing approach is to find a test-suite: This is a finite number of test input signals (satisfying ) and then obtain output behaviors using these signals as test inputs.
If each corresponding output signal satisfies the output property , then testing concludes, indicating that the model is correct for the given test-suite (i.e. no output in the test-suite violates .

## Slide 33: Signal Generation
Find a signal generator for the property
  Function that uses random-ness to generate an input signal that satisfies (hopefully, an input signal different from previously generated ones!)
Signal generation usually relies on defining a finite parameterization for the input signal
  For the chosen class of signals, find parameters that define the shape
  Define acceptable ranges for the parameters
  Define a generation function that takes the parameter values as inputs and generates an input signal

## Slide 34: Finite parameterization using control points
Finite Parameterization of :
Control points
Acceptable ranges on parameters (control points)
We can view this as values of are picked for (fixed) time points (determined a priori), and then is generated using constant interpolation

## Slide 35: Finite parameterization using linear interpolation
Finite Parameterization of :
We can view this as values of are picked for (fixed) time points (determined a priori), and then is generated using linear interpolation
Control points
Acceptable ranges on parameters (control points)

## Slide 36: Finite parameterization variable control point times
Finite Parameterization of :
Control points
Acceptable ranges on parameter values
We can view this as values of and time increments in are both picked, and then is generated using constant interpolation
Acceptable ranges on time increments

## Slide 37: Signal Generator
Signal Generation controlled by the testing algorithm
  Parameter space could be sampled all at once
  Parameter space could be sampled in a sequential fashion, e.g. using a method such as Markov Chain Monte Carlo
  Sampling scheme could be application-specific: uniform random, quasi-random (more evenly spread out), truncated normal, grid-based sampling (points from a fixed grid), etc.
Generate Signal
Sample Parameter Space

## Slide 38: Checking output properties
Output properties could be simple static bounds check, dynamic bounds check, or any other function returning yes/no answers (e.g. any Matlab function that maps a signal to a yes/no answer)
More systematic approach is to use properties specified in STL
  Properties could be over just output signals or specify some relation between input and output signals
  Tool Breach provides both Boolean/Quantitative monitoring approaches to check if a given set of signals satisfies an STL property

## Slide 39
Breach tutorial

## Slide 40: Falsification or Automated Test Generation
In most industrial settings, test generation is still quite manual
  Engineer knows the input patterns of interest from technical insights
  Regulatory or other external agencies may provide test input signals
  Companies may build a library of interesting test input signals
Random sampling to generate a test-suite of input signals is one method for automatic input test-generation
Falsification takes automatic test generation to the next level by directing test generation to focus on input signals that are likelier to cause violations of correctness properties

## Slide 41: Quick Introduction to Black-box Optimization
Cost function
Black-box Optimizer
Given:
  Function with unknown symbolic representation
  Ability to query the value of at any given valid ; query will return some value
  Cost function
Objective of black-box optimizer
  Let
  Find such that is small
Let be the best answer found by optimizer in its iteration
Ideally,

## Slide 42: Falsification using Optimization
\
Minimize robustness

\
Compute Robustness

## Slide 43: Step-by-step of how falsification works
Given: a finite parameterization for input signals, a model that can be simulated and an STL property
While the number of allowed iterations is not exhausted do:
  pick values for the signal parameters
  generate an input signal
  run simulation with generated input signal to get output signal
  compute robustness value of given property w.r.t. the input/output signals
  if robustness value is negative, HALT
  pick a new set of values for the signal parameters based on certain heuristics

## Slide 44: Picking new parameter values to explore
Basic method: locally approximate the gradient of the function locally, and chose the direction of steepest descent (greedy heuristic to take you quickly close to a local optimum)
Challenge 1: cost surface may not be convex, thus you could have many local optima
Challenge 2: cost surface may be highly nonlinear and even discontinuous, using just gradient-based methods may not work well

## Slide 45: Exploring parameter space using heuristic search
Heuristics rely on:
  combining gradient-based methods with perturbing the search strategy (e.g. simulated annealing, stochastic local search with random restarts)
  evolutionary strategies: Covariance Matrix Adaptation Evolution Strategy (CMA-ES), genetic algorithms etc.
  probabilistic techniques: Ant Colony Optimization, Cross-Entropy optimization, Bayesian optimization
Can also pick random sampling as a (not very good) strategy!

## Slide 46: Stochastic Tabu-Search and Refinement
Point | Robustness
(1, -2, 1) | 30
(3, 1, -2) | 40
(-2, -3, -2) | 10
(-3, -2, -3) | 5
(1, -3, 1) | 10
Tabu List
time
3
1
-2
-3
3
1
-2
-3
time
Ego point: (1,-2,1)
3
1
-2
-3
time
Neighbor 1: (3,1,-2)
3
1
-2
-3
time
Neighbor 2: (-2,-3,-2)
Key Idea: Make input signal space finite (even further simplification than finite parameterization)
Stochastically estimate least cost neighbor and descend to it
Use Tabu-list to avoid revisiting points
Use random restarts to escape local optima
Refine search space in promising regions

## Slide 47: Specification Templates using PSTL
If we convert all values in an STL formula to parameters, then we get a specification template, or a Parametric STL (PSTL) formula
PSTL = Parametric Signal Temporal Logic
time
Overshoot:
Step:
In a previous slide, were some fixed values, here they represent parameters

## Slide 48: Specification Mining
Specification Mining: Try to find values of parameters of a PSTL formula from a given model
Why?
  Good to know “as-is” properties of the model
  Finds worst-case behaviors of the model
  Can be used to do design-space exploration

## Slide 49: Specification Mining
Parameter Inference:
Find “Tightest” Answers
Settling Time is ??
Overshoot is ??
Bounds on x are ??
Falsification:
trace ⊭ Property?
Settling Time is 5 ms
Overshoot is 5 KPa
Upper Bound on x is 3.6
YES
1.
1.
m.
Counterexamples
Settling Time is 6 ms
Overshoot is 5.5 KPa
Upper Bound on x is 5
1.
n.
YES
NO
Settling Time is 6 ms
Overshoot is 5.5 KPa
Upper Bound on x is 5

## Slide 50: Specification Mining
Parameter Inference:
Find “Tightest” Answers
Settling Time is ??
Overshoot is ??
Bounds on x are ??
Falsification:
trace ⊭ Property?
Settling Time is 5 ms
Overshoot is 5 KPa
Upper Bound on x is 3.6
YES
1.
1.
m.
Counterexamples
Settling Time is 6 ms
Overshoot is 5.5 KPa
Upper Bound on x is 5
1.
n.
YES
NO
Settling Time is 6 ms
Overshoot is 5.5 KPa
Upper Bound on x is 5
Secret Sauce:
Infer parameters for a given PSTL formula from traces
Falsify given STL formula

## Slide 51: Parameter inference for PSTL
Given:
  PSTL formula , [ ]
  Traces
Find:
  Valuation such that:
c= 1000
c = 1.5
time
Problem: Could find very conservative valuations!!
-tight valuation
  and :
    i.e. small perturbation in makes some trace not satisfy formula
Finding -tight valuations hard in general, but efficient for Monotonic PSTL
formula sat for given valuation greater (or lesser) valuations sat
Binary search on parameter space

## Slide 52: Bibliography
G. Fainekos, and G. J. Pappas. Robustness of temporal logic specifications for continuous-time signals. Theoretical Computer Science 2009.
Maler, Oded, and Dejan Nickovic. "Monitoring temporal properties of continuous signals." Formal Techniques, Modelling and Analysis of Timed and Fault-Tolerant Systems. Springer, Berlin, Heidelberg, 2004. 152-166.
Donzé, Alexandre, and Oded Maler. "Robust satisfaction of temporal logic over real-valued signals." International Conference on Formal Modeling and Analysis of Timed Systems. Springer, Berlin, Heidelberg, 2010.
Kapinski, James, et al. ST-Lib: A library for specifying and classifying model behaviors. No. 2016-01-0621. SAE Technical Paper, 2016.

## Slide 53: Bibliography
Several excellent papers on the first development of falsification technology can be found on the web-site of S-TaLiRo : https://sites.google.com/a/asu.edu/s-taliro/references
Breach : https://link.springer.com/chapter/10.1007/978-3-642-14295-6_17
Jyotirmoy Deshmukh, Marko Horvat, Xiaoqing Jin, Rupak Majumdar, and Vinayak S. Prabhu. 2017. Testing Cyber-Physical Systems through Bayesian Optimization. ACM Trans. Embed. Comput. Syst. 16, 5s, Article 170 (September 2017)
Deshmukh, Jyotirmoy, Xiaoqing Jin, James Kapinski, and Oded Maler. Stochastic Local Search for Falsification of Hybrid Systems. In International Symposium on Automated Technology for Verification and Analysis, pp. 500-517.
Jin, Deshmukh et al. Mining Requirements from Closed-loop Control Models (HSCC ’13, IEEE Trans. On Computer Aided Design ’15)