## Slide 1: Autonomous Cyber-Physical Systems: Communication, Coordination
Fall 2024. CS 513.
Instructor: Jyo Deshmukh
USC Viterbi
School of Engineering
Department of Computer Science

## Slide 2: Multi-agent Autonomous Systems
Consensus
Coordination
Co-operation
Case studies

## Slide 3: Co-operative multi-agent systems
Each individual:
  Senses its immediate environment
  Communicates with others
  Processes gathered information
  Takes local actions in response
Swarm of birds

## Slide 4: Multi-agent robotic systems
Networks of vehicles
Drone swarms for biological applications, surveillance
Environment monitoring
Military applications
Warehouse robots
Industrial manufacturing robots

## Slide 5: Coordination tasks
Logic-based: Consensus, Synchronization, Team-Forming
Motion-based: Gathering, Flocking, Forming a pattern
Sensor-based: Search, Estimation, Identification, Tracking, Mapping

## Slide 6: Basic Model for Consensus
Nodes:
Edges:
Neighbors of node
: value of node
: Algebraic graph/Network
  value
  topology or information flow
Olfati-Saber, Reza, and Richard M. Murray. "Consensus problems in networks of agents with switching topology and time-delays." IEEE Transactions on automatic control 49, no. 9 (2004): 1520-1533.

## Slide 7: Some neat things from algebraic graph theory
Laplacian matrix of a graph defined as:
If graph is weighted replace 1 with the weight of that edge
Multiplicity of the zero eigenvalue of the matrix is the number of components of the graph (nodes that can be reached from each other)
Speed of convergence of algorithms for flocking, rendezvous, consensus depend on the second smallest eigenvalue of the Laplacian matrix

## Slide 8: Consensus
Nodes and agree iff
Nodes of a network have reached consensus iff
Common value of all nodes is called “group decision value”
Dynamic graph : Dynamical system in which evolves according to dynamics function where

## Slide 9: -consensus problem
L be a function of
is an initial state of the system, then
-consensus problem is to calculate by applying inputs that only depend on and the neighbors of
is called a protocol with topology if the cluster satisfies the property that (i.e., if the feedback only uses a node and some subset of its neighbors)
above is called a distributed protocol: if

## Slide 10: Solving the -consensus problem
Protocol solves the -consensus problem iff there exists an asymptotically stable equilibrium of satisfying for all
Some special cases:
  Max-consensus:
  Min-consensus:
  Average-consensus:

## Slide 11: Example of a consensus protocol
Imagine a network of agents with integrator dynamics
The protocol for fixed topology or switching topology (set of neighbors can change):
With time delay for each

## Slide 12: Challenge problems in consensus
Different kinds of topologies
Different assumptions on structures of the graphs
Types of problems to solve (min/max/average)
How do you prove that the consensus algorithm actually converges?
  Requires ideas similar to Lyapunov functions
  Called disagreement functions that show that disagreement decreases over time
Olfati-Saber, Reza, and Richard M. Murray. "Consensus problems in networks of agents with switching topology and time-delays." IEEE Transactions on automatic control 49, no. 9 (2004): 1520-1533.

## Slide 13
Vehicle to Vehicle (V2V) and Vehicle to Everything(V2X)

## Slide 14: V2V algorithms
Forward crash avoidance
Cooperative Adaptive Cruise Control
Cooperative Collision Avoidance
Cooperative Merging
https://www.its.dot.gov/research_archives/safety/v2v_comm_safety.htm

## Slide 15: Cooperative Adaptive Cruise Control (CACC)
Used for platoons of vehicles (e.g., trucks)
Several goals:
  Improve safety
  Improve traffic flow dynamics by damping disturbances (new cars, braking, bumps in the road)
  Increasing highway capacity by shorter following gaps
  Saving energy and pollution through aerodynamic drafting
  Improving driver comfort and convenience

## Slide 16: CACC uses different gap regulation strategies
Constant clearance or constant distance gap (CDG)
  Separation does not change with vehicle velocity
  Gives experience of mechanical linkage between vehicles
  Requires more formal platoon architecture and tight communication between platoon leader and followers
  Communication interruption can cause safety hazards
  Need larger gaps to ensure safety of platoon
  (Emergency brake by leader can cause domino effect)

## Slide 17: CACC uses different gap regulation strategies
Constant Time Gap
  Resembles how normal human drivers drive
  Distance between vehicles is proportional to their speed + a small fixed offset distance
  E.g., doubling of speed causes doubling of gap between vehicles
  Time gap criterion described in terms of time between rear bumper of leading vehicle and front bumper of trailing vehicle pass a fixed point on the roadway
  Often described as headway or time headway
  Vehicles in CTG CACC are often called a “string of vehicles” rather than platoon

## Slide 18: CACC string splits and faults
CACC needs to handle trucks leaving string
Ideally, departing truck signals intent and remaining string close gaps to maintain platoon structure
In some cases, may require string to be split while the truck in the middle departs
Protocols have NUMEROUS fault conditions, errors and abnormal operating conditions (obstacle in the road, accidents, etc.)
Safety: model each truck as an asynchronous process and reason about composition of asynchronous processes!
Specifications: Safety and String stability

## Slide 19: Autonomous Intersection Management
AIM protocol and its variants proposed based on V2I communication
Main idea :
  Each car equipped with a driver agent
  Each intersection equipped with an intersection manager
  Driver agents call ahead to reserve space-time in an intersection
  Intersection manager decides to grant or reject reservation requests according to an intersection control policy

## Slide 20: AIM protocol4
Approach vehicle announces arrival to manager
Vehicle indicates its size, predicted arrival time, velocity, acceleration, arrival and departure lanes
Intersection manager simulates vehicle’s path through the intersection, checking for conflicts with paths of previously processed vehicles
If there are no conflicts, issues a reservation
It is the vehicle’s responsibility to arrive at and travel through the reserved space-time block within some range of error tolerance
In case of conflict, intersection manager suggests an alternate later reservation
Car enters intersection only if reservation successful
Upon leaving intersection, car conveys successful passage to the manager

## Slide 21: Intersection control policies
Divide intersection into grid of reservation tiles

## Slide 22: Collaborative merge
Purpose: allow vehicles merging onto a freeway from a ramp to do so in safe fashion
Can be formulated as a specific case in AIM
Specialized approaches based on highway ramp metering have existed for some time (do not utilize V2V, do not guarantee safety)

## Slide 23: References
[1] Shladover, Steven E., et al. "Cooperative adaptive cruise control: Definitions and operating concepts." Transportation Research Record: Journal of the Transportation Research Board 2489 (2015): 145-152.
[2] ibid., https://escholarship.org/uc/item/7jf9n5wm
[3] Liang, Chi-Ying, and Huei Peng. "String stability analysis of adaptive cruise controlled vehicles." JSME International Journal Series C Mechanical Systems, Machine Elements and Manufacturing 43.3 (2000): 671-677.
[4] Stone, Peter, Shun Zhang, and Tsz-Chiu Au. "Autonomous intersection management for semi-autonomous vehicles." Routledge Handbook of Transportation. Routledge, 2015. 116-132.
[5] Qian, Xiangjun, et al. "Autonomous Intersection Management systems: criteria, implementation and evaluation." IET Intelligent Transport Systems 11.3 (2017): 182-189.
[6] de Campos, Gabriel Rodrigues, et al. "Traffic coordination at road intersections: Autonomous decision-making algorithms using model-based heuristics." IEEE Intelligent Transportation Systems Magazine 9.1 (2017): 8-21.
[7] Rios-Torres, Jackeline, and Andreas A. Malikopoulos. "A survey on the coordination of connected and automated vehicles at intersections and merging at highway on-ramps." IEEE Transactions on Intelligent Transportation Systems 18.5 (2017): 1066-1077.