## Slide 1: Autonomous Cyber-Physical Systems: Decision-making and planning
Spring 2018. CS 599.
Instructor: Jyo Deshmukh

## Slide 2: Overview
Decision-making hierarchy
Motion planning

## Slide 3: Decision-making hierarchy
Route Planning
Behavioral Planning
Lane following
Lane changing
Adaptive cruising
Intersection negotiation
Collision avoidance
Trajectory planning/Motion planning
Low-level Feedback control
Road topology, network
Perception layer outputs
Estimated pose and free space
Vehicle state estimates
User-specified
destination
Sequence of way-points
Motion specification
Reference path
Steering and throttle commands

## Slide 4: Route planning
Represent road network/topology as a directed graph
  Nodes represent way-points
  Edges represent a cost of traveling between nodes
Cost can represent time, distance, fuel economy, a weighted combination of some of these, etc.
Simplest solutions based on Dijkstra’s shortest-path or A* search algorithms
  In practice, these do not scale well
  Lots of different algorithms proposed in the literature5

## Slide 5: Behavior planning
Navigate selected route while interacting with traffic participants (pedestrians, bicycles, other cars).
Behavioral layer responsible for selecting appropriate driving action based on perceived mode (as dictated by other participants, road conditions, etc.)
FSM-based approach:
  Model driving contexts and behaviors as finite sets, and use finite state machines to represent possible behaviors.
  Planning then becomes a problem of choosing appropriate transitions that ensure a desired behavior.
  Can view this is a 2-player game between the car’s controller (player 1) and the environment (player 2). Game-theoretic approaches for FSMs can identify winning strategies for the controller.

## Slide 6: Behavioral planning under uncertainty
FSM-based view may not adequately address uncertainty
Uncertainty exists in the intention of traffic participants
Intention prediction of cars, bicycles, pedestrians has been researched
  Techniques based on Gaussian mixture models
  Switching linear dynamical and stochastic systems
  Gaussian Process Regression
A big new push is probabilistic planning formalisms using Markov Decision Processes such as Partially Observable Markov Decision Processes
We will learn about POMDPs in the lecture on reinforcement learning

## Slide 7: Motion planning
Behavior plan decides a high-level set of maneuvers (e.g. cruise-in-lane, turn right, turn left, etc.)
This plan needs to be translated into a reference path or a reference trajectory to be followed by the vehicle.
Motion planning computes a feasible reference plan that respects feasibility (according to vehicle dynamics), obstacle avoidance, while optimizing certain costs (e.g. maximizing comfort, minimizing battery usage, etc.)
Popular approaches
  Variational methods from nonlinear optimal control
  Graph-search approaches using discretization of the state-space
  Incremental tree-based methods

## Slide 8: Path planning vs. Trajectory planning
Path planning:
  Simply provides a parametric function
    is the configuration space or state-space of the vehicle
    gives the initial configuration, and gives the final configuration, and for all intermediate , gives the intermediate configurations
  May not include a velocity profile or those for other states, but delegates this to lower-level control
Trajectory planning: Is aware of vehicle dynamics and can account for dynamic obstacles

## Slide 9: Trajectory planning
Defines a parametric function , where
  is the planning horizon, and is the set of configurations
  precisely describes how the vehicle’s behavior evolves in configuration space at each time
Trajectory planning is a more nuanced version of path planning

## Slide 10: Trajectory planning setup
: set of all continuous functions from to
Let , then:
  (where is a set of initial configurations/states)
  (where is a set of goal states)
Set of all allowed states at time denoted as
encodes holonomic constraints
  A constraint is holonomic if you can express it as , where the ’s are coordinates, i.e. constraint depends only on spatial configuration
  Holonomic constraints can encode path constraints, and dynamic and static obstacles

## Slide 11: Trajectory planning setup continued
is a differential constraint specifying constraints on smoothness of the path, velocity, acceleration, jerk constraints etc.
is a cost functional mapping any trajectory to some cost in
Optimal trajectory can be stated as follows:
Trajectory planning in dynamic environments and static path planning are both PSPACE-hard problems
  At least as complex as checking SAT of a quantified Boolean formula (QBF)
  Example QBF formula:

## Slide 12: Variational methods
Rely on results from nonlinear continuous optimization
We transform the trajectory optimization to the following standard form:
Standard trick to go from constrained to unconstrained optimization is to introduce penalty functions
  Penalty method:
  Barrier function method:
  ()

## Slide 13: Variational methods
Common to use logarithmic barrier functions with Newton-like iterative methods
One problem: Trajectory space is infinite-dimensional. Solution:
  Direct methods:
    Restrict to finite-dimensional subspace, , where are some basis functions (e.g. piecewise linear interpolation uses PWL basis functions)
    Requires numerical integration approximations for the trajectory combined with optimizers like conjugate gradient descent
  Indirect methods: use Pontryagin’s minimum principle that gives optimality conditions for trajectory optimization problem
    Requires solving boundary-value problems of ODEs, that can be approximated numerically

## Slide 14: Graph-search-methods
Variational methods may get stuck in local optima, graph-search methods try to do global search
Configuration space is represented as a graph , where is a set of selected discrete configurations, and is a set of edges, where each edge is labeled by the path segment that the edge represents.
  If , then and
Feasible path can be found by concatenating feasible edges
Does require discretization of the configuration/state space!
  Hand-crafted lane graphs2
  Geometric representations
  Sampling-based discretization

## Slide 15: Some geometric representations3
Voronoi diagrams
Occupancy Grid Map
Cost Map
State Lattice
Driving Corridors
Several nice results or path planning using geometric representations, but usually computationally expensive!

## Slide 16: Sampling-based methods
Typical constraints (differential, holonomic) are usually very difficult to obtain at real-time through sensors
Sampling-based methods explore reachability of free configuration space by trying to apply controls (steering) and checking for collisions
Main purpose of these methods is to construct a roadmap, and use it for planning
Steering functions:
  Random : returns a path obtained by applying a random steering command
  Heuristic: tries to guide vehicle from point to point
  Exact: computes exact path that takes vehicle from to
  Optimal: Returns an optimal exact path

## Slide 17: Probabilistic Roadmap (PRM) Construction
for
  for
    if
    endif
  end
End
return
Sample:
Return points on a grid
Random samples
Neighbors:
-nearest neighbors using appropriate distance function
Points within a ball of radius around
Trajectory plan: Use Dijkstra’s shortest-path algorithm on the resulting roadmap

## Slide 18: Heuristic search A*
Dijkstra’s shortest path algorithm: uses best first search to build a tree representing shortest paths from a given source to all other vertices in the graph
We typically need a path to only a single vertex (in the goal set), in this case a heuristic can be used to guide the search process
Most prominent heuristic search algorithm is A*
Shown to be optimally efficient if heuristic function is admissible (never overestimates the cost)

## Slide 19: How A* works
It constructs a tree of paths starting from the initial node, expanding paths one step at a time, till one of the path reaches the goal
In each iteration, A* determines which of its partial paths to expand based on an estimate of the cost. It selects the path that minimizes , where, . Here, = cost of path from start node to , and is an estimate of the cheapest cost to go from to the goal
Heuristic function is problem-specific. For the heuristic to be admissible, it should never over-estimate actual cost to get to the goal
Dijkstra’s shortest path is a special case of A*, where

## Slide 20: Weighted A*
Admissibility criterion forces A* to inspect all equally promising paths to find the optimal
Approximate shortest paths can be found by relaxing the admissibility criterion (these guarantee that the path found is no worse than times the optimal path).
Weighted A* variants involve defining a heuristic that is a function of . E.g. static weighted A* uses
A*, Dijkstra’s shortest-path are all special cases of dynamic programming

## Slide 21: Many variants of A*
Real-time re-planning: D*, Focused D*, D* Lite: recompute shortest path anytime the underlying graph changes, making use of results from previous search
Anytime search algorithms: Quickly find a (possibly sub-optimal) path first, and continue to improve the solution if there is more computational time
  Anytime A*: weighted heuristic that continues searching using cost of previously identified path as upper bound and admissible heuristic as lower bound
  Other variants such as Anytime Repairing A*, Anytime Dynamic A* etc.

## Slide 22: Rapidly Exploring Random Trees (RRTs)
RRT one of a family of algorithms based on incremental sampling, i.e. when you do not want to a priori build the entire roadmap
Also known as single-query PRMs
Very fast algorithm, allows on-the-fly construction of paths
while
randomly select a goal-point in
find the node in the tree closest to (say this is )
find control input that takes towards while being collision-free
let be the point reached by applying to
add edge
if (

## Slide 23: RRT in action
Target
Sample goal
Select closest neighbor
Find collision-free control
Obstacle
Target
Obstacle
Target
Obstacle

## Slide 24: Many variants of PRMs and RRTs
There are many variants that exist: RRG, RRT*, PRM*, etc.
Some of them add optimality criteria such as costs on edges
Algorithms differ in the underlying structure maintained: PRM (forest), RRT (tree), RRG (graphs with possible cycles), RRT* (acyclic graphs) etc.
There are two key considerations:
  Probabilistic completeness: given infinite time, will the procedure identify a path to the goal set
  Asymptotic optimality: does the optimal path found by the algorithm converge to the actual optimum in the limit

## Slide 25: Combining RRTs with STL
Define path planning objectives in STL
Define robustness of STL on partial trajectories
Use RRT to explore the search space
When selecting nearest neighbors of the goal point, select ones with high robustness
Allows path-planning with STL objectives!
Combining RRTs with LTL objectives has been extensively studied in the literature

## Slide 26: Bibliography
Pendleton, Scott Drew, Hans Andersen, Xinxin Du, Xiaotong Shen, Malika Meghjani, You Hong Eng, Daniela Rus, and Marcelo H. Ang. "Perception, planning, control, and coordination for autonomous vehicles." Machines 5, no. 1 (2017): 6.
Most material in this lecture is from this paper: Paden, Brian, et al. "A survey of motion planning and control techniques for self-driving urban vehicles." IEEE Transactions on Intelligent Vehicles 1.1 (2016): 33-55. https://arxiv.org/pdf/1604.07446.pdf
Katrakazas, C., Quddus, M., Chen, W. H., & Deka, L. (2015). Real-time motion planning methods for autonomous on-road driving: State-of-the-art and future research directions. Transportation Research Part C: Emerging Technologies, 60, 416-442.
https://en.wikipedia.org/wiki/A*_search_algorithm
Bast, D. Delling, A. Goldberg, M. Müller-Hannemann, T. Pajor, P. Sanders, D. Wagner, and R. F. Werneck, “Route planning in transportation networks”, https://arxiv.org/pdf/1504.05140.pdf

## Slide 27: POMDPs
6-tuple :
  : set of states
  : set of actions
  : set of observations
  : transition function
    gives the probability of state transitioning to under action
  observation function
    gives the probability of observing if action is taken in state
  reward function
    gives a reward for taking action in state