## Slide 1: Autonomous Cyber-Physical Systems: Dynamical System Models
Fall 2022. CS 513.
Instructor: Jyo Deshmukh

## Slide 2
Dynamical System Models

## Slide 3: Dynamical Systems
Most natural model for describing most physical systems
Continuous/discrete systems that continuously evolve over time
Convenient to model such systems with differential equations
Typically consist of physical quantities modeled as state variables
  Pressure, Temperature, Velocity, Acceleration, Current, Voltage, etc.
Could include algebraic relations between state variables
Execution semantics similar to synchronous models, but with continuous-time semantics instead of discrete-time

## Slide 4: Continuous-time Component (Algebraic)
error = (x – xref)
real x
real xref
real error
Input variables: x and xref of type real, Output variable: error of type real
No state variables
Signals: Assignments of values to variables as a function of time
At each time t, error(t) = x(t) – xref(t)
Input/Output relation expressed algebraically instead of as an assignment

## Slide 5: Model of a simple car
Position
Velocity
Force
Friction
Newton’s law of motion:

## Slide 6: Continuous-time component (differential)
real
real
Rate of change of each state variable and output variables defined using expressions over inputs and states
Expressions, not assignments!

## Slide 7: Executions of Car
Let represent a set representing time instants, i.e.
Input Signal: Function from
  Input signal is assumed to be continuous or piecewise-continuous
Given an initial state and an input signal , the execution of the system is defined by state-trajectories and (from to ) that satisfy the initial-value problem:
  ;

## Slide 8: Sample Execution of Car
Suppose . Then, we need to solve:
  ;
Solution to above differential equation (solve for first, then ):
;
Note, as , , and

## Slide 9: Sample Execution of Car with constant force
Suppose . Then, we need to solve:
  ;
Solution to above differential equation (solve for first, then ):
Compute solution using Simulink/Matlab/Breach

## Slide 10: Plots
Phase Plot
Input/Output Signals

## Slide 11: Continuous-Time Component Definition
Set of real-valued input variables
Set or real-valued output variables
Set of real-valued (continuous) state variables
Initialization specifying a set of initial values for states
Dynamics: for each state variable, , a real valued expression over and
Output Function: for each output variable, , a real valued expression over and .

## Slide 12: Execution Definition
Convention:
Given an input signal , an execution consists of a differentiable state signal , and an output signal such that:
  For each output variable and time t,
  For each state variable ,

## Slide 13: Existence and Uniqueness of Solutions
Given an input signal , when are we guaranteed that the system has at least one execution? Is there nondeterminism in continuous-time components?
Input signal should be piecewise-continuous, and additional conditions need to be imposed on the RHS of dynamics and output functions
Related to solutions for the initial value problem in the classical theory of ODEs

## Slide 14: Existence
There exists at least one solution if the function is continuous
Definition of continuity uses notion of distance between points
  Euclidean distance:
is uniformly continuous if for all , there exists a , such that for all , if , then .
Example when solution does not globally exist:

## Slide 15: Uniqueness
Solution to initial value problem is unique if is Lipschitz continuous
Lipschitz-continuity is a stronger version of continuity: upper bounds how fast a function can change
Function is Lipschitz-continuous if there exists a constant (called the Lipschitz constant) such that:
Examples:
  Linear functions (e.g. ) are Lipschitz continuous
  Functions: , are not Lipschitz continuous over
Can restrict and to some bounded and closed set such that is piecewise-continuous and Lipschitz to get unique solutions over such compact domains

## Slide 16: What do Matlab/Simulink do?
Allow modeling arbitrarily complex functions: even functions with unbounded discontinuities
May not be even possible to check for Lipschitz conditions for what’s implemented in a Matlab function/Simulink model
Rely on numerical integration schemes/solvers to obtain solutions
  ode45, ode23, ode15, etc.
We assume that any continuous component model we will use can be numerically simulated by Matlab/Simulink

## Slide 17: Linear Systems
Equation of simple car dynamics can be written compactly as:
Letting , we can re-write above equation in the form:
, where , and

## Slide 18: Linear Components
Linear components model linear systems
  is of the form + or compactly,
  is of the form + or compactly,
Linear algebra was invented to reason about linear systems!
Linear systems have many nice properties:
  Many analysis methods in the frequency domain (using Fourier/Laplace transform methods)
  Superposition principle (net response to two or more stimuli is the sum of responses to each stimulus)

## Slide 19: Solutions to Linear Systems
Autonomous linear system has no inputs:
Solution of autonomous linear system can be fully characterized:
  is a matrix exponential =
  is usually approximated to the first terms
Computing is easy if is a diagonal matrix (non-zero elements are only on the diagonal)
In practice, numerical integration methods outperform matrix exponential
For a linear system with exogenous inputs?

## Slide 20: Stability of Systems
Property capturing the ability of a system to return to a quiescent state after perturbation
  Stable systems recover after disturbances, unstable systems may not
  Almost always a desirable property for a system design
Fundamental problem in control: design controllers to stabilize a system
Problem: Inverted Pendulum on a moving cart is inherently unstable, aim: keep it upright
Solution Strategy: Move cart in direction in the same direction as the pendulum’s falling direction
Design problem: Design a controller to stabilize the system by computing velocity and direction for cart travel

## Slide 21: Lyapunov stability
System
Equilibrium point when is zero (say
Equilibrium point is Lyapunov-stable if:
  For every ,
    There exists a , such that
      if then,
      for every we have
-ball
-ball

## Slide 22: Asymptotic + Exponential Stability
System
Equilibrium point is asymptotically-stable if:
  is Lyapunov-stable +
  There exists s.t. if , then
Equilibrium point is exponentially-stable if:
  is asymptotically stable +
  There exist s.t. if , then for all

## Slide 23: What do these definitions all mean?
Lyapunov stable: solutions starting close from equilibrium point must remain close (within forever
Asymptotically stable: solutions not only remain close, but also converge to the equilibrium
Exponentially stable: solutions not only converge to the equilibrium, but in fact converge at least as fast as a known exponential rate
  All stable linear systems are exponentially stable
  This need not be true for nonlinear systems!

## Slide 24: Analyzing stability for linear systems
Eigenvalues of a matrix :
  Value satisfying the equation . is called the eigenvector
  Equivalent to saying: values satisfying , where is the identity matrix
Interesting result for linear systems: System is asymptotically stable if and only if every eigenvalue of has a negative real part
Lyapunov stable if and only if every eigenvalue has non-positive real part
Nonlinear systems: no simple analysis technique exists
  Next time we will look at Lyapunov’s methods, which allow reasoning about stability of nonlinear systems

## Slide 25: Simulink and Breach Brief Demo
Plot of Signals vs. Time

## Slide 26: Simulink and Breach Demo
Plot in phase-space or state-space.
Shows trajectory of states starting from ,